## Slide 1: Proposal on handling LTE CRS interference in scenarios with overlapping spectrum for LTE and NR
China Telecom, Vodafone, ZTE, Orange, Telecom Italia, CMCC, Telefonica, Huawei, HiSilicon, Intel, CATT
3GPP TSG RAN Meeting #91e
Electronic Meeting, March 16 - 26, 2021
Agenda: 9.7.17
RP-210521

## Slide 2: Introduction
The proposal on handling LTE CRS interference in scenarios with overlapping spectrum for LTE and NR was discussed in previous RAN plenary meetings, with no conclusion.
The following contributions shared the performance gain for NR PDSCH by LTE CRS-IM:
  RP-202659, Intel Corporation, Scope update for Rel-17 NR demodulation performance WI: CRS-IM for LTE/NR DSS, RAN #90e.
  RP-202676, ZTE, Sanechips, WI scope of further enhancement on NR demodulation performance, RAN #90e.
  It is also noted that CRS-IM has been introduced in LTE for various scenarios.
  This contribution discusses operators’ scenarios which requiring NR UE to handle LTE CRS, and proposes to add LTE CRS interference handling receiver to Rel-17 RAN4 demod WI scope.

## Slide 3: Scenarios with overlapping spectrum for LTE and NR - 1: LTE and NR DSS
As well known, LTE and NR dynamic spectrum sharing (DSS) is an efficient way to deploy NR in the same or overlapping spectrum with the existing LTE deployment.
In DSS scenario with LTE non-MBSFN sub-frame:
  For serving cell LTE CRS, rate matching is one option of handling the always-on LTE CRS for NR UE, at the cost of unusable REs occupied by LTE CRS.
  The LTE CRS from neighboring cell will produce obvious interference to NR PDSCH, and the impact of the interference is related to the UE location and the traffic level of the interfering cell.

## Slide 4: Scenarios with overlapping spectrum for LTE and NR - 2: LTE and NR deployed in neighboring BS/areas
Another scenario with overlapping spectrum for LTE and NR is that LTE and NR are deployed in neighboring BSs/areas.
In this scenario:
  The LTE CRS from neighboring cell will produce obvious interference to NR PDSCH in the overlapping spectrum.

## Slide 5: Proposal
Add the following objective in Rel-17 NR demod performance enhancement WI:
  Define NR PDSCH demodulation requirements for LTE CRS-IM in scenarios with overlapping spectrum for LTE and NR
    Candidate reference receiver is neighboring cell CRS-IM
    Handling of the neighboring cell LTE CRS is included. The need of handling the serving cell LTE CRS in DSS scenario is to be further discussed and considered as lower priority.
      The potential impact to LTE operation needs to be considered when deciding whether or not to handle the serving cell LTE CRS in DSS scenario during the WI
    Further discuss whether or not to assume assistant information from network

## Slide 6
Thanks!