## Slide 1: Lab testing results on performance impact by LTE CRS interference to NR UE in DSS scenarios
China Telecom
3GPP TSG RAN Meeting #91e
Electronic Meeting, March 16 - 26, 2021
Agenda: 9.7.17
RP-210522

## Slide 2: Lab testing on performance impact by neighboring cell LTE CRS - Test scenarios
General parameters for LTE-NR DSS:
  20MHz LTE and 20MHz NR DSS, FDD, 15kHz SCS
  DL 2x2 with max 2-layer PDSCH for LTE; DL 4x4 with max 4-layer PDSCH for NR
  Serving cell LTE CRS rate matching is employed, and different REs occupied for LTE CRS in serving and interfering cells.
  2 OFDM symbols for LTE control channel, 1 OFDM symbol for NR control channel
Two comparison schemes are also tested:
  One is LTE only in the 20MHz carrier; the other is NR only in the 20MHz carrier

## Slide 3: Lab testing on performance impact by neighboring cell LTE CRS - Test results
DL throughput (Mbps) | LTE only | NR only | NR in DSS
Near point | 192.0 | 394.0 | 290.0
Middle point | 164.0 | 340.0 | 136.0
Far point | 131.0 | 310.0 | 100.0
Compared to NR only scenario, the performance degradation for NR DL in DSS scenario are mainly due to:
  Unusable REs occupied by LTE PDCCH and serving cell LTE CRS
  Interference from neighboring cell LTE CRS
Significant performance impact due to neighboring cell LTE CRS interference is observed, especially for UEs in middle point and far point!
  NR performance is even much poorer than LTE, for UEs in middle point and far point.
Case 1: No PDSCH scheduled in neighboring cell
Case 2: 50% PRB scheduled for neighboring cell PDSCH
DL throughput (Mbps) | LTE only | NR only | NR in DSS
Near point | 191.0 | 314.0 | 285.0
Middle point | 140.0 | 255.0 | 127.0
Far point | 87.0 | 130.0 | 37.0
  Near point: serving cell -80, interference -105
  Middle point: serving cell -90, interference -105
  Far point: serving cell -100, interference -95
  Unit: dBm/15kHz

## Slide 4
Thanks!