## Slide 1: Guidelines for FR1 CA/DC band combinations not subject to block approval
Apple Inc., Skyworks Solutions Inc.
3GPP TSG-RAN #91-e
Electronic Meeting, March 16th – 26th
RP-210639

## Slide 2: Background
UE band combination basket work items block approval process has been implemented since LTE and continued in NR.
The framework has successfully facilitated the TR TP review process and improved RAN4 work efficiency on developing the UE RF requirements for majority of band combinations.
Nonetheless, there are certain band combinations which may require additional technical justifications or requirements not covered by the standard basket TR TP format and may not be suitable for block approval process.
This contribution is intended to provide guidelines for FR1 band combinations which shall not be subject to block approval process.

## Slide 3: Guidelines for FR1 Generic Band Combinations
Inter-band CA/DC with adjacent or overlapping frequency ranges
  Need a discussion paper to address the front-end implementation feasibility and usage scenarios.
Inter-band CA/DC with two or more bands below 1 GHz
  Need a discussion paper to address the front-end implementation feasibility and usage scenarios. The aspect of antenna configuration including diversity path and its implication to form factor shall be considered.
  UL CA needs further discussions if the corresponding DC combination only supports SUO.
Intra-band contiguous EN-DC with new bandwidth class, such as classes AC and CB
  Need a new feature defined.
Intra-band CA with more than 2 non-contiguous DL CCs with > 200 MHz frequency span
  Need a discussion paper to address the implementation feasibility including DL MIMO support.

## Slide 4: Guidelines for FR1 UL Specific Band Combinations
Intra-band UL CA with 2 CCs where A-MPR requirements have not been specified (in basket WID not for block approval)
Intra-band contiguous UL CA with 3 CCs (feature not yet defined)
UL CA with three or more non-contiguous CCs (feature not yet defined) including
  Inter-band UL CA with UL in three or more bands
  Intra-band non-contiguous UL CA with three or more discrete UL CCs
  Inter-band UL CA consisting of intra-band non-contiguous UL CA

## Slide 5: Additional Aspects
Band combinations which can be directly introduced in CR
  Adding DL intra-band CA to an existing inter-band combination (but not for intra-band UL CA) where DL intra-band CA has been specified.
  Adding > 3 FR1 band combinations if the corresponding fallbacks are complete.
  Adding FR2 band or existing FR2 CA to an existing FR1 combination.
  No TP for TR is required, BC request sheet is sufficient.
Regional spectrum restriction is allowed with a clarification note, but not operator specific spectrum allocation.
UL configuration allowing SUO or mandating SUO shall be clearly stated in TP.
TDD-TDD supporting simultaneous Rx/Tx or not shall be clearly stated in TP.
Inter-band UL CA including intra-band contiguous UL CA, such as UL CA_n3-n41C
  Triple beat issue needs to be addressed.