## Slide 1: Clarifications on intra-band contiguous and non-contiguous EN-DC combinations
Apple Inc.
3GPP TSG-RAN #91-e
Electronic Meeting, March 16th – 26th
RP-210640

## Slide 2: Background
Intra-band contiguous and non-contiguous EN-DC can be clearly differentiated when there is only one LTE CC and one NR CC in the combination, such as DC_(n)48AA (contiguous) and DC_48A_n48A (non-contiguous).
However, when there are more than one CCs in LTE or/and NR cell groups, for certain combinations, RAN4’s definition of contiguous or non-contiguous in conjunction with RAN2 UE capability signaling design became ambiguous, such as DC_(n)48CA for DL with DC_48A_n48A as UL which is currently defined as contiguous EN-DC in 38.101-3.
  RAN2 signaling parameter intraBandENDC-support is only defined for the combination, but not for DL and UL separately.
  RAN4’s contiguous or non-contiguous definition is also for the combination, but not for DL and UL separately.

## Slide 3: Background
In RAN4 #98-e meeting, a WF was approved [1] which is intended to resolve the issue as described in previous slide.
However, both options considered in the WF did not seem to catch the essence of the EN-DC definition where the DL and UL configuration should be interdependent.
For example, in Option 1, DL DC_48A-(n)48AA would be considered as an intra-band contiguous EN-DC combination where UL DC_48A_n48A could be falsely allowed by the proposed RAN2 signaling change for R16.
In this contribution, we propose to resolve the aforementioned issue by revising the contiguous and non-contiguous EN-DC combination categorization in RAN4 specification TS 38-101-3 without the necessity of RAN2 signaling change.

## Slide 4: Proposals for intra-band EN-DC definition
Proposal 1: Contiguous or non-contiguous is determined by the configuration between the primary cells for each cell group.
  For example, DC_(n)48CA with UL DC_48A_n48A should be defined as intra-band non-contiguous EN-DC combination.
    This definition only allows DL fallback to DC_48A_n48A.
  For another example, DC_48A-(n)48AA with UL DC_(n)48AA should be defined as intra-band contiguous EN-DC combination.
    This definition only allows DL fallback to DC_(n)48AA.
Proposal 2: Capability wise, the existing RAN2 signaling design is sufficient to indicate UE’s support for different configurations. There is no need to introduce new signaling to differentiate intra-band DL and UL EN-DC configurations separately.
  For example, UE can signal LTE DL CA BW class C and UL CA BW class A, NR DL CA BW class A and UL CA BW class A, and intraBandENDC-support as “both” in order to support DC_(n)48CA with UL DC_(n)48AA and UL DC_48A_n48A.
  intraBandENDC-support with “non-contiguous” only (meaning supporting non-contiguous but not contiguous) does not look to be very practical from UE implementation perspective.