## Slide 1: Operators’ views on Reduced Capability NR devices
BT, Deutsche Telekom, Orange, Telecom Italia, Telefonica, Telia Company
3GPP TSG RAN Meeting #91e
Electronic Meeting, March 16 - 26, 2021
Agenda: 9.7.27
RP-210668

## Slide 2: Context
A new WID on “support of reduced capability NR devices” (RP-202933) was approved at the last 3GPP RAN plenary #90e.
Two topics remained open:
  Maximum bandwidth of an FR1 RedCap UE during and after initial access of 20 MHz is supported. The possibility of, and any associated conditions for, optional support of a wider bandwidth up to 40MHz after initial access for this case will be further discussed at RAN#91e.
  For frequency bands where a legacy NR UE (other than 2-Rx vehicular UE) is required to be equipped with a minimum of 4 Rx antenna ports, the minimum number of Rx branches supported by specification for a RedCap UE will be decided at RAN#91e; hence no specific work for these frequency bands will be done before RAN#91e.

## Slide 3: Operator Contributions
Orange submitted a RAN1 contribution “On the effect of reducing the number of UE Rx antennas on DL capacity” (R1-2004270) at 3GPP RAN WG1 #101, illustrating the impact of the introduction of reduced capability UEs on the average throughput of eMBB UEs.
  It was concluded that the introduction of a large population of reduced capability UEs with single Rx antenna degrades significantly the downlink capacity of the network particularly in loaded scenarios
Telecom Italia submitted RP-210289 “On RedCap UE performance” at RAN#91e, presenting the results of a measurement campaign in TIM's live commercial network.
  The document shows that two Rx antenna ports allow the use of higher modulation schemes even in poor SINR conditions, while UEs with a single antenna port highly degrade the spectral efficiency

## Slide 4: Operator observations
Observation #1:
  For frequency bands where a legacy NR UE (other than 2-Rx vehicular UE) is required to be equipped with a minimum of 4 Rx antenna ports, reduction of the minimum number of antenna ports to 1 Rx would significantly degrade end user performance and the spectral efficiency of the network
Observation #2:
  The support of “Maximum bandwidth of an FR1 RedCap UE during and after initial access of 20 MHz” is seen by operators as sufficient to address the use cases targeted in the WI, i.e. Industrial wireless sensors, Video surveillance and Wearables.
  In specific cases where high demanding devices would benefit from a higher bandwidth (e.g. high end video surveillance), operators would recommend not to rely on RedCap UE capabilities and support instead the mandatory requirements set in Rel15/16.

## Slide 5: Proposals
Proposal #1
  Maximum bandwidth of an FR1 RedCap UE during and after initial access of 20 MHz is supported.
  No wider bandwidth should be included in the WID.
Proposal #2
  For frequency bands where a legacy NR UE (other than 2-Rx vehicular UE) is required to be equipped with a minimum of 4 Rx antenna ports, the minimum number of Rx branches supported by specification for a should be 2 Rx.

## Slide 6
Thanks!