## Slide 1: Capability for per FR groups
Qualcomm Inc.
3GPP TSG RAN Meeting #90-e
e-meeting, June 14th - June 18th 2021
RP-211310
Document for: Discussion

## Slide 2: Issue of Rel-15 “per-FR gap” capability (1)
UEs capable of “per-FR gap” only need gaps in one FR when doing measurements
  The other FR can still be used for data transmissions
The capability is defined “per UE” which implies that the UE has to support it with all the CA/DC combinations it supports
If UE cannot support the capability even for one combinations out of all combinations it can support, it has to declare no support
The capability is unnecessarily overloaded, i.e. many different requirements not immediately related to measurement gap are tied to “per-FR gap” capability.
Conclusion
  The current Rel-15 “per-UE” based “per-FR gap” capability makes the feature difficult to support for FR1+FR2 capable UE it because many different requirements associated to the feature shall be fulfilled even for the highest order of CA combination that can be supported by the UE.

## Slide 3: Issue of Rel-15 “per-FR gap” capability (2)
Measurement capabilities depend on both RF implementation (e.g. number of RF chains) and baseband processing (capability to process measurements)
  If UE cannot support “per-FR gaps” for a single high order CA/DC combo(e.g. 5-6 CCs CA combo in FR1 or inter-band CA in FR2)
The current Rel-15 “per-UE” based “per-FR gap” capability makes the feature difficult to support for FR1+FR2 capable UEs because requirements associated to the feature shall be fulfilled even for the highest order of CA combination that can be supported by the UE.
Feature is very useful to increase throughput during measurements – see Annex

## Slide 4: RAN4 Background (1)
In RAN4 it was proposed to add a “per-BC” based “per-FR gap” capability
  Single bit per band combination
  Can be introduced in a backwards compatible way by maintaining the per UE bit and add this new capability bit
    UEs supporting the capability for all combinations can signal the “old bit”
    UEs supporting the capability only on certain combinations can set the per UE bit to 0 and set the bit to “supported” for the combinations in which the feature is supported

## Slide 5: RAN4 Background (2)
RAN4 discussed the proposal for a few meetings, there are still objections without clear technical justification
  Added complexity of NW side -> network can ignore the new signaling and not configure per FR gaps
  Major changes to RAN4 specifications -> changes are small, if any. Requirements depending on per FR gaps still apply for each combination depending on whether UE supports per FR gaps or not for the configured combination
  Too late for changes in Rel. 16 -> New capabilities were just introduced for Rel.16 in Q2 2021
However, the proposal was not adopted without any technical reason. RAN4 made instead the following agreement.
  RAN4 has a common understanding that further enhancements to the per-FR measurement gap UE capabilities to address UE implementation constraints can be further studied in future (e.g. in Rel-17) and the work is subject to RAN plenary approval and available time budget.

## Slide 6: Proposal
Introduce a new A new “per-BC based per-FR gap capability” in Rel.16
  If the feature cannot be introduced from Rel.16 because it is “too late”, it should be introduced from Rel.17

## Slide 7: Annex

## Slide 8: Benefit to NW/UE from the new “per-BC based per-FR gap” capability
A better FR1/FR2 resource utilization is expected even without a precise cell deployment in terms of SSB periodicity, SMTC, measurement gap configurations for FR1 and FR2 cells.
For example,
  when UE doesn’t support the per-FG gap feature just because it cannot meet all the relevant RAN4 requirements in some extreme cases, NW may have to configure parameters such as SSB periodicity, SMTC, and MG (gapUE) very much precisely so that UE can use a one MG pattern for both FR1 and FR2 measurements while not losing too much throughput. In other words, the MG should be configured in such a way that the configured FR1 and FR2 measurement resources fall into one common MG if the measurement requires a gap, e.g. the UE can go and measure FR1 and FR2 in every alternating MGs, otherwise it will result in a significant throughput loss.

## Slide 9: Benefit to NW/UE from the new “per-BC based per-FR gap” capability
FR2
FR1
FR2
FR1
MG
for FR1
MG
for FR2
No traffic scheduling
on FR2 cells
UE is configured with 4 FR2 cells and one common MG for both FR1 and FR2 cells
6ms
40ms
40ms
1.5ms
MG for
FR1 and FR2
15% loss on FR2
with MG#0
80ms
6ms
3.75% loss on FR2
with MG#21
UE is configured with 4 FR2 cells and one MG for each FR

## Slide 10: RAN4 Discussion and Conclusion References
Technical contributions for “per-BC” based “per-FR gap” capability
  2020 Nov. RAN4#97 e-meeting
    R4-2014488, “Overloading of the Per-FR gap capability,” Qualcomm Incorporated
  2021 Jan. RAN4#98 e-meeting
    R4-2101659, “Discussion on per-FR gap capability,” Huawei, HiSilicon
  2021 Apr. RAN4#98bis e-meeting
    R4-2106989, “Discussion on per-FR gap capability,” Huawei, HiSilicon
    R4-2106442, “Discussion on UE capabilities,” Intel Corporation
  2021 May RAN4#99 e-meeting
    R4-2110367, “On UE behavior due to separate NR HST capability and on Per BC indication of per-FR gap,” Huawei, HiSilicon
    R4-2109225, “Discussion on UE capabilities in Rel-16,” Intel Corporation
    R4-2108332, “WF on per-BC indication of per-FR measurement gap UE capabilities,” Qualcomm Inc.
    Email discussion: [99-e][241] R16_UE_feature_list_RRM-WF on per-BC indication of per-FR measurement gap UE capabilities