## Slide 1
RRC-less solution for SDT
3GPP TSG RAN Meeting #92e
Electronic Meeting, June 14 – 18, 2021
Source: ZTE, Sanechips
Agenda: 9.7.2.7
RP-211433

## Slide 2: General status
Small Data Transmission (SDT) feature enables the UE to send and receive small data packets whilst the UE is in INACTIVE state
Two mechanisms are being specified to support SDT
  RA-SDT: Where the SDT transmission is initiated by RACH procedure and both 2-step and 4-step RACH are supported for this
  CG-SDT: Where type 1 configured grant resources are configured for the UE to be used in INACTIVE state in a given cell
At the very beginning of the WI, RAN2 discussed RRC-based and RRC-less solutions for SDT
  RRC-based solution includes an RRC message (sent over the CCCH channel) to initiate SDT
    RRC-based solution works both for CG-SDT and RA-SDT
    RRC-based solution works in the same cell as well as in a different cell (than the cell in which the UE entered INACTIVE state)
  RRC-less solution does not include any RRC message in the first UL message
    RRC-less solution only works in the same cell as the cell in which the UE entered INACTIVE state
Considering the commonality across RA-SDT, CG-SDT and mobility scenarios as noted above, RAN2 agreed to use the RRC-based solution as baseline for both RA-SDT and CG-SDT and deprioritised the RRC-less solution

## Slide 3: Discussion on RRC-less solution
Some companies have promoted RRC-less solution with the expectation that it provides better signalling overhead
Other companies pointed out that this depends on a number of considerations
  Some of the information included in the CCCH message is assumed to be redundant in case of RRC-less solution
    Further discussion is needed in RAN2 on which information in CCCH message is redundant
    There may be implications on RAN3 and SA3 for the above discussion and these dependencies need to be checked
  The gains materialise for the same cell scenario only
    It is generally understood that an RRC message is necessary in case of cell change
  There seem to be different views on how the RRC-less solution is terminated
    Options include an RRC message in DL to terminate the RRC-less SDT and a solution where there is no RRC message in DL either
    The overall gains again depend on which solution is chosen eventually
Further effort is needed to iron-out these details (first in RAN2) and then to trigger the necessary interaction with other WGs

## Slide 4: Status of the general discussions in RAN2 for SDT
As with other Rel-17 WIs, the work on SDT is being progressed as best as possible given all the bottlenecks that result from the loss of face-to-face meeting time
A base-line solution for SDT which works for both RA-SDT and CG-SDT is essential to deliver the SDT work in Rel-17
  RRC-based solution is such baseline
  RRC-less solution is not essential for the feature to work
    If only one solution were to be specified for the Rel-17, then RRC-based solution that works for all scenarios is the obvious choice
Work on deprioritised aspects should only be considered when there is time in the WGs after completing the base-line work
  Although SDT work is progressing as planned, the current status of the work is not yet at a state where the deprioritised work can be taken on board
    Some stage-2 aspects of the RRC-based solution are still open
    Stage-3 CRs have just been initiated and this will require more time and effort from delegates to iron out the details and the review process will also require further meeting time

## Slide 5: Conclusion and proposals
Proposal 1: RAN2 continues to focus on RRC-based solution for SDT
Proposal 2: RAN plenary to discuss the RRC-less solution at RAN#93 as part of the general discussions on Rel-17 WI scope

## Slide 6: Thanks