## Slide 1
RP-211469
Agenda Item: 10.5.1
Type: Discussion
Document for: Discussion
3GPP TSG RAN 92-e
June 14-18, 2021
Market rationale for IoT NTN features in Release 17
Sources: Novamint,

## Slide 2
Strong need for “urgent” IoT over NTN solutions for many verticals:
  Asset tracking / container
  Asset monitoring (utilities, railway…)
    Remote areas
    Mountains
  Back up or roaming
Proprietary solutions emerging
  Decision are made now – long lasting (5 years min) once engaged
Verticals perspectives on IoT over NTN

## Slide 3
  First solution of 3GPP “IoT over NTN” work with existing ecosystem (Operators / devices)
Allow cost-effective solution:
  On the device:
    Minimum impacts (antenna, battery…)
    Capability to reuse existing devices as much possible…
    Generic cellular device supporting both TN & NTN
  On the NTN side – similar cost than TN (LEO 600 + existing GEO)
Key market expectations

## Slide 4
Smart grid asset monitoring use cases
 | Characteristics
Main Assets to monitor in the grid | Remote-controlled Switches/Operating device Fault Indicators Sensors along Hydroelectric Plants
Location | Outdoor Mainly Rural areas / mountains
Type of message | MO mostly No Application level ACK needed MT for Remote-controlled Switches
Payload size | 12 to 100 Bytes
Transmission periodicity | 1 per day (keep alive)
Duration of life | 15-20 years
Network access | Seamless support of TN & NTN

## Slide 5
Essential features to be supported
Essential Features | Rationale
Connection to EPC / 4G core | Support of existing ecosystem & operators’ deployments
Standalone deployment for NB-IoT / eMTC | Easy deployment
Support of legacy cell selection/reselection mechanisms | No need for enhancement for basic asset monitoring
Support of legacy Handover and RLF/reestablishment mechanisms | No need for enhancement for asset monitoring
DRX, PSM, eDRX, relaxed monitoring and WUS without enhancements | No need for specific enhancement for asset monitoring (as for Terrestrial) expect for addressing specific NTN needed enhancement with discontinuous coverage
Support of Discontinuous coverage | Key NEW Feature very important for asset monitoring to reduce power consumption when device waking up to communicate with Satellite (especially needed for early constellation with limited number of Satellite or when constellation is changing)
All features
identified
in
TR 36.763 v1.0.0
=> Essential features have been identified for Release 17 for market adoption

## Slide 6
Next Steps
Study Item ““IoT over NTN” completed for Release 17
Ready for Work Item to start
Decision: to approve Work Item in accordance with TR 36.763 recommendations