## Slide 1: Discussion on introduction of new UE categories with 1 Rx based on Category 3 and 4 for LTE
3GPP TSG RAN Meeting #92-e
Electronic Meeting, June 14th – 18th, 2021
Document for: Approval
Agenda Item: 10.11
Source: CAICT, China Telecom, China Unicom, CMCC, Guangdong Genius, Honor, Huawei, HiSilicon, OPPO, Samsung, Spreadtrum, vivo, Xiaomi
RP-211493
Was RP-211466

## Slide 2
Background
In Rel-14 the new UE DL category 1bis (Cat 1bis) was introduced for wearable devices with single antenna based on UE category 1 [1].
  The new RF, RRM and performance requirements are specified for Cat 1bis to verify the single Rx antenna performance in TS 36.101 and TS 36.133 (RAN4)
  The new DL category 1bis is specified in TS 36.306 and TS 36.331 (RAN2)
  To ensure backward compatibility, UE indicating support of Category 1bis is mandated to report both Category 1bis and Category 1.
An urgent market need is observed for high-end wearable devices, e.g., smart children watches to support High Definition Video, and the data rate of this devices cannot be met by LTE Category 1bis.
At the same time due to form factor reasons, that is same as for Category 1bis, such wearable devices would require single Rx, which cannot be supported by LTE Category 3 and 4.

## Slide 3
Discussion-1
To meet high-end wearable devices market demand, new UE DL categories with single Rx antenna and support of higher throughput than LTE Cat 1bis need to be defined from Rel-17. Possibility for early implementation should be discussed.
The new DL categories with single Rx antenna based on Category 3 and Category 4 could be considered as we did for Cat 1bis in TS 36.306 and TS 36.331.
Also to ensure backwards compatibility, a UE indicating support of Cat 3bis and Cat 4bis is mandated to report both Cat 3bis/Cat 4bis and Cat 3/Cat 4.
Proposal 1: Define new LTE UE DL categories 3bis and 4bis with single Rx antenna based on UE category 3 and 4 in TS 36.306 and TS 36.331.

## Slide 4
Discussion-2
Because a similar framework has already been established for Cat 1bis, and in our view most of RAN4 requirements for Cat 1bis could be reused for Cat 3bis/4bis except the peak data rate, and considering the urgent market demand, we would like to minimize the workload for introduction of the new DL UE categories:
  Reuse the REFSENS requirements of Cat 1bis defined in TS 36.101
  Reuse all RRM requirements of Cat 1bis defined in TS 36.133
  Reuse all demodulation tests and CQI test of Cat 1bis defined in TS 36.101
  Specify additional SDR (Sustained DL Data Rate) tests to verify the peak data rate for new DL category 3bis and Category 4bis in TS 36.101
  Complete the above work within one quarter by TEI-17 considering that most of requirements specified for Cat 1bis are reused
Proposal 2: For LTE Cat 3bis and Cat 4bis, reuse the existing RF, RRM and performance requirements specified for DL 1bis to verify single Rx antenna performance, and add additional SDR tests to verify the peak date rate.
Proposal 3: Task RAN2 and RAN4 to finalize the work for LTE Cat 3bis and Cat 4bis in TEI17

## Slide 5
Discussion-3
Introduction of Cat 3bis/4bis does not mean the introduction of new type of chipset. In our understanding, the wearable devices still use chipset of Cat 3 and Cat 4. Because of limitation of form factor, only 1Rx is enabled.
There is massive demand for such kind of high-end wearable device with the increasing need of support video application, especially in China, without corresponding 3GPP specification, the certification process is impacted.
The proposed LTE Cat 3bis/4bis are for immediate market needs, while Rel-17 NR RedCap is not available for market yet.
In case some companies have concerns about the impact to legacy network, from our perspective, one approach that can be considered is:
  A UE reporting Category 3bis/4bis can report and therefore fall back to Cat 1bis when it roams to other regions, considering also that Cat 1bis UEs existed in the networks around the world for a long time already.
Proposal 4: UE reporting Category 3bis/4bis can report and therefore fall back to Cat 1bis when it roams to other regions if needed

## Slide 6
Reference
[1] RP-170791, Revised WID: Requirements for a new UE category with single receiver based on Category 1 for LTE, Qualcomm