## Slide 1: In-device coexistence for NR
3GPP TSG RAN#93-e
Electronic Meeting, 13th – 17th September, 2021
RP-212032
Xiaomi Communications, T-Mobile USA,
Deutsche Telekom, TELUS, Bell Mobility, Telstra, Telecom Italia, CMCC, China Telecom, China Unicom, Apple, Sony, TCL Communication Ltd., Spreadtrum Communications, OPPO, CATT, InterDigital

## Slide 2: IDC issues
The IDC issues include the followings:
  Cross band frequency interference between 3GPP and other RAT(s), or between 3GPP frequencies
  Harmonics, harmonic mixing and Inter-modulation (amongst 3GPP frequencies) interference to 3GPP or other RAT(s)
  Harmonics, harmonic mixing and Inter-modulation (between 3GPP frequency(ies) and other RAT) interference to 3GPP or other RAT(s)
  Capability sharing (e.g. shared RF chain, or shared UL power, or shared MIMO layer(s)) between 3GPP and other RAT(s), or between different SIM(s).
  Measurement (e.g. for SON or MDT) inaccuracy caused by IDC
  RLF/HOF caused by the IDC interference

## Slide 3: MSD issue
Issue: Too large values of MSD for the DL band of band combinations causes that gNB is not able to configure CA, or else the network configures CA and ignores MSD.
Maximum sensitivity degradation (MSD) is specified for CA and DC configurations where there is Rx interference caused by Tx (i.e., harmonics, intermodulation products, etc)
MSD is sometimes specified to be very large, i.e., more than 20 or 30 dB! This is a severe impact to DL performance and renders CA practically unusable for most UE’s in the cell.
RP-211305, Improved MSD for CA and DC, Qualcomm Incorporated, T-Mobile USA, Verizon, AT&T, DISH Network, TELUS, Deutsche Telekom, CMCC, CHTTL, KT Corp, Vodafone, BT plc., Telecom Italia, Bell Mobility
Observation: The UE internal interference issue caused by the MSD in CA/DC can be considered as a subset of the IDC issues.

## Slide 4: What can IDC do to resolve MSD issue?
Dynamic indication of the harmonic/inter-modulation interference via IDC report from the UE: (e.g. IDC FDM solution)
  Aggressor frequency or frequency-combination
  Victim frequency
  The relation between the aggressor and the victim
Combination of IDC and “low MSD” capability
  The UE not indicating “low MSD” may still be able to use CA in the following cases:
    Case 1: The real sensitivity of the UE receiver is (normally) higher than the REFSENS.
    Case 2: The interference to the DL could be small when the Tx power is not large (e.g. UEs in cell center or small cell).
    Case 3: The UE could still be able to decode the DL signal when the received signal power is large, even though the interference to the DL is not small.
  When the UE indicates the capability “low MSD”, the UE does not need to provide the IDC report.
  When the UE does not support “low MSD”, the UE can be configured to provide the IDC report.

## Slide 5: Defects of the current IDC report
Issues of the current IDC reporting for MSD:
  Not able to indicating the interference between 3GPP frequencies (i.e. Aggressor frequency is 3GPP, and victim frequency is also 3GPP).
  The UE does not know when to indicate the harmonic/inter-modulation interference. The harmonic/inter-modulation interference is always there for some band combinations. It is not clear to the UE what interference level is not acceptable to the gNB while configuring CA/DC.
In Rel-15, the IDC FDM solution is introduced to support the EN-DC. In Rel-16, the IDC FDM solution is introduced to support the standalone NR. However, the current solutions for NR IDC issues have the following defects:
No clear trigger event (e.g. like the measurement report event) is defined for the IDC report, as whether the interference to other RATs is acceptable to other RATs is out of the scope of 3GPP, and there is no measurement defined for the interference from other RATs.
Do not support NE-DC.
Do not support TDM solution (e.g. autonomous deny and UE preferred TDM pattern (e.g. UL/DL configuration)).
The UE is only allowed to report the ARFCN. When a large range of frequencies (e.g. 40 MHz) is affected, the UE needs to indicate a long list of ARFCN(s). If the UE only indicates one frequency within the affected frequency range, it is not clear for the gNB whether a large range of frequencies is affected or whether only a small bandwidth including the reported frequency is affected.
Cannot resolve the capability sharing issue.
Cannot resolve the measurement inaccuracy issue (e.g. for SON or MDT).

## Slide 6: Full list of potential solutions of IDC proposal
The IDC proposal is to identify the aggressor/victim band(s)/channels due to the in-device coexistence issue within the same UE operating on NR frequency, and to provide solution(s) that can effectively avoid/reduce/cancel coexistence interference.
The IDC proposal includes:
Identify the solution(s) (e.g. via dynamic report or via static UE capability report) to indicate the interference issue caused by the MSD of CA/DC. (RAN4, RAN2) (The Rel-18 discussion on the MSD issue is pending for the Rel-17 RAN4 MSD discussion.)
Enhanced FDM solution, which allows more flexible indication of affected frequencies (e.g. granularity of BWP or sub-band or PRB level). (RAN2)
TDM solution (e.g. indication of UE preferred TDM pattern for UL/DL). (RAN2) (TBD on whether autonomous deny of UL transmission is needed.)
Indication of allowed UE capability for the gNB (e.g. allowed band/ band combination, allowed transmission power and allowed MIMO layer): (RAN2)
  The UE can indicate the allowed UE capability between SIM(s) (TBD on whether this should be discussed in another WI of multi-SIM)
  The UE can indicate the allowed UE capability between different RATs (e.g. between 3GPP and WiFi) (TBD on whether this should be included.)
Indication/suspension of IDC-affected measurement (e.g. for immediate MDT). (RAN2) (TBD on whether this is included, e.g. for immediate MDT or early measurement.)
Note: The specified solutions are expected to be applicable to various MR-DC architectures (including NR-DC, EN-DC). (TBD on whether NE-DC is included.)
Note: The objectives which are acceptable to most companies are highlighted in Green.

## Slide 7: Issues to be resolved in the IDC proposal
The IDC proposal would mainly target at resolving the following issues:
The interference caused by the high MSD value of 3GPP CA/DC. (The Rel-18 discussion on the MSD issue is pending for the Rel-17 RAN4 MSD discussion.)
The interference between 3GPP and other RATs.
Capability sharing issue between 3GPP and other RATs.

## Slide 8: Solutions of IDC proposal
The IDC proposal is to identify the aggressor/victim band(s)/channels due to the in-device coexistence issue within the same UE operating on NR frequency, and to provide solution(s) that can effectively avoid/reduce/cancel coexistence interference.
The IDC proposal includes:
Identify the solution(s) (e.g. via dynamic report or via static UE capability report) to indicate the interference issue caused by the MSD of CA/DC. (RAN4, RAN2) (The Rel-18 discussion on the MSD issue is pending for the Rel-17 RAN4 MSD discussion.)
Enhanced FDM solution, which allows more flexible indication of affected frequencies (e.g. granularity of BWP or sub-band or PRB level). (RAN2)
TDM solution (e.g. indication of UE preferred TDM pattern for UL/DL). (RAN2)
Indication of allowed UE capability between 3GPP and other RATs (e.g. WiFi) (RAN2)
Note: The specified solutions are expected to be applicable to various MR-DC architectures (including NR-DC, EN-DC).

## Slide 9: Thanks