## Slide 1: Views on Rel-18 Sidelink Relay Enhancements
RP-212248
3GPP TSG RAN WG Meeting #93-e
Electronic Meeting, September 13 - 17, 2021‎
Document for: Discussion
Agenda Item: 9.0.3
China Academy of Telecommunications Technology (CATT)

## Slide 2
Sidelink relay enhancements got wide interests as one potential area for Rel-18 evoluation
  During the pre-meeting email discussion ([RAN93e-R18Prep-06]), 30 companies expressed interests in this area.
Related Progresses are being made in other TSGs/WGs, e.g.,
  In SA2, [1] was agreed to server as a basis for further discussion of Rel-18 ProSe;
  In [2], SA3 already started the study of sidelink relay security issues;
  In [3], SA5 is studying the charging aspect of sidelink relay;
  In [4], CT groups agreed to study the support of UE-to-Network relay for proximity based services.
Background
Reference:
[1] S2-2106806 New SID on Study on Proximity based Services in 5GS – Phase 2 CATT, OPPO
[2] S3-213236 Study on Security Aspects of Enhancement for Proximity Based Services in 5GS CATT, China Unicom
[3] S5-205468 Revised SID on charging aspects of Proximity-based Services in 5GC CATT
[4] C1-214476/C4-214568 Revised WID on CT aspects of proximity based services in 5GS CATT, OPPO

## Slide 3: Overview of the previous discussion
 | Topic | Majority view on the scope | Further questions to discuss
Non-controversial | U2U | Single hop U2U relay | Both L2 and L3? Limited to unicast? Secondary WG to involve?
 | Service continuity | Inter-gNB mobility Indirect/indirect path switching | Indirect/indirect path switching includes the inter-gNB case?
Controversial | Multi-path | Direct + indirect | Limited to intra-cell?
We will discuss on these questions and present our views in the reminder of this document.

## Slide 4: Single-hop U2U relay
Motivation
  Meet the requirements of various uses cases, e.g.,
Views on the FFS issues
V2X use case | Public safety use case
 | Our view | Reasoning
Both L2 and L3? | Yes | Relay discovery/(re-)selection procedures are common for L2 and L3 U2U relay.
Limited to unicast? | No, for all cast types | BC/GC is important for both V2X and public safety services.
Secondary group to involve? | RAN3 | RAN3 should be involved for relay/remote UE authorization.

## Slide 5: Single-hop U2U relay (cont.)
Potential scopes
  U2U relay discovery and (re-)selection;
  Relay and Remote UE authorization;
  PC5 adaption layer design for L2 U2U relay;
  Control plane procedures;
  User plane procedures (e.g., resource allocation).

## Slide 6: Service continuity enhancements
Motivation
  Meet the all the possible mobility requirements in real deployment.
Views on the FFS issues
 | Our view | Reasoning
Whether indirect/indirect path switching includes the inter-gNB case? | Yes | This scenarios is valid in relay deployment. Compared with intra-gNB case, the additional specification effort is not much.
Indirect/direct path switch (inter-gNB) | Direct/indirect path switch (inter-gNB) | Indirect/indirect path switch

## Slide 7: Service continuity enhancements (cont.)
Potential scopes
  Service continuity enhancements for inter-gNB case:
    e.g., direct/indirect, indirect/indirect and indirect/indirect path switching.
  Service continuity enhancements for intra-gNB case:
    e.g., indirect/indirect path switching.

## Slide 8: Multi-paths
Benefits vs effort
  From the performance improvement aspects, introducing multi-paths can improve the reliability and peak data rate especially for cell edge UE, which is meaningful for the user experience;
  The work load should be manageable based on further discussions on the exact scenarios to cover in this release
It is therefore suggested to include multi-paths as part of Rel-18 work scope.

## Slide 9: Multi-paths (cont.)
Whether multi-paths should be restricted within one cell?
  Both intra-cell multi-paths and inter-cell multi-paths can be considered:
    Relay UE and remote UE may in the coverage of different cells, hence it is natural to support multi-paths across different cells.
    In Uu, UE can aggregate multiple serving cells. Hence, there is no strong motivation to exclude it with the introduction of sidelink relay.

## Slide 10: Multi-paths (cont.)
Which kind(s) of multi-paths should be considered?
  Indirect/direct multi-paths should be studied with higher priority.
  Indirect/indirect multi-paths, due to its complexity, could be put to lower priority.

## Slide 11: Summary
This document present CATT’s views on some open questions based on the previous email discussions on SL relay enhancements.
It is suggested to include multi-paths into Rel-18 SL relay enhancement work scope.
A WID is provided in [5], as an input to RAN’s further discussions on the topic.
Reference:
[5] RP-212249‎, New WID: Sidelink Relay Enhancements, CATT