## Slide 1: HAPS in Release 18
RP-212263
Ericsson

## Slide 2: Background
The Release 17 NTN Work Item covered both Satellite and HAPS
The TR 38.821 describes the WI outcome. Although both Satellite and HAPS are covered, the TR is rather focused on Satellite

## Slide 3: Discussion
HAPS deployment scenarios differ from Satellite deployment scenarios
The deployment, configuration and operation of HAPS networks will differ from Satellite networks. Our understanding though is that the RAN1-3 specifications are sufficiently flexible to accommodate both kinds of network.
In case it is discovered that HAPS specific optimizations are needed, a place is needed to discuss and include them
HAPS will be related to NTN in several aspects
The Release 18 NTN WI should contain objectives to address, if needed, any HAPS related issues that necessitate changes or additions to the specifications, and improve the documentation of HAPS in the TR

## Slide 4: Proposal
The following HAPS related objectives are included in a Rel-18 NTN WI:
Address HAPS deployment and configuration scenario(s) for which the current specifications are not sufficient, if identified.
  Possible aspects not covered in current specs might include
      Co-ex study with other HAPS and/or TN, i.e., leftovers from Rel-17 including frequency sharing between TN and HAPS (RAN4)
      Mobility and interference considering spectrum (RAN1/2)
      Applicability of TDD from remote interference PoV (RAN1)
      Applicability of regenerative and transparent payload (RAN2/3)
Ensure that the TR 38.821 adequately captures that HAPS deployment scenarios are taken into account and enabled in the NTN related specifications.