## Slide 1: Motivation for New WID on User Plane Integrity Protection support for EPC connected architectures using LTE and EN-DC
Source: Vodafone
Agenda Item 9.1.3
3GPP TSG RAN Meeting #93e
Electronic Meeting, September 13 - 17, 2021
RP-212298
Update of RP-211432

## Slide 2: UPIP support for EPC connected architectures using LTE and EN-DC
Background and SA 3 Status (September 2021)
  In order to provide user plane data security, SA3 have agreed to support UPIP for EPC connected architectures. The conclusions are captured in the version of TR 33.853 that is sent for approval in the June TSG SA #92e plenary.
  March TSG SA #91e plenary agreed the “WID for normative changes for User Plane Integrity Protection for LTE options” in SP-210105.
  SA3 has been discussing normative CRs but have not yet sent them to TSG-SA for approval.
  Their “living”, draft CRs are in S3-213266 for TS 33.401 and S3-213256 for TS 33.501.
RAN 2 and RAN 3 status
  SA3 questions have been answered in response LSs in R2-2104349 (from April RAN 2 #113bis-e) and R3-212812 (from May RAN 3 #112-e). RAN 2 have indicated that NR PDCP will be used to provide UPIP.
  Clause 4.2.2 of TS 37.340 (Release 15 and onwards) already permits the use of NR PDCP on LTE-only radio connections.
RAN 92-e (June 2021)
  A draft WID in RP-211431 was discussed under discussion thread [92-e-27-UserPlane-Integrity] and summarised in RP-211564.
  There was a preference for a WID rather than use of TEI-17, and a preference for RAN 3 to lead.

## Slide 3: UPIP support for EPC connected architectures using LTE and EN-DC
SA 2 Status (September 2021)
  SA2 have agreed the following stage 2 CRs and they are attached to an LS in RP-212494 (S2-2106974)
    TS 23.401 CR3645r1
    TS 23.501 CR 3009r1
    TS 23.502 CR 2957r1
RAN #93-e
  Draft WID is updated in RP-212297
  Still includes:
    EPC <-> LTE-only, and
    EPC <-> EN-DC for both S1-U terminated in eNB and en-gNB
  But now excludes NB-IoT (as Control Plane data supports full rate integrity protection)
  eMTC remains “in scope” as it shares a common RRC protocol with “LTE”.
  Clearly indicates that UPIP in LTE is intended to be optional (for security related reasons, the support/non-support of UPIP will, at least, be signalled in NAS signalling).
  Indicates that this is “full data rate UPIP or nothing” without any Release 15-style 64 kbit/s option.

## Slide 4: UPIP support for EPC connected architectures using LTE and EN-DC
Proposal
  Agree RP-212297 – a New Release 17 building block WID for RAN 2 and RAN 3 to specify the RAN enhancements to enable UPIP (at the full data rate supported by the UE) for the following EPC connected architecture options:
    EPC <-> LTE-only, and
    EPC <-> EN-DC for both S1-U terminated in eNB and en-gNB

## Slide 5: Thank you