## Slide 1: Evolution of NR positioning in Rel-18
3GPP TSG RAN Meeting #93-e
Electronic Meeting, September 13 - 17, 2021
Source: ZTE, Sanechips
Agenda: 9.0.2
RP-212381

## Slide 2: Overview
    Sidelink positioning in Rel-18
      Enable sidelink positioning in out-of-coverage, partial-coverage and in-coverage scenarios
    Further enhancements on accuracy, integrity, and power efficiency
      Accuracy enhancement for general use cases, mainly focus on multiple frequency layers/carriers aggregation
      Extend positioning integrity for more positioning methods
      Power efficiency enhancement to support positioning in RRC inactive sate(when network triggering location service)
    RedCap positioning

## Slide 3: SL Positioning – Scenarios and Requirements
Requirements based on TR38.845
V2X:
- Set 1: 10 – 50 m with 68 – 95 % confidence level. This includes Group 1 in 3GPP RP-210040(Source 5GAA) and Service level 1 in TS22.261
- Set 2: 1 – 3 m with 95 – 99 % confidence level. This includes Group 2 in 3GPP RP-210040(Source 5GAA), Service level 2, 3, 4 in TS22.261.
- Set 3: 0.1 – 0.5 m with 95 – 99 % confidence level. This includes Group 3 in 3GPP RP-210040(Source 5GAA), Service level 5, 6, 7 in TS22.261, the requirements in TS22.186.
Public Safety:
- 2 – 3 m (absolute) or 0.2 m (relative) vertical accuracy, 95 – 99.9% positioning service availability, 10 ms – 1 s positioning service latency.
Scenarios

## Slide 4: SL Positioning – Positioning methods
    Support absolute positioning and relative positioning
      Strive to resue Rel-16/17 NR positioning methods (Probabaly with slight modification) including RTT(multi-RTT), OTDOA, etc.
        Absolute positioning
          Should be applicable for in-coverage and partial-coverage scenarios
          SL positioning measurement can complement to Uu positioning for better accuracy/low latency absolute positioning
        Relative positioning
          Should be applicable for all of in-coverage, partial-coverage and out-of-coverage scenarios
RTT for relative positioning
OTDOA for SL positioning

## Slide 5: SL Positioning – Signaling design
    Strive to resue Rel-16/17 NR RS design with necessary adpation
      Staggering Pattern and Comb Structure with AGC symbol
      PN sequence (Sidelink info. e.g. source ID for initialization)
    Considering separate PRS resource pool from the existing SL resource pool
      Larger PRS bandwidth than PSSCH is supported for more positioning accuracy
      Support SCI triggered PRS transmission
        Rel-16/17 SL signaling/configuration should be the starting point
PRS symbol #0 #1 # 2
Because the existing sidelink specification cannot support beam management in FR2 and unlicensed spectrum well (Rel-18 V2X may have the corresponding enhancement), we propose to deprioritize(or not support) sidelink positioning in FR2 and in unlicensed spectrum in Rel-18

## Slide 6: SL Positioning – Initial simulation results
UE drop | Option A -Vehicle type distribution: 100% vehicle type 2. -Clustered dropping is not used. -Vehicle speed is 140 km/h in all the lanes for the highway scenario -Vehicle speed is 60 km/h in all the lanes for the urban grid scenario:
Carrier frequency | 6GHz
Bandwidth | 20MHz
Subcarrier spacing | 15KHz
Channel model | As defined in 37.885
transmitter-receiver association | For each transmitter, the target receiver is randomly selected among the UEs within X=150 meters

## Slide 7: SL Positioning – Proposals
    Motivation
      Positioning in three scenarios:
        Positioning in out-of-coverage : Network independent, GNSS is not reliable in some cases
        Positioning in in-coverage : Complement to Uu positioning for better accuracy/low latency absolute positioning
        Positioning in partial-overage
      Low latency/high accuracy relative positioning for all scenarios
      Lowe latency/high accuracy absolute positioning for in-coverage and partial coverage scenarios
    Potential Further Study and Normative Work [ RAN1, RAN2]
      Study evaluation methodology and evaluate SL positioning and SL assisted Uu positioning
      Target to fulfill at least some of requirements captured in TR 38.845
        Support absolute positioning and relative positioning.
        Specify SL RS/channel
        Specify SL signaling including SL PRS configuration, SL location request, measurement report, etc.
        Support Uu positioning solutions + sidelink positioning solutions for in-coverage and partial coverage scenarios
          Enhance LPP and NRPPa protocol

## Slide 8: Further accuracy enhancement
    Motivation
      Pursue higher positioning accuracy for UEs supporting multiple positioning frequency layers (PFLs) or carriers
        For example, in China, band n41 (160MHz bandwidth ) and band n78 (two chunks of 100MHz bandwidth) are very promising to be deployed with intra-band CC/PFLs aggregation
    Potential enhancements [RAN1, RAN4]
      Prioritize intra-band PFLs/CCs aggregation over inter-band PFLs/CCs aggregation
      Study the solutions to mitigate the impact of timing error delay and phase offset
      Coherent transmission & reception for DL PRS from mutiple PFLs
      Coherent transmission & reception for positioning SRS from multiple carriers
      Details of RS enhancements, UE and gNB masurements and physical-layer procedures

## Slide 9: Extend integrity for more positioning methods
    Status
      Positioning integrity is supported only for A-GNSS in Rel-17
      Positioning integrity for RAT-dependent is not included in Rel-17 WI
    Motivation
      Specify the positioning integrity for other positioning solutions, e.g.
        RAT-dependent: DL-TDOA, UL-TDOA, DL-AoD, UL-AoA, multi-RTT
    Potential Further Study and Normative Work [RAN2]
      Strive to reuse procedures and signaling for Rel-17 defined integrity
      Study whether new requirements are needed
      Introduce new feared events for new involved positioning solutions

## Slide 10: Power efficiency enhancement
    Status
      Positioning for UE in RRC inactive state will be specified in Rel-17 in the case when UE initiates location service;
      Positioning for UE in RRC inactive state will not be supported in Rel-17 in the case when network initiates location service
    Motivation
      Support positioning for UE in RRC inactive state when network initiates location service
    Potential enhancements [RAN2]
      Specify positioning procedures, signaling, etc. for UE in RRC inactive state when network initiates location service
        Considering DL, UL and DL+UL positioning methods

## Slide 11: Support RAN-dependent positioning for RedCap UEs
    Motivation
      high accuracy under low bandwidth, low power consumption
      low latency under low UE processing capability, low UE complexity
        Probably looser targets of accuracy and latency should be defined compared with Rel-17
      Large capacity, i.e. Large number of devices for positioning
    Potential enhancement for RedCap UEs[RAN4, RAN1]
      Define new positioning requirement/capability, e.g.
        New PRS processing capability including PRS buffering capability
        New Measurements Period Requirements
      Study and specifiy if need new positioning methods, positioning RS, signaling and procedures to improve capacity, latency reduction and positioning accuracy

## Slide 12: Overall proposal for Rel-18 positioning
    Motivation
      Support sidelink positioning
      Enhancement on positioning accuracy, integrity and power efficiency
      Define new positioning requirement/capability for RedCap UEs
    A work item with study phase can be considered:
      Study and if needed, specify the functional components, procedures, signaling, etc. to enable positioning in out-of-coverage, in-coverage and partial coverage scenarios for Sidelink [RAN1, RAN2]
        Support absolute positioning and relative positioning
      Specify multiple PFLs aggregation for joint DL PRS transmission/reception and specify multiple carriers aggregation for joint UL SRS transmission/reception [RAN1, RAN4]
      Specify positioning integrity for RAT-dependent positioning methods [RAN2]
      Specify positioning procedures and signaling for UE in RRC inactive state when network initiates location service [RAN2]
      For RedCap UEs, define new positioning requirement/capability and study new positioning methods, RS, signaling and procedures to improve capacity, latency reduction and positioning accuracy [RAN4, RAN1]

## Slide 13: Thanks