## Slide 1
SDT enhancements for Rel-18
3GPP TSG RAN Meeting #93e
Electronic Meeting, September 13 – 17, 2021
Source: ZTE, Sanechips
Agenda: 9.0.3
RP-212397

## Slide 2: Background
Applications generating small and infrequent data are becoming more prevalent
With higher penetration of the 5G devices requirements on the system to optimise for such traffic becomes ever more important
Latency, power consumption and signalling overhead for such small data traffic is a well known bottleneck in 5G systems
Rel-17 has addressed some of these issues for mobile originating traffic through the work item for small data transmission (SDT) in INACTIVE state
Supporting more applications for SDT will improve the overall system efficiency
Rel-17 work focussed on the following for INACTIVE state:
  Only mobile originating traffic is considered
  Minimisation of signalling overhead and latency over the air-interface is prioritised
  Optimisation of the SDT session for the successful SDT case (i.e. data recovery for abrupt termination of SDT session or late anchor relocation etc were deprioritised)
Background traffic characteristics in UL – source 3GPP TR 36.822

## Slide 3: MT traffic
Any DL traffic generated as a result of the mobile originated traffic can still be sent to the UE during SDT session as part of the Rel-17 work
However, not all applications generate MO-traffic at all times
Any MT-data will require the to UE move to CONNECTED state in case of Rel-17 SDT
Some critical applications exist for MT small data traffic:
  Positioning applications that are initiated by MT traffic (e.g. the positioning server paging the device for its location) is a well known application
  Whilst some applications rely on keep-alive packets in UL, many applications rely on the central server periodically pinging the clients for updates
  IM and other chat clients generate a lot of traffic that is MT in nature and typically contains small and infrequent data (and the situation in DL is not too dissimilar to that in UL – compare the UL and DL stats in slide 1 and slide 2)
  So, optimising the system for MT traffic is equally as important as optimising this for UL
Proposal 1: Rel-18 SDT enhancements should include an objective to optimise the INACTIVE state for DL (i.e. MT) small data transmissions
Background traffic characteristics in DL – source 3GPP TR 36.822

## Slide 4: Abrupt termination and failure handling
Rel-17 SDT will not optimise the system for failure events such as cell reselection, RLC failure, beam failure etc
Whilst some failure events may be rare, others may be more frequent and more relevant for some applications
For instance for positioning applications including high mobility UEs, cell reselection during SDT cannot be ignored
Rel-17 system rightly focusses on the successful case as this is the first release for this feature and enabling the basic solution is important rather than optimising for failure events
As the system matures and more applications start using SDT, failure handling becomes more important
Proposal 2: Rel-18 SDT enhancements should include an objective to avoid data loss and/or out of order delivery of data to upper layers during failure events

## Slide 5: Minimization of network signalling
Rel-17 supports SDT without anchor relocation
However, SDT without anchor relocation still requires context fetch since RLC and other protocol layers are configured for SDT using stored UE context
Unnecessary context fetch increases network signalling overhead and may also result in SDT failure in some cases where such context cannot be retrieved
In order to avoid signalling overhead on network interfaces, it is proposed to include one objective to optimise the system for lower network signalling
Proposal 3: Rel-18 SDT enhancements should include an objective to minimise the network signalling and to avoid unnecessary context fetch

## Slide 6: Other miscellaneous enhancements
RRC-less SDT in the same cell case is useful to further reduce signalling overhead and seems to be preferred for some applications
  Signalling overhead reduction depends on security requirements and any objective for this can be conditional to meeting such security requirements from SA3
Enhancements for IDLE mode
  eLTE CIoT works for IDLE mode UEs with 5GC
  Reusing the above framework for NR can open up even more applications for SDT
  It should be noted that enabling SDT for IDLE mode UEs may require more substantial amount of time and such work can be included in scope if there is enough support
Enhancements for power consumption
  Rel-17 doesn’t define any UE specific DRX during SDT and to further improve power consumption during SDT, some enhancement to use UE specific DRX may be defined in Rel-18
  However, one alternative to the above is to use a more sparse search space for SDT and hence gains of having a DRX cycle in SDT should first be carefully analysed
Proposal 4: Rel-18 SDT enhancements for RRC-less SDT, enhancements for IDLE state and enhancements for power consumption may be considered if there is sufficient support for these.

## Slide 7: Conclusions
In this document we discussed the scope of work for Rel-18 SDT enhancements and propose the following:
Proposal 1: Rel-18 SDT enhancements should include one objective to optimise the INACTIVE state for DL (i.e. MT) small data transmissions
Proposal 2: Rel-18 SDT enhancements should include one objective to avoid data loss and/or out of order delivery of data to upper layers during failure events
Proposal 3: Rel-18 SDT enhancements should include one objective to minimise the network signalling and to avoid unnecessary context fetch
Proposal 4: Rel-18 SDT enhancements for RRC-less SDT, enhancements for IDLE state and enhancements for power consumption may be considered if there is sufficient support for these.

## Slide 8: Thanks