## Slide 1: Views on Rel-18 RAN4 non-spectrum related topics
CMCC
3GPP TSG RAN Meeting #94-e RP-213042
Electronic Meeting, December 6 - 17, 2021
Notes: RP-213042

## Slide 2: Introduction
Rel-18 RAN4 WI/SI package (except for <5MHz and DSS in this email thread) will be approved in March 2022
17 topics had been discussed in previous Rel-18 email discussion
In this contribution, we present our view on what items should be prioritized for approval

## Slide 3: Principles
Technologies to meet clear and concrete commercial applications should be prioritized
Only essential and effective enhancements/leftovers that has clear benefits and/or deployment demand should be prioritized
  Do not prioritize leftovers over new proposals by default
Timeline for Rel-18 RAN4 start.
  For new topics, start RAN4 Rel-18 in Q3
  For follow-up topics, decide in RAN#95e whether it is feasible to start Rel-18 in Q3 depending on the progress of Rel-17

## Slide 4: Topic #3: UE FR1 requirement evolution
One single WI on UE FR1 evolution in REL-18
For FWA/CPE, support 4Tx for FWA/CPE, 8Rx for FWA/CPE
For smart phone, support 6Rx and 3Tx
  Prioritize 3Tx simultaneous transmissions for two band inter-band CA with 1Tx on one uplink operating band and 2Tx on the other uplink operating band
    It should be clarified no impact on RAN4 Tx switching requirements, i.e. Tx switching period should be 0us.
    Example band combinations: CA_n3A-n41A and SUL_n41A-n80A
  Others
    Lower MSD
    UL Tx switching for UL CA with multiple TAG
      Multiple TAG is a useful scenario for CA between low and high frequency band.
      Since the issue is difficult to be addressed in Rel-17, we support to specify in Rel-18.

## Slide 5
Topic #4: UE FR2 requirement evolution
  Support UL 256QAM for FR2
Topic #5: BS RF requirement evolution
  Home base station (HBS) should be prioritized to meet operators’ commercial demand.
    Example band is n41
    Specify RF requirements for BS
    Identify the scenario and conduct co-existence study for defining the BS requirements
    Specify conformance testing requirements
    No new demodulation performance requirement is needed
  NOTE: The exact scenarios for co-existence study should be discussed in the WI as usual.
Topic #7: OTA testing enhancement
  Dynamic OTA testing method for FR2-1
  FR2 OTA testing for UEs with multi-panel reception and 4DL layer for FR2-1 if corresponding core requirements are agreed to be specified.

## Slide 6: Topic #8: ATG
  ATG has clear and urgent commercial demand from operators. The WI was proposed as a Rel-17 RAN4 WI from 2019. The WI scope is already quite stable after at least 6 rounds of email discussions tasked by RAN. Considering the commercialization, ATG should be prioritized in Rel-18.

## Slide 7: Topic #10: RRM requirements enhancement
RRM enhancements had been conducted for 2 releases. Rel-18 enhancements should focus on topics that are essential for deployment and/or have clear benefits. One single WI on RRM requirements enhancement in REL-18
General RRM requirement enhancement and leftovers
  FR1-FR1 NR DC RRM requirements: to meet operators’ potential deployment demand, it is important to specify NR DC RRM requirements
  HO with PSCell for new scenarios: to meet operators’ potential deployment demand, HO with PSCell should be extended to new scenario including SA-NEDC, SA-NR DC, LTE-ENDC.
Measurement gap related enhancement and leftover
    NeedForGap: feature is introduced in Rel-16 already, and this is a useful feature to reduce the gap overhead, the benefits are clear.
    Inter-RAT NR measurement without gaps: inter frequency without gap is already supported in Rel-17, extension to inter-RAT is very straightforward and beneficial on reducing the gap overhead.

## Slide 8: Topic #11: Demodulation requirement evolution
There are many proposals on demodulation requirements enhancements. In order to get a proper scoping, we consider following objectives as high priority:
  Soft IC to cancel inter-stream interference in SU-MIMO scenario
  Inter-cell CSI-RS/SSB interference mitigation (IM)
  Advanced receiver to cancel inter-user interference for MU-MIMO

## Slide 9: Topic #13: FR2 HST enhancement
Support to enhance FR2 HST requirements in general
  500km/h support for FR2 HST
  intra-band carrier aggregation scenario, e.g. n258
  Maximum 2 active panels supporting the multi-panel simultaneous reception.
  Mixed near-to-track scenario (depending on the conclusion in Rel-17)
  New uplink timing adjustment mechanism for FR2 HST scenario with large propagation delays from different TRPs to UE (depending on the conclusion in Rel-17)