## Slide 1: Views on workload of Rel-18 SDT
RP-213230
3GPP TSG RAN #94-e 6-17 December 2021 Online
Source: Ericsson Agenda Item: 8A.2 Document for: Decision

## Slide 2: Background
The preparatory RAN email discussion on Rel-18 SDT is summarized in RP-212686 and a draft WID is available in RP-212726.
  The WID contains the following objectives:
  2-6 TUs are proposed for RAN2 in the moderator’s summary.
Specify the support for paging-triggered SDT (MT-SDT) [RAN2, RAN3]
MT-SDT triggering mechanism for UEs in RRC_INACTIVE, supporting RA-SDT and CG-SDT as the UL response;
MT-SDT procedure for initial DL data reception and subsequent UL/DL data transmissions in RRC_INACTIVE.

## Slide 3: Rel-18 MT-SDT workplan
The current, open-ended, draft WID formulation includes all types of solutions (see e.g. discussion for MT-EDT in R2-1910420):
  DL data in paging DCI
  RNTI in paging message to schedule the DL data
  DL data in paging message
  DL data in Msg2
  DL data in Msg4
Even after down-selection to one solution, many details must be agreed for that solution
  (signaling, triggering, RAN3 interworking, etc.)
Unclear what kind of solution "MT-SDT supporting CG-SDT as the UL response" would be (likely taking several TUs on its own to align).
Observation: The workload of the WID is substantial.
Observation: 2-6 RAN2 TUs in total has been proposed for Rel-18 SDT.
Observation: It is not realistic to agree on the best MT-SDT solution and to specify it in only 6 TUs.
Proposal: MT-EDT is used as baseline for MT-SDT (i.e. ‘Data in Msg4’)
Proposal: ‘MT-SDT supporting CG-SDT as the UL response’ is down-prioritized.

## Slide 4: WID Text Proposal
Based on the previous proposals we provide the following text proposal:
Specify the support for paging-triggered SDT (MT-SDT) [RAN2, RAN3]
MT-SDT triggering mechanism for UEs in RRC_INACTIVE, supporting RA-SDT and CG-SDT as the UL response;
        CG-SDT as UL response is treated with lower priority.
MT-SDT procedure for initial DL data reception and subsequent UL/DL data transmissions in RRC_INACTIVE.
Note: ‘Data in Msg4’ is considered as baseline.

## Slide 5
https://www.ericsson.com/en/5g