## Slide 1: Moderator’s summary for discussion [94e-17-R18-NTN-NR]
RAN Vice-Chair (AT&T)
3GPP TSG-RAN Meeting #94-e
Electronic Meeting, December 6-17, 2021
Agenda Item: 8A.2
RP-213542

## Slide 2: Moderator Proposed WF on Remaining Issues
Objective 2: NR-NTN deployment in above 10 GHz bands
The following assumptions are taken a baseline for this work:
  GSOGEO and NGSO (e.g. LEO, MEO, HEO) based satellite access to be considered
    NGSO is not applicable for ESIM scenarios in Ka band from ITU perspective
  Targeted UE types: fixed and mobile VSAT. VSAT UE characteristics from TR38.821 to be considered in priority but additional NTN UE classes may be considered if justified
    Regarding mobile VSAT, three types of terminal and scenario exist; airborne, maritime and land based ESIM. Which type(s) to be specified depends on the outcome of the regulation analysis and co-existence study.
  FDD mode is assumed for satellite operation above 10 GHz, while TDD mode is assumed for terrestrial operation in FR2
  The harmonized Ka band frequency range (17.7-20.2 and 27.5-30.0) as common across all regions will serve as reference
The following covers the objectives for NR-NTN deployment in above 10 GHz bands. In accordance with the WF in RP-211596, this work would start after March 2022 once FR1 NTN coexistence study is stable enough.

## Slide 3: Moderator Proposed WF on Remaining Issues
Objective 2: NR-NTN deployment in above 10 GHz bands (continued)
Study and identify NTN example bands: Analysis of regulations and adjacent channel co-existence scenarios. The example band shall be identified early in the WI. Additional bands can be introduced in a release-independent manner. [RAN4]
  Consider at least a portion of the Ka band as the example band, according to ITU allocation; identify which parts of the Ka band are suitable as 3GPP bands taking into account deployment type (e.g. VSAT, ESIM) [RAN4]
  Study implications of FDD operation in FR2 and derive requirements for the identified part(s) of the Ka example band appropriately. Satellite bands introduced in 3GPP for NTN for FDD shall not impact the existing 3GPP TDD specifications for terrestrial bands (see note 3 of the approved way forward RP-211596 in RAN#92-e). [RAN4]
  Relevant coexistence scenarios and analysis to be considered in RAN4, if and where applicable, to ensure that satellite bands introduced in 3GPP for NTN shall neither not impact the existing specifications of nor and shall not cause degradation (in the sense of RAN4 co-existence studies) to present and future networks in 3GPP specified terrestrial bands. [RAN4]
  For this, RAN4 process as agreed for NTN in FR1 shall be leveraged for coexistence analysis in above 10 GHz bands [RAN4].
  Definition of NTN band(s) above 10 GHz does not change the current FR1/FR2 definition, nor automatically apply to future terrestrial bands defined in this frequency region; (see proposal 2 of the approved way forward RP-211596 in RAN#92-e) [RAN4]
Specify Rx/Tx requirements for satellite BS access node and different VSAT UE class (not only 60 cm aperture) as appropriate for the identified example band [RAN4]
Identify values for physical layer parameters chosen from the existing FR1 and FR2 sets. The following set of parameters to specify, but not necessarily limited to, are listed as follows [RAN4]:
  time relationship related enhancement (e.g. K_offset)
  subcarrier spacing for different UL/DL signals/channels
  PRACH configuration index for FDD above 10 GHz. Introduction of new values for physical layer parameters (e.g., SCS for a given signal/channel) on top of already defined values is not in scope. [RAN1,RAN4]

## Slide 4: Moderator Proposed WF on Remaining Issues
Objective 4: NTN-TN and NTN-NTN mobility and service continuity enhancements
This work considers existing methods from NR TN as baseline for NTN-TN mobility as well as Rel-17 WI outcome and the further mobility enhancements objectives based on confirmation of feasibility and impact are listed below.
  Address handover interruption and handover signalling overhead [RAN2,RAN1]
  Specify NTN-TN and NTN-NTN measurement/mobility and service continuity enhancements [RAN2,RAN4]
  [Consider RLF reduction issue for different delay and/or network topology between the different access types/points/nodes if justified] [RAN2, RAN1]
  [Address RACH congestion and/or RACH-less HO as second priority] [RAN2,RAN1]