## Slide 1
3GPP TSG RAN Meeting #95-e RP-220598
Electronic Meeting, March 17-23, 2022
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.3.2.3
Discussion on RRM requirements for Rel-17 MUSIM features in Rel-18

## Slide 2: Motivation for RRM requirements for MUSIM
In RP-213622 [1] in RAN#94 meeting
  Proposal 2: Postpone all the discussion on RRM requirements related to MUSIM gaps to Rel-18. Whether this aspect will be covered under the R18 MUSIM WI or another RAN4 WI can be discussed as part of the Rel-18 RAN4 package.
    Conclusion: proposals 1/2/3/4 are endorsed
In Rel-18 RAN4 package discussion pre RAN#95 meeting, as summarized in RP-220021 [2]
  Proposal #5: Further discuss inclusion of objectives on RRM requirements for Rel-17 MUSIM features in the scope of Rel-18 MUSIM WI in RAN #95e.
MUSIM features and new gap patterns were introduced in Rel-17. However, corresponding RRM requirements are not specified due to lack of RAN4 TUs for Rel-17 MUSIM WI.
Without corresponding RRM requirements, the introduced MUSIM features and new gap patterns cannot be implemented in practical NW due to unpredictable impact to NW A.
  Proposal 1: Specifying RRM requirements for Rel-17 MUSIM features and new gaps in Rel-18 MUSIM WI.

## Slide 3: Objectives of RRM requirements for MUSIM
Objectives
  RRM requirement for MUSIM Enhancements in network A [RAN4, RAN2]
    Specify solutions for collision handling between MUSIM gap and R16 legacy measurement gap/MUSIM gap/SMTC (e.g., the priority rules defined in R17) [RAN4, RAN2]
    Identify potential impacts on L1 measurements (including RLM/BFD) and L3 measurements and specify corresponding requirements, if necessary, when MUSIM gap(s) are in the presence, for the following scenarios [RAN4]
      Only MUSIM gap(s) are in the presence
      MUSIM gap(s) and legacy measurement gap are in the presence
    Specify scheduling restriction for MUSIM gaps [RAN4]
    Specify applicability of requirements for MUSIM, if necessary [RAN4]
  Proposal 2: Include the objectives above in Rel-18 MUSIM WI.

## Slide 4: References
  [1] RP-213622 Moderator's summary of discussion [94e-45-R17-MUSIM-WID] RAN2 Vice-Chair (ZTE)
  [2] RP-220021 Moderator's summary for discussion [RAN95e-RAN4-R18Prep-03] RRM Enhancements RAN4 vice-chair (Intel)