## Slide 1: TX switching and multiple TAG for 2 bands
Ericsson
RP-220649

## Slide 2: TAG switching and multiple TAG
The current RAN4 requirements for TX switching explicitly restrict operation to deployments where both bands are in a single TAG
  Practically speaking, this means that non-co-location of the BS on the two bands is not supported. As an example, if one band is low band FDD and the second band is TDD, then in some scenarios the FDD and TDD BS may not be co-located.
    Example band combinations CA_n2-n77 and CA_n3-n77 (DL interruptions not allowed for CA_n3-n77 and would not depend on multi-TAG support)
The restriction is arbitrary
  If multiple TAG would be allowed, then the UE requirements and behavior would be exactly the same as single TAG (UE not expected to transmit during the switching period)
  There is no impact on RAN1 procedures or RAN2 signaling for multiple TAG; they can operate in the same way as they do for non-switching CA
  There is no impact to downlink interruptions
  The network will need to adapt the scheduling to take into account a 1 slot interrupt if there are different TAG. This has no impact on UE requirements.
  Further explanation in R4-2204064
To remove the restriction, all that is needed is a simple RAN4 change (see annex 1)
  It is beneficial for test coverage, but not essential to add a specification of the timing diagram for multiple TAG

## Slide 3: TAG switching and multiple TAG
For the Rel-18 WI on multi-carrier enhancements, it is agreed to introduce support for CA and multiple TAG for 3 and 4 bands. The situation for 2 bands is not explicitly mentioned (see annex 3)
There are two ways to solve the issue for 2 bands:
  Agree a CR for Rel-17 as part of TEI17
  Clarify the scope of the Rel-18 WI to include 2 bands switching
TX switching defined for
  one carrier with 1TX and another with 2TX (Rel-16)
  one carrier with 2TX and another with 2TX (Rel-17)
these cases can be supported for UL CA by UEs supporting the optional supportedNumberTAG capability (multiple-TAG) specified in Rel-15

## Slide 4: Proposal
Since
  the switching with two bands has already existed in the specifications since release 16
  the intention with the Rel-18 is actually to extend functionality with support for 3-4 bands and
  the Rel-17 CR is very simple with no impact to any other working group,
  there is not any motivation to keep the two-band deployment restriction in the current specifications until Rel-18 timeframe.
Proposal: RAN tasks RAN4 to agree extension of switching to multiple TAG in Rel-17 for UL CA
  The basic change in annex 1 should be recommended to be adopted
  RAN4 can decide whether to add additional timing diagrams for multiple TAG for information or not in May

## Slide 5: Annex 1: Minimum required change in Rel-17 specification
To implement the change, as a minimum the text highlighted in yellow should be added and the text in blue removed.
An alternative could be to add an additional timing diagram for multiple TAG as proposed in R4-2204605 for increased test coverage (different DL receive timing on the two carriers)

## Slide 6: Annex 2: timing diagrams for increased test coverage with different DL timing: principle
The UE is not expected to transmit on any of the two carriers preceding time T0 (start of uplink transmission) just as for the single-TAG case; the gNB scheduler (or test system) would ensure that there are no transmissions during the switching period (complete timing diagrams in R4-2204605)
Same TA on the carriers
  including single-TAG
Different TA on the carriers (carrier 1 lagging in DL timing)
  UEs supporting the optional supportedNumberTAG

## Slide 7: Annex 3: Objectives of Rel-18 Multicarrier enhancements WID
Study and if necessary specify following enhancements for multi-carrier UL operation [RAN1, RAN2, RAN4]
  UL Tx switching schemes across up to 3 or 4 bands with restriction of up to 2 Tx simultaneous transmission for FR1 UEs, including mechanisms to enable more configured UL bands than its simultaneous transmission capability and to support dynamic Tx carrier switching across the configured bands for both single TAG and multiple TAGs configurations (RAN1, RAN4)
The objective is clear for 3-4 bands, but not entirely clear whether removal of the multiple TAG restriction for 2 bands is included.
  Anyhow for two bands the change is a minor CR