## Slide 1: Moderator's summary for discussion [95e-12-RAN4-R18-OTATest]
Moderator (Qualcomm Incorporated)
3GPP TSG RAN Meeting #95-e
Electronic Meeting, March 17 - 23, 2022
Agenda item: 9.1.4
RP-220872

## Slide 2: Introduction
This email thread is to discuss the detailed scope for RAN4 Rel-18 OTA testing proposals. The following two topics are covered:
  Finalize the SID on Study on NR FR2 OTA testing enhancements
  Discuss how to handle the other OTA topics

## Slide 3: Topic#1: SID on Study on NR FR2 OTA testing enhancements
Justification
  In RAN1 Rel-17 WI on further enhancements on MIMO for NR (Acronym: NR_FeMIMO), the objective is to extend the specification to support several aspects on NR MIMO including multi-panel UEs which also has RAN4 impact. With RAN4 considering an objective to define requirements for UEs with multi-panel reception and up to 4DL layers for FR2-1, the FR2 test methodologies for RF, RRM, and demodulation need to be enhanced to support the verification of these new requirements, together with a preliminary assessment of the related uncertainties.
Detailed objective:
  The objectives for FR2-1 OTA testing for UEs with multi-panel reception and 4DL layer are as follows.
    Define a test methodology for RF/RRM/Demodulation requirements testing for devices that can receive/transmit simultaneously from multiple Angle of Arrival (AoA)
      The multiple AoA test setup should enable testing of up to 2 DL Layers with dual polarization for each angle
      For RRM, the target should be to allow testing of 4 AoAs with 2 simultaneously active AoAs
        Note: The angular distance between tested AoAs should be minimized while maintaining good isolation between test equipment (TE) probes
    Define a test methodology for up to 4 DL MIMO layer demodulation testing
  Smartphone form factor should be the first priority, other UE types should also be discussed as 2nd priority
  Develop the related preliminary uncertainty assessments for the test methodologies
  FR2 test methods defined in TR 38.810 and TR 38.884 should be used as the baseline.
  The tests shall take the test system reuse, test system complexity and test time into account to keep the whole test costs within a reasonable level.

## Slide 4: Topic#2 : How to handle other OTA topics
WF on how to handle other OTA topics
    The other OTA topics including Dynamic OTA testing method for FR2-1, FR2 testing framework for FWA devices (PC1/PC5), Rel-17 OTA leftovers and follow-up work for ongoing Rel-17 SISO OTA and MIMO OTA will be postponed and revisited in future RAN plenary meetings designated as the checking point by RAN chair.
  The above WF is agreeable. The moderator’s recommendation is to capture the above WF into the meeting minutes.