## Slide 1: RAN level guidance required for sensing
3GPP TSG RAN#97-e
Electronic Meeting, 12th – 16th September, 2022
RP-221942
Xiaomi

## Slide 2: Difficulties found in SA1 sensing SI
Observation 1: The use cases/requirements applicable for different sensing solutions are different. However it is difficult for SA1 to evaluate which sensing solution is feasible for which use case. Some coordination between RAN and SA1 is needed.
The following sensing options have been discussed in SA1:
Sensing option 1: UE acting as both transmitter and receiver
Sensing option 2: gNB acting as both transmitter and receiver
Sensing option 3: UE as transmitter, gNB as receiver
Sensing option 4: UE as transmitter, other UE as receiver
Sensing option 5: gNB as transmitter, UE as receiver
Sensing option 6: gNB as transmitter, other gNB as receiver

## Slide 3: Difficulties found for channel model used for sensing evaluation
Observation 2: It is difficult to use the channel model(s) given in 38.901 to evaluate the sensing feasibility/performance.
We found the following difficulties while reusing the channel model(s) (including TDL (Tapped Delay Line), CDL (Clustered Delay Line), fast fading model and so on) given in 38.901:
It is difficult to define the interference caused by the environment (e.g. reflection interference caused by environment object), especially for RX/TX collocated sensing.
  The LOS channel of reflection from the environment object causes strong interference to the receiver.
  It is difficult to define the location of the environment object, which is critical to determine the environment interference to the receiver.
    It is difficult to use TDL to locate the environment object, as TDL has no angle information.
    It is difficult to use CDL/fast fading model to locate the environment object, as the angle from CDL/fast fading model is based on statistics (which could be based on one or more reflections for one cluster).
It is difficult to define the sensing target/object, especially when the target is not a UE.
The RCS(s) (Radar cross-section) for many substances and frequencies are missing.

## Slide 4: Difficulties found for sensing scenarios used for sensing evaluation
NR/LTE
  Sensing under the framework of NR or LTE or both
Frequency range
  Sensing operated at FR1 or FR2 or higher
Waveform
  Sensing using OFDM or others
Observation 3: It is difficult to evaluate the sensing feasibility/performance before determining RAT, frequency range, and waveform.

## Slide 5: Conclusion
Observation 1: The use cases/requirements applicable for different sensing solutions are different. However it is difficult for SA1 to evaluate which sensing solution is feasible for which use case. Some coordination between RAN and SA1 is needed.
Observation 2: It is difficult to use the channel model(s) given in 38.901 to evaluate the sensing feasibility/performance.
Observation 3: It is difficult to evaluate the sensing feasibility/performance before determining RAT, frequency range, and waveform.
Proposal: RAN is kindly requested to evaluate the feasibility of the candidate sensing solutions as discussed in SA1, so as to facilitate the study of the sensing techniques in SA1. Some RAN-level guidance (e.g. channel model, RAT, frequency range, and waveform) is required for such evaluation.

## Slide 6: Thanks