## Slide 1: Motivation of R18 TRP TRS enhancement
OPPO, CAICT
3GPP TSG-RAN Meeting #97-e
Electronic Meeting, 12th – 16th Sep., 2022
RP-222071

## Slide 2: Background
R17 UE TRP/TRS WI is targeted to be closed in RAN#97e though not all of the objectives included in the WID are complete
  High priority objectives have been well managed during process of this WI
    Core and performance part of NR SA and EN-DC have complete including test methodology and requirements for n41 and n78 bands
  Some valuable but 2nd priority objectives were studied but not finished due to time limitation
    Multi antenna transmission like TxD and one layer two port UL MIMO, transmit antenna switching, etc.
    Reverberation chamber which as an cost effective test method was not included in Rel-17 spec
  For the lefts of R17 and also some new important features can be further considered as part of new R18 WI after the completion of R17 WI.

## Slide 3: Reverberation chamber
  Reverberation chamber is a fast and effective test method defined in 3GPP 3G/4G OTA specifications and has shown good alignment with anechoic chamber base method.
  In R17 NR TRP/TRS discussion, Reverberation chamber was preliminarily analysed but not included in the NR specification due to time restriction. It should be considered as one of the most important items in R18 to well utilize existing test systems in industry.

## Slide 4: RedCap UE and CA enhancement
  Redcap as one of the important feature can be applied in many compact devices, like wearable devices.
    OTA test methods to verify its antenna performance currently are not supported. Test configurations, suitable test phantoms need to be studied in NR to serve the upcoming Redcap UEs in R18 timeframe.
  Commercial devices with CA are launched into the market. The new Rel-18 WI should cover the test method for UE with CA.
    Test procedures and test system implementations need to be defined for inter-band CA scenario.

## Slide 5: TxD and UL MIMO OTA
  Multi antenna transmission is one of the important feature in boosting UL coverage and throughputs. And current UEs have widely support these features.
  R17 TRP only consider UE with 1Tx in the TRP test, though TxD was one of the objective in the WID.
    TxD was put on 2nd priority due to core RF requirements were discussed in parallel in R17. Now TxD feature was specified in the RF specification, the OTA test discussion can be resumed in R18.
  Similarly, single layer with 2 port UL MIMO which was considered as one of the basic transmission in the cell edge scenario during R17 TRP/TRS discussion can also be further studied in R18.

## Slide 6: Conclusion
  Following items can be further studied in R18 as the R17 leftovers or new demands from industry:
  Introduce reverberation chamber based method in NR
  Specify test methods for RedCap UEs
  Study TRP tests for UE with multi-antenna, e.g. TxD and/or UL MIMO
  Study OTA tests for inter-band CA
  New UE types like tablet or new NR bands can be considered based on operator requests