## Slide 1
Motivation for RAN-level SI for Extended-IoT in R18
CMCC
3GPP TSG RAN Meeting #97-e RP-222126
Electronic Meeting, September 12-16, 2022
Notes: 全场景物联网

## Slide 2
SA1
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Rel-18
R18 L1 Start
R18 L1
R18 L2/3
ASN.1
Rel-19
Q1
Q2
Q3
Q4
R18 L2/3
ASN.1
R19 L1
R19 L1 Start
SA1 SI: Study on Ambient power-enabled Internet of Things
Approved at SA1#97
e-IoT RAN-level SI
To be approved at RAN#97
Start RAN SI at RAN#98
R19 e-IoT SA2 SI
e-IoT SA2 WI
RAN
SA2
e-IoT RAN WG SI
RAN WG
To be complete at SA1#100
e-IoT RAN WG WI
SA1 will complete the SI at Nov 2022.
RAN level SI is necessary to consolidate the SA1 output into a set of RAN design targets for the follow-up RAN WGs to work on in Rel-19
RAN level SI is proposed to be approved at RAN #97, then start discussion at RAN#98 at Dec 2022.
Start WG SI and complete normative work within Rel-19, in order to meet the opportunity of market.
Proposed Work plan for RAN level SI for e-IoT
2022
2023
2024
2025

## Slide 3
Motivation
Motivation
Wide-area and low-cost inventory, positioning and environmental perception are persistent demands for the industry.
Limitations of existing RFID technology to fulfill the requirement of industry:
  Bad coverage due to short transmission distance, 8~10m @36dBm
    Low reference sensitivity and High interference for both intra- and inter-reader
  High cost due to deployment of massive RFID readers, >10000￥/reader
  Not supporting positioning
Both operator and vertical costumers expects to deploy one network to fulfill all these 4 requirements, including communication, positioning, perception and PLC control
e-IoT device type
This study targets for an IoT segment below the existing 3GPP LPWA IoT technologies, i.e., lower than NB-IoT, eMTC, RedCap, etc. Not aim to replace existing 3GPP LPWA technologies.
In terms of energy storage, the study assumes to support two kind of e-IoT devices
  Pure batteryless devices with no energy storage capability at all, and completely dependent on the availability of the ambient source of energy it is harvesting
  Devices with energy storage capability (e.g. up to that available from ambient sources via energy harvesting) that do not need to be replaced or recharged manually, and which can manage short periods of ambient energy unavailability.

## Slide 4
Use cases
Manufacturing | Electricity | Medical | Husbandry | Logistics
Inventory check Product positioning Disaster prevention | Disaster prevention Device monitoring | Medicine monitoring, Health monitoring e.g., heart, SpO2 | Livestock inventor, monitor and positioning | Product tracking Product positioning | Smart home, industry control
e-IoT has a wide range of use cases for manufacturing, electricity, medical, husbandry and logistics.
Activator
Notes: 满足这些use case。

## Slide 5
Requirements for the use cases
Target Industry | Target Use Case | User Requirement | Technical Requirement | e-IoT Tag capability
Manufacturing | Indoor inventory | Inventory Positioning Tracking Perception | Positioning: 2m (Horizontal & Vertical) @90% Coverage: 20m indoor 200m outdoor Cost: 0.1￥(~0.02$) Sensor: temperature, humidity, gas, light and smoke | Passive/Semi-passive: Identification, inventory, sensor, RF enhancement
 | Outdoor inventory and tracking |  | Temperature, gas sensoring, | Identification, inventory and sensor
Electricity | Transformer station, power transmission monitor | Perception | Coverage: ≥ 100m Sensor: temperature, acceleration and water level | Semi-passive: Identification and sensor
Medical | Medicine monitor, Health monitor | Positioning Perception | Coverage: ≥ 20m Sensor: temperature, heartrate, SpO2 and acceleration | Passive/Semi-passive: Identification and sensor
Animal husbandry | Livestock monitoring | Inventory Positioning Perception | Positioning: ≤ 2m@90% Coverage: ≥ 20m@NLoS indoor Sensor: temperature, acceleration | Passive/Semi-passive: Identification, inventory, sensor
Logistics | Cargo tracking | Inventory Positioning Tracking | Positioning: ≤ 2m@90% Coverage: ≥ 200m Cost: 0.1￥(~0.02$) | Passive: Identification, inventory, RF enhancement
Activator | Smart home, industry control | ON/OFF control, control of procedures | To be studied | Passive
For each use case, passive and semi-passive e-IoT is expected to be customized to meet the various need of vertical industries.
Notes: 有传感需求的，用半无源更合适些。没有传感需求的，无源更合适些，成本更低

## Slide 6
RAN design targets
 | RFID | 5G e-IoT
Coverage | ~ 10m | Indoor, NLOS: ≥ 20m Outdoor, NLOS: ≥ 200m
Positioning | Not support | Support
Tag Power Consumption | Passive: ~ 1μW | Similar as RFID
 | Semi-Passive: ~ 100μW | 
Cost | Passive: ~ 0.03 USD | Similar as RFID
 | Semi-Passive: ~ 0.3 USD | 
Technical requirements for 5G e-IoT | 
Reader | Massive connections Positioning: 2m (Horizontal & Vertical) @90% Interference mitigation, for intra-/inter-reader, and inter-system
Tag | Access collision avoidance enhancement Reference sensitivity enhancement Support simplified 5G protocol stack and signaling Sensor capability for semi-passive tag
To meet the requirement of use cases, e-IoT is expected to achieve higher performance over RFID, especially on coverage, cost, positioning and perception capability
Use cases and performance requirements in SA1 TR 22.840 are taken as starting point.
RAN design targets should be studied.
For the use cases, RAN level SI should study:
  Gap between existing RFID and e-IoT requirement
  Compare the different deployments options for each use case
Assess the feasibility and identify assumptions on required functionality to be supported
Notes: 基于use case的requirement，我们期望可以进一步提升性能来满足垂直行业需求。需要确保Tag low cost and power consumption.

## Slide 7
E2E Architecture
RAN design for e-IoT should consider both E2E architecture options, i.e., connection to servers through proxy or simplified CN.
Filtering &Collection
Middleware
Reader Role
Tag Role
Application Level Events (ALE)
ALE Client
Low Layer Reader Protocol Interface (LLRP)
Reader Role
Reader
Tag Role
Tag
Air protocol Interface
RFID architecture
eIoT architecture
Key functions:
Tracking
Paging
Connect to RAN and multi-servers
Notes: The architecture of passive IoT can be a light-weight one without core network architect or a heavy-duty one with core network. RAN is compatible for both.
对用户最友好。右面与现网网络结构最吻合，但不一定适合现在业务的便利性、终端成本、功耗。明确说出我们的倾向

## Slide 8
RAN architecture
1-1：Direct connection
1-2：Direct connection with energy supplied
Energy supply node
Uu interface
DL inventory Trigger
Energy supply
UL backscatter
2-1
2-2
2-4
2-3
2：Connect through relay node
RAN SI is expected to study and compare different RAN topologies for each use case.
RAN SI is expected to provide guidance to the follow-up RAN WG SI.
E-IoT should provide better coverage than RFID.
Notes: 图中反应对系统设计的影响，基站增加适配层，IP出去

## Slide 9
This study targets at a new 3GPP IoT technology, suitable for cellular deployment, which relies on ultra-low complexity devices with ultra-low power consumption for the very-low end IoT applications. In terms of energy storage, the study will consider the following:
  Pure batteryless devices with no energy storage capability at all, and completely dependent on the availability of the ambient source of energy it is harvesting
  Devices with energy storage capability (e.g. up to that available from ambient sources via energy harvesting) that do not need to be replaced or recharged manually, and which can manage short periods of ambient energy unavailability.
Identify the suitable deployment scenarios and their characteristics, at least for the use cases/services agreed in SA1’s “Study on Ambient power-enabled internet of Things”, comprising among at least the following aspects:
  Indoor and/or outdoor environments
  Base station characteristics, e.g. macro, micro, pico cell-based deployment
  RAN connectivity topologies, including which node(s) serve as reader or activator, e.g., gNB, UE, relay.
  TDD/FDD, and frequency bands in licensed or unlicensed spectrum
  Coexistence with UEs in frequency bands for existing 3GPP technologies
  Mobile originated and/or mobile terminated traffic assumption
Formulate a set of RAN design targets based on the requirements from the relevant SA1’s agreed use cases, at least including
  Power consumption
  Complexity
  Coverage
  Data rate
  Positioning accuracy
Compare and assess the feasibility of meeting the design targets for each agreed SA1 use case on the basis of the deployment scenario(s) appropriate to it, and identify assumptions on required functionality to be supported.
NOTE: This study shall target for an IoT segment well below the existing 3GPP IoT technologies, e.g. NB-IoT, eMTC, RedCap, etc. The study shall not aim to replace existing 3GPP LPWA technologies.
R18 RAN SI objectives

## Slide 10
Thanks