## Slide 1: Views on New Rel-18 WI: Enhanced support of reduced capability NR devices
Ericsson
3GPP TSG RAN meeting #97e
Electronic Meeting
September 12 - 16, 2022 Agenda Item: 9.2.10
RP-222209

## Slide 2: Introduction
A draft WID on RedCap enhancements was provided in RP-212705 in RAN#94e with following proposed objectives:
    Enhanced eDRX in RRC_INACTIVE > 10.24s
    Further reduced UE cost/complexity
    Support for lower UE power class
RAN1 has carried out a study item on further UE complexity reduction for UEs targeting 10 Mbps peak rate
    The conclusions and recommendations from RAN1 are provided in clause 9 in TR 38.865 in RP-222207.
An updated draft WID is provided in RP-222208, but it contains several discussion/decision points for the RAN plenary.
    Some down-selection between the potential UE complexity reduction techniques needs to be done by the RAN plenary.
This contribution presents our views on the open issues in the conclusions and recommendations from RAN1.

## Slide 3: Background: Rel-17 RedCap
Rel-17 RedCap achieves significant UE complexity reduction compared to Rel-15 reference UEs.
    65%-70% cost reduction according to the methodology adopted in TR 38.875
        Maximum UE bandwidth 20 MHz in FR1 and 100 MHz in FR2
        Minimum number of Rx branches and DL MIMO layers is 1
        Support of 256QAM in DL is optional in FR1
        Support of HD-FDD operation type A
Additional cost saving by further UE complexity reduction in Rel-18 is expected to be modest.

## Slide 4: Background: Study of further UE bandwidth reduction
Three options for further bandwidth reduction (from 20 MHz to 5 MHz) were studied:
    Option BW1: Both RF and BB bandwidths are 5 MHz for UL and DL
    Option BW2: 5 MHz BB bandwidth for all signals and channels with 20 MHz RF bandwidth for UL and DL
    Option BW3: 5 MHz BB bandwidth only for PDSCH (for both unicast and broadcast) and PUSCH with 20 MHz RF bandwidth for UL and DL.
        The other physical channels and signals are still allowed to use a BWP up to 20 MHz maximum UE RF+BB bandwidth.
Average cost reduction compared to Rel-17 baselines (based on TR 38.865):
Cost saving relative to Rel-17 RedCap (20 MHz BW) | FD-FDD (1 Rx) | TDD (1 Rx) | HD-FDD (1 Rx)
Option BW1 | 11.9% | 11.3% | 14.1%
Option BW2 | 9.2% | 8.1% | 11.9%
Option BW3 | 8.0% | 7.7% | 8.9%

## Slide 5: Background: Study of further UE peak rate reduction
Three options for further peak rate reduction were studied:
    Option PR1: Relaxation of the constraint from ≥4 to ≥1
    Option PR2: Restriction of maximum TBS for PDSCH and PUSCH to 10000/5000 bits for 15/30 kHz SCS
    Option PR3: Restriction of maximum number of PRBs for PDSCH and PUSCH to 25/11 PRBs for 15/30 kHz SCS
Average cost reduction compared to Rel-17 baselines (based on TR 38.865):
Cost saving relative to Rel-17 RedCap (20 MHz BW) | FD-FDD (1 Rx) | TDD (1 Rx) | HD-FDD (1 Rx)
Option PR1 | 4.1% | 4.0% | 5.0%
Option PR2 | 4.3% | 4.2% | 5.1%
Option PR3 | 7.1% | 6.7% | 8.1%

## Slide 6: Background: Study of relaxed UE processing timeline
Two options for , relaxed UE processing timeline were studied:
    Option PT1: Relaxation of UE processing time for PDSCH/PUSCH in terms of N1 and N2 compared to those of UE processing time capability 1
        The relaxation factor for N1 and N2 is assumed to be 2 in TR 38.865
    Option PT2: Relaxation of UE processing time for CSI in terms of Z and Z’
        The relaxation factor for Z and Z’ is assumed to be 2 in TR 38.865
Average cost reduction for PT1 in combination with BWx and PRx options (based on TR 38.865):
Cost saving relative to Rel-17 RedCap (20 MHz BW) | FD-FDD (1 Rx) | TDD (1 Rx) | HD-FDD (1 Rx)
Option BW1+PT1 | 12.4% | 11.6% | 14.3%
Option BW3+PT1 | 8.7% | 7.8% | 10.2%
Option PR1+PT1 | 5.4% | 4.9% | 6.6%
Option PR3+PT1 | 7.7% | 7.2% | 9.3%

## Slide 7: Background: Study of relaxed UE processing timeline, cont.
Average cost reduction for PT1 and PT2 in combination with BWx and PRx options (based on TR 38.865):
Cost saving relative to Rel-17 RedCap (20 MHz BW) | FD-FDD (1 Rx) | TDD (1 Rx) | HD-FDD (1 Rx)
Option BW1+PT1+PT2 | 14.8% | 14.7% | 17.5%
Option BW2+PT1+PT2 | 11.5% | 10.9% | 15.3%
Option BW3+PT1+PT2 | 11.6% | 11.5% | 12.9%
Option PR1+PT1+PT2 | 7.9% | 8.7% | 9.3%
Option PR2+PT1+PT2 | 7.2% | 6.2% | 9.5%
Option PR3+PT1+PT2 | 10.2% | 10.7% | 12.1%

## Slide 8: Conclusions and recommendations from RAN1 (TR 38.865)
Based on its study, RAN1 has the following conclusions and recommendations in clause 9 in TR 38.865 in RP-222207:
    Most companies in RAN1 recommend that option BW3 or PR3 is selected.
    Some companies instead want to consider option PR1 or BW1.
    Finally, some companies also want to consider options PT1 and/or PT2.
Furthermore, RAN1 recommends that option PR1 can be considered as a potential add-on to the other techniques.
    Whether to adopt this potential add-on can be decided during WI phase.
On the following slides, we present our views on the open issues in the conclusions and recommendations from RAN1.

## Slide 9: Views on further reduced UE bandwidth or peak rate (Options BW1/BW3/PR1/PR3)
We agree with the majority view in RAN1 that one of options BW3 or PR3 may achieve a good balance between complexity reduction and expected impacts.
    Option BW3 has slightly higher expected complexity reduction but also somewhat higher expected impacts than option PR3.
    Both BW3 and PR3 (as well as the other PR options) avoid major specification work, which is important given the expected small TU allocation in WI phase.
Option BW1 should be avoided due to significant network impacts compared to the expected complexity reduction.
    The difference in cost saving between different BW reduction options is small (in the range 3.6% to 5.2%).
    Option BW1 results in significant impacts on link performance, coexistence, network deployment flexibility, and specification:
        Significant link performance degradation for PBCH and PDCCH
        Significant coexistence impacts in terms of support of SSB/CORESET#0 configurations (especially 30 kHz SCS)
        Limitations of RACH configurations and PRACH sharing procedure
        Potential additional SSB overhead

## Slide 10: Views on relaxed UE processing timeline (Options PT1/PT2)
Additional cost saving for PT1+PT2 are:
    2.9 to 4.0% on top of BWx options
    3.2 to 4.7% on top of PRx options
The additional cost saving for PT1 and PT2 incurs significant network impacts (e.g., scheduling flexibility and complexity).
    PT1 could also cause coexistence issues with legacy UEs (if early identification of Rel-18 RedCap UEs in Msg1 is not available).
    PT1 and PT2 will also have latency and specification impacts.
Options PT1 and PT2 should be avoided due to small cost saving but significant network impacts.

## Slide 11: Summary
Regarding the studied techniques for further RedCap UE complexity reduction in Rel-18,
    Option BW3 or PR3 achieves a good balance between complexity reduction and expected impacts.
    Options BW1, PT1 and PT2 should be avoided due to their significant network impacts.
    Whether to adopt option PR1 as a potential add-on can be decided during WI phase.
For the other objectives in the draft WID discussed during RAN#94e (RP-212705),
    Support for Enhanced eDRX in RRC_INACTIVE > 10.24s should be specified in Rel-18.
    Whether to introduce support for lower UE power classes needs further RAN plenary discussion.