## Slide 1
Title: On the work scope of Rel-18 NR sidelink evolution
Agenda item: 9.3.1.5
Source: Samsung
Document for: Decision
3GPP TSG RAN Meeting #97-e
Electronic Meeting, September 12 – 16, 2022
RP-222233

## Slide 2: Background
According to the WID, RAN1 has studied Objectives 2 and 4, and RAN needs to check whether other objectives can be started from RAN1#110bis-e:
To check in RAN#97 for objectives 1 and 3, taking into account the progress on objectives 2 and 4, aiming to have specification work for both objective 1 and 3
  1. Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation [RAN2, RAN1, RAN4] (This part of the work is put on hold until further checking in RAN#97)
  2. Study and specify support of sidelink on unlicensed spectrum for both mode 1 and mode 2 where Uu operation for mode 1 is limited to licensed spectrum only [RAN1, RAN2, RAN4]
  3. Study and specify enhanced sidelink operation on FR2 licensed spectrum [RAN1, RAN2, RAN4] (This part of the work is put on hold until further checking in RAN#97)
  4. Study and specify, if necessary, mechanism(s) for co-channel coexistence for LTE sidelink and NR sidelink including performance, necessity, feasibility, and potential specification impact if any [RAN1, RAN2, RAN4]

## Slide 3: Conclusion in RAN1#110
The following conclusion was made to support co-channel coexistence:
  For co-channel coexistence in Rel-18, RAN1 concludes that the TDM-based semi-static resource pool partitioning based on Rel-16/17 specifications is one possible solution to ensure co-channel coexistence between LTE-V UEs and NR-V UEs.
    Note: The LTE and NR resource pools do not overlap in time with each other in the TDM-based semi-static resource pool partitioning.
    Note 2: Rel-16 in-device coexistence framework can ensure alignment between the slot boundary of the NR SL time slot and the subframe boundary of the LTE SL subframe
    FFS: potential enhancements for synchronization can be further investigated

## Slide 4: Discussion on the work scope of Rel-18 sidelink
For objective 4 (Co-Ex), there is no need to further optimization because a feasible solution (i.e., the TDM-based semi-static resource pool partitioning) to support co-channel coexistence was already identified.
  It was shown that the TDM-based scheme can provide most of scenarios with a significant performance gain
  Dynamic approach is beneficial in a limited scenario with a marginal gain.
For objective 2 (SL-U), there are many remaining open issues to be discussed and RAN1 continues to work on objective 2.
For objective 3 (SL-FR2), time used for objective 4 discussion can be replaced by objective 3 in the way that RAN1 focuses on the update of evaluation methodology for objective 3.
For objective 1 (SL-CA), it is led by RAN2 and the exact work scope from RAN 1 will be able to be determined based on RAN2 progress. Therefore, RAN1 needs to postpone objective 1.

## Slide 5: Proposals
Proposal 1: RAN concludes that RAN1 work to support co-channel coexistence for LTE sidelink and NR sidelink (i.e., objective 4) is completed in Rel-18 sidelink.
Proposal 2: RAN guides RAN1 to start the discussion on objective 3 (i.e., sidelink operation on FR2 licensed spectrum) from RAN1#110bis-e.