## Slide 1: Discussion on potential scope for Rel-18 NTN Coverage Enhancements
MediaTek Inc.
3GPP TSG RAN#97-e RP-222342
Electronic Meeting, September 12-16, 2022 Agenda Item 9.3.2.7

## Slide 2: Introduction
RAN to determine by RAN#97 (for RAN1 items) and RAN#98 (for RAN2 items) whether the study phase has identified any need for NTN-specific coverage enhancements in Rel-18. If needed, the set of NTN-specific work item objectives will be updated.
RAN1#110 captured observations and conclusions for evaluation of necessary NTN coverage enhancements for UL physical channels

## Slide 3: MediaTek View - NO DL NTN Coverage enhancements necessary - Prioritize UL NTN Coverage enhancements
Assumptions
  Antenna loss -5 dBi
  Polarization loss 3 dB
  Target UL SNR with Set-1 parameters for LEO 1200 km in LOS
Targeted service:
  VoIP using AMR 4.75 kbps.
  Low data rate of 3 kbps.
Prioritize UL physical channel Coverage enhancements:
  PUCCH for Msg4 HARQ-ACK
  PUSCH for VoIP
  PRACH (discuss first in Rel-18 Further NR Coverage Enhancements WI)
Case | Satellite orbit | Satellite parameter set | Service type
1 | GEO | 1 | Low-data rate service
2 | GEO | 2 | Low-data rate service
3 (Optional) | LEO-1200 | 1 | VoIP
4 | LEO-1200 | 2 | VoIP
5 | LEO-1200 | 2 | Low-data rate service
6 (Optional) | LEO-600 | 1 | VoIP
7 | LEO-600 | 2 | VoIP
8 (Optional) | LEO-600 | 2 | Low-data rate service
9 (Optional, with higher priority than case 10) | MEO | 1 | Low-data rate service
10 (Optional) | MEO | 2 | Low-data rate service

## Slide 4: Background NTN Coverage Enhancement Objective
Rel-18 NTN Enhancements WID was revised in RP#97June/2022 in RP-221819
A 1-TU 6-month study phase focusing on the following (to derive clear & limited scope):
  Evaluate the coverage performance and identify the candidate physical radio channels that have coverage issues specific to NTN with following target services taking into account the studies in TR38.830 where appropriate, as well as general coverage enhancement techniques specified in Rel-18 [RAN1,RAN2,RAN4]
The following items are shown as examples of areas to consider in the next step of the study. The actual items for study will be based on the evaluation of coverage issues specific to NTN identified above.
  NTN-specific repetitions enhancements beyond techniques covered in Rel-17 CovEnh WI for the relevant channels
  NTN-specific techniques for improved diversity and/or reduced polarization loss
  Improved performance of low-rate codecs in link budget limited situation including reducing RAN protocol overhead for VoNR
  NOTE: Intent is not to introduce a new codec.
RAN to determine by RAN#97 (for RAN1 items) and RAN#98 (for RAN2 items) whether the study phase has identified any need for NTN-specific coverage enhancements in Rel-18. If needed, the set of NTN-specific work item objectives will be updated.

## Slide 5: Thank You!