## Slide 1: Motivation for Rel-18 new WI on NR MIMO OTA
http://www.caict.ac.cn/
CAICT
3GPP TSG RAN #97-e
Electronic Meeting, September 12-16, 2022
Source: CAICT
Document for: Discussion
Agenda Item: 9.5.4.1
RP-222345

## Slide 2
Background
RAN4 has achieved good progress in NR MIMO OTA WI according to the latest SR in RAN#97e [1]:
    Core part is 100% completion level with a full package of test method aiming for requirement development, the outcome is captured in TS38.151 v17.1.0
      Test system setups are defined, i.e., MPAC for FR1 and 3D-MPAC for FR2.
      Test methods focus on smartphone UE type with Free space test condition.
      FR1 and FR2 Channel model validation pass/fail limits are finalized.
      Preliminary MU assessments for FR1 and FR2 are approved.
    Performance part is 90% completion level with FR1 TRMS requirements and recommended Test Tolerance (TT) specified
      The FR1 requirement work is focused on limited working scope, i.e. SA mode and only n41/n78 with smartphone UE type and Free space test condition.
      Figure of Merits (FoM) of FR2 MIMO OTA is defined but no agreement in RAN4 for FR2 MIMO OTA requirement. How to conclude the performance part of FR2 depending on the RAN-P decision.
      The WI is expected to be finalized on time in Sep RAN meeting.
  A LS to 3GPP RAN5, CTIA MOSG, CCSA TC9 WG1 was approved to provide information on the technical progress of NR MIMO OTA WI in 3GPP RAN4 [2].

## Slide 3
Previous discussion outcome in RAN-P
According to moderator’s summary for discussion [95e-12-RAN4-R18-OTATest] [3], WF on how to handle other OTA topics is captured in the meeting report [4].
    The other OTA topics including Dynamic OTA testing method for FR2-1, FR2 testing framework for FWA devices (PC1/PC5), Rel-17 OTA leftovers and follow-up work for ongoing Rel-17 SISO OTA and MIMO OTA will be postponed and revisited in future RAN plenary meetings designated as the checking point by RAN chair.

## Slide 4
Views on the follow-up work of R17 WIs (1)
Considering that the core part of Rel-17 NR MIMO OTA and TRP TRS OTA WIs were closed, and OTA performance requirements were specified in RAN4#104-e, it is expected that these WIs will be closed in Sep. RAN-P meeting.
However, Rel-17 WI focused on limited scope due to the workload and limited TUs
  Only single UE type (smartphone) in single test condition (free space) is discussed
  Requirement development focused on few test frequencies (n41, n78)
  FR2 figure of merit is only applicable for PC3 UEs
  No agreement on FR2 MIMO OTA requirement
The above limited scope of Rel-17 WI will lead to some limitations, for example:
  Free space condition has limitations in evaluating the TRMS performance of UEs in actual use scenarios.
  The proportion of tablet is gradually increasing, and their use scenarios have higher requirements on throughput, but lack of corresponding requirements.
  The deployment frequency bands of NR has increased, these bands also need to define MIMO OTA requirements.
  Performance requirement for FR2 MIMO OTA is not finalized, which cannot guarantee the actual performance of FR2 UEs in the realistic network.

## Slide 5
Views on the follow-up work of R17 WIs (2)
Therefore, in order to accurately evaluate the actual performance of the UE under the realistic network conditions, we propose a continuous work for NR MIMO OTA in Rel-18 to address Rel-17 leftovers and provide enhanced test methodology for other UE types and UE features, develop requirements for both FR1 and FR2 frequency bands.
For example:
  Test method for Smartphone in browsing mode using hand phantom
  Test method for laptop/tablet/FWA in free space
  FR1 Performance requirements for other FR1 bands for smartphone, e.g. n1,n28,n77
  FR2 FoM and criteria for other power classes
  Framework for FR2 MIMO OTA performance requirements development
  FR2 MIMO OTA performance requirements.

## Slide 6
Observations and Proposals
Observation 1: Based on current progress of Rel-17 OTA topics, these WIs are expected to be concluded in September RAN-P meeting without additional extension.
Observation 2: Rel-17 WI focused on limited scope due to the workload and limited TUs, study on enhanced test methods and performance requirement is necessary in Rel-18 timeline to guarantee the performance of UEs in the actual use scenario.
Proposal 1: Rel-17 OTA leftovers and follow-up work for ongoing Rel-17 SISO OTA and MIMO OTA will be revisited in RAN plenary meetings designated as the checking point by RAN chair, i.e., September or December.
Proposal 2: Propose to consider a continuous work of NR MIMO OTA WI in Rel-18 timeline to provide enhanced test method and performance requirements. For example:
  Test method for Smartphone in browsing mode using hand phantom
  Test method for laptop/tablet/FWA in free space
  FR1 Performance requirements for other FR1 bands for smartphone, e.g. n1,n28,n77
  FR2 FoM and criteria for other power classes
  Framework for FR2 MIMO OTA performance requirements development
  FR2 MIMO OTA performance requirements.

## Slide 7
References
    [1] RP-222347, Status report for WI: Multiple Input Multiple Output (MIMO) Over-the-Air (OTA) requirements for NR UEs; Rapporteur: CAICT
    [2] R4-2215136, LS on NR MIMO OTA progress, CAICT
    [3] RP-220978, Moderator’s summary for discussion [95e-12-RAN4-R18-OTATest], Qualcomm
    [4] RP-221776, Meeting report for TSG RAN meeting #95e

## Slide 8
http://www.caict.ac.cn/
中国信息通信研究院
谢谢！
国家高端专业智库 行业创新发展平台