## Slide 1: Views on WID of Rel-18 eRedCap
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #97-e
Electronic Meeting, September 12th - 16th , 2022
RP-222391

## Slide 2: Background
RAN1 propose down-selection for potential complexity reduction for Rel-18 eRedCap UE
Based on the analysis of the studied UE complexity reduction options, most companies in RAN1 recommend that a single option is down-selected from a list of options as the main Rel-18 RedCap UE complexity reduction option at RAN plenary. The list includes the following options.
Option BW3:
  5 MHz BB bandwidth only for PDSCH (for both unicast and broadcast) and PUSCH with 20 MHz RF bandwidth for UL and DL.
  The other physical channels and signals are still allowed to use a BWP up to the 20 MHz maximum UE RF+BB bandwidth.
Option PR3:
  Restriction of maximum number of PRBs for PDSCH and PUSCH.
  For 15 kHz SCS, the maximum number of RBs is 25.
  For 30 kHz SCS, the maximum number of RBs is 11 or 12.
  The restricted number of PRBs in Option PR3 is a hardcoded limit.
Some of the companies who participated in the study also wanted to include one or both of the following options in the above list, for RAN plenary to assess the trade-off between degree of complexity reduction and specification impact.
Option PR1:
  Relaxation of the constraint for peak data rate reduction.
  The relaxed constraint is, e.g., 1 (instead of 4).
  The parameters [38.306] can be as in Rel-17 RedCap.
Option BW1:
  Both RF and BB bandwidths are 5 MHz for UL and DL.

## Slide 3: Background
RAN1 propose down-selection for potential complexity reduction for Rel-18 eRedCap UE
Furthermore, RAN1 recommends that Option PR1 is considered as a potential add-on. Whether to adopt this potential add-on can be decided during WI phase.
Whether or not to also introduce support for option PT1 and/or PT2 for a Rel-18 RedCap UE can be decided at RAN plenary.
Option PT1:
  Relaxation of UE processing time for PDSCH/PUSCH in terms of N1 and N2 (as defined in TS 38.214) compared to those of UE processing time capability 1
  The relaxation factor for N1 and N2 is assumed to be 2 in the study.
Option PT2:
  Relaxation of UE processing time for CSI in terms of Z and Z’ compared to the values defined in TS 38.214 clause 5.4
  The relaxation factor for Z and Z’ is assumed to be 2 in the study.

## Slide 4: Views on BW/PR options
Overview of the BW/PR options regarding complexity, coverage, spec impact, co-existence
Observation
  As recommended by RAN1, BW3 and PR3 achieve the best trade-off
    BW3 slightly outperforms PR3 in terms of complexity reduction
  BW1 is not preferred, considering the limited TU and foreseen huge workload
Proposal
  Adopt Option BW3 for Rel-18 eRedCap WI
Options | Complexity reduction |  | Coverage loss | Spec impact | Co-existence issue
 | FD-FDD 1Rx | TDD 1Rx |  |  | 
BW1 | 11.85% | 11.25% | Medium | Large | Large
BW3 | 8.02% | 7.66% | Small | Small | Small
PR1 | 4.13% | 4.02% | None | minimal | minimal
PR3 | 7.06% | 6.74% | Small | Small | Small

## Slide 5: Views on PT options
Overview of the PT options regarding complexity, coverage, spec impact, co-existence
Observation
  Both PT1 and PT2 will heavily increase scheduling complexity of network
  PT2 achieves larger complexity reduction at a smaller cost of spec impact and co-existence issue
Proposal
  At least Options PT1 shall NOT be adopted for Rel-18 eRedCap WI
  Option PT2 is not preferred either, but can live with standalone PT2
  If PT2 needs to be bundled with PT1, none of them shall be adopted
Options | Complexity reduction |  | Spec impact | Co-existence issue | Network complexity
 | FD-FDD 1Rx | TDD 1Rx |  |  | 
BW3 | 8.02% | 7.66% | (assuming BW3 as baseline) |  | 
PT1 | 8.70% (BW3+PT1) (PT1 add-on: 0.68%) | 7.84% (BW3+PT1) (PT1 add-on: 0.18%) | Medium | Medium | Large
PT2 | 11.55% (BW3 + PT1 + PT2) (PT2 add-on: 2.85%) | 11.50% (BW3 + PT1 + PT2) (PT2 add-on: 3.66%) | Small | none | Large

## Slide 6: Conclusion
Proposals
  For down-selection between BW/PR options
  Adopt Option BW3 for Rel-18 eRedCap WI
  For PT1/PT2
  At least Options PT1 shall NOT be adopted for Rel-18 eRedCap WI
  Option PT2 is not preferred either, but can live with standalone PT2
  If PT2 needs to be bundled with PT1, none of them shall be adopted