## Slide 1
Further enhancement of RAN slicing in Rel-18
3GPP TSG RAN#97-e
Electronic Meeting, Sep. 12 - 16
Source: ZTE, Sanechips
Agenda: 9.1
RP-222443

## Slide 2: Rel-18 network slicing progress in SA2
SA2 has the Rel-18 FS_eNS_Ph3 study in TR 23.700-41.
This study includes 6 key issues and associated solutions so far.
SA2 is now evaluating all solutions and trying to conclude the study at Oct meeting.
An LS (S2-2207435 LS Out on RAN dependency of FS_eNS_Ph3) has been sent to RAN2 and RAN3 to ask for views on solutions with RAN dependency.

## Slide 3: Key issues in FS_eNS_Ph3 with potential RAN impact (1)
Key issues in FS_eNS_Ph3 in SA2 | Solutions in TR 23.700-41 | Potential RAN impact
Key Issue#1: Support of Network Slice Service continuity | Solution#1,2,3,4,5,15,32,40,41,42,43 | Solution#3: Target RAN node -> Source RAN node: Accept the PDU session with the slice requires remapping due to the remapping action and indicate the remapped slice. RAN node->AMF: The PDU session associated with the network that requires slice remapping needs to be terminated and a new PDU session is to be setup with the remapped slice. Solution#43: Handling PDU session modification which related to the secondary S-NSSAI.
Key issue#3:Network Slice Area of Service for services not mapping to existing TAs boundaries and Temporary network slices | Solution#8,9,10,11,21,22,23,24,26,29,44,45 | Solution#9: Broadcast one or more Secondary TAIs via an updated SIB or new SIB, and report them to the CN and between gNBs as per existing Tracking Area related information exchange procedures but with indication they are secondary. The additional TAIs are associated with specific S-NSSAI(s) like the existing TAs and will be treated by UEs supporting secondary TAs as a normal Tracking area from RM standpoint.

## Slide 4: Key issues in FS_eNS_Ph3 with potential RAN impact (2)
Key issues in FS_eNS_Ph3 in SA2 | Solutions in TR 23.700-41 | Potential RAN impact
Key issue#3:Network Slice Area of Service for services not mapping to existing TAs boundaries and Temporary network slices | Solution#8,9,10,11,21,22,23,24,26,29,44,45 | Solution#11 and others: NG-RAN to be configured with a slice availability on a per-cell basis and inform AMF and other gNBs in NGAP messages. Solution#29 and others: The NG-RAN receives the partially allowed S-NSSAIs in addition to the Allowed NSSAI and trigger handover procedure to a supporting TAI of the partially allowed S-NSSAIs to enable the support of the maximum number of S-NSSAIs in the Allowed and partly allowed S-NSSAIs lists. Solution#45: Prevent the UE from entering into a cell belonging to the CSANS unnecessarily when any PDU session related to the S-NSSAI has an active user plane. Keep the configuration of the Constrained Service Area information.

## Slide 5: Proposal on further enhancement of RAN slicing in Rel-18
Observation: Clear impact on RAN can be seen from the key issues and solutions in Rel-18 FS_eNS_Ph3 study in SA2.
Proposal: A WI with study phase is required in Rel-18 late package to address the corresponding impact on RAN and some R17 leftover issues with the following objectives:
  Further enhancement on RAN support of slicing, including:
    Specify mechanisms and signalling to support MT triggered slice aware cell reselection and slice based random access. [RAN2]
    For non-supported slice by the serving cell, specify mechanism to support UE to access to the intended slice by setting up DC or CA. [RAN2, RAN3]
  Study the RAN impacts of SA2 slicing enhancement in Rel-18, and specify the corresponding signalling if required:
    NOTE: To be updated in RAN#98 based on the conclusion from SA2 SI.
    For non-supported slice by target NG-RAN node in case of inter-RA mobility scenario, study the RAN impacts of SA2 solutions to provide service continuity, and specify the corresponding signalling if required. [RAN3]
    Study the RAN impacts of the SA2 solutions, and specify the corresponding signalling to support Network Slice Area of Service for services not mapping to existing TAs boundaries and Temporary network slices, if required. [RAN2, RAN3]

## Slide 6: Thanks!