## Slide 1: Moderator’s summary for discussion [97e-22-R18-NR-NTN]
Rapporteur (Thales)
3GPP TSG-RAN Meeting #97-e
Electronic Meeting, September 12-16, 2022
Agenda Item: 9.3.2.7
RP-222582

## Slide 2: Topic #1: NTN cov enh Reference scenario
The following way forward can be agreed:
Capture in Rel-18 NR_NTN_enh WI
« The following reference scenario is considered for the definition of coverage enhancements for NTN: parameter set-1 for LEO-1200 satellite operating at Line of Sight (LOS) and commercial smartphones with -5.5 dBi antenna gain and 3 dB polarisation loss.
Note: It is understood that the enhancements defined for LEO can also apply to GEO and MEO scenarios as appropriate.
The targeted services are VoIP using AMR 4.75 kbps and data transmission services with Low data rate of 3 kbps”

## Slide 3: Topic #2: UL channels (PUCCH/PUSCH) enhancements
The following way forward can be agreed:
Capture in Rel-18 NR_NTN_enh WI
« The objectives are for NTN:
To specify coverage enhancements to PUCCH for Msg4 HARQ-ACK [RAN1, RAN4]
To study DMRS bundling for PUSCH taking into account NTN-specific time-frequency pre-compensation and, if necessary, specify enhancements to the Rel-17 procedures [RAN1] »

## Slide 4: Topic #3: PRACH enhancements
The following way forward can be agreed:
Capture in Rel-18 NR coverage enhancements WI
« additional PRACH enhancements are considered, if needed, in view of NTN specifics (i.e. agreed at RAN1#109, under NR_NTN_enh WI) »

## Slide 5: Topic #4: DL enhancements
Company views
  The interest on DL channel enhancements is acknowledged by large number of companies. However the use case is not clear which prevents to provide a clear guidance for RAN1.
  There are different views on the use case
    Power split on board: Apple, Lockheed, Ligado, Novamint, Inmarsat
    PFD limits: ZTE, Inmarsat
  A majority of companies are favorable to continue discussing the topic except Mediatek, Samsung, Nokia, Ericsson which consider the issue unclear.
Moderator recommendation
  further discuss the issue at RAN1 until RAN#98-e then decide at RAN#98-e, the way forward
The following way forward can be discussed online:
Capture in Rel-18 NR_NTN_enh WI :
“Start normative phase on uplink channel enhancements after RAN#97-e.
RAN1 discuss further DL enhancements and decide the way forward at RAN#98-e.”

## Slide 6: Topic #5: High power UE
This topic was discussed during the initial round and collected a wide support.
The following way forward can be discussed:
Capture in the chair’s note:
“High power UE (e.g. 26 dBm Tx power) may be considered for NTN FDD bands to enhance the coverage”

## Slide 7: Reference T-Docs
Documents [1] through [13] can be noted.
[1] RP-222081 discussion Discussion on NR NTN coverage enhancement LG Electronics Polska
[2] RP-222096 discussion Discussion on Rel-18 NTN Coverage enhancement Beijing Xiaomi Mobile Software
[3] RP-222151 discussion Discussions on NR NTN coverage enhancements vivo
[4] RP-222206 discussion Views on NTN coverage enhancements Qualcomm Incorporated
[5] RP-222234 discussion On the work scope of Rel-18 NR NTN enhancements Samsung
[6] RP-222254 discussion Discussion on coverage enhancement for Rel-18 NR NTN NTT DOCOMO, INC.
[7] RP-222301 discussion Discussion on direction for NTN enhancement SK Telecom
[8] RP-222305 discussion On the need for NTN-specific coverage enhancements in Rel-18 Ericsson
[9] RP-222316 discussion Views on the coverage enhancements in Rel-18 for non-terrestrial networks Huawei, HiSilicon
[10] RP-222319 discussion Coverage enhancements for NTN THALES
[11] RP-222342 discussion Discussion on potential scope for Rel-18 NR NTN Coverage Enhancements MediaTek Inc.
[12] RP-222439 discussion Discusssion on NR-NTN in Rel-18 ZTE, Sanechips
[13] RP-222485 discussion Discussion on Rel-18 NR NTN Coverage Enhancement Apple Inc., Lockheed Martin, Inmarsat, OPPO