## Slide 1: On support of measurement(s) for FR2 in SL positioning Agenda Item: 9.3.1.9 Source: OPPO Document for: Discussion, Decision
3GPP TSG RAN #99
Rotterdam, Netherlands, March 20-23, 2023
RP-230143

## Slide 2: Background
  In the WID RP-223549 for Expanded and Improved NR Positioning there is one Note on SL PRS transmission in FR2:
    “NOTE: SL PRS transmission in FR2 is not precluded but no FR2 specific aspects will be specified. “
  In RAN1#112, companies debated on whether measurement(s) for FR2 should be specified or not due to different understanding on the Note.
    Some companies believe measurement(s) for FR2 should be specified as SL PRS transmission in FR2 is allowed, however, it was objected by some other companies as the Note says “no FR2 specific aspects will be specified”.

## Slide 3: Discussion
  In our view, measurement(s) should be specified for FR2:
    Without measurement(s), most SL positioning methods are not workable in FR2.
      In particular for RTT-type methods, it is completely dependent on Rx-Tx time difference report regardless of UE based or network based positioning.
    The work load to specify the measurement(s) for FR2 is trivial
      Similar as the measurements specified in Uu positioning, the only difference between a measurement for FR1 and FR2 is the “reference point”.
    According to the Note SL PRS transmission in FR2 is not precluded, following the spirit, SCS for SL PRS in FR2 was agreed in RAN1#112, it is NOT desirable if SL positioning is not supported in FR2 in the end.
Agreement (RAN1#112) Support SCS values for SL PRS include: 15 kHz, 30 kHz, 60 kHz for FR1, and 60 kHz, 120 kHz for FR2 Which SCS values are required, and which ones are optional follow Rel-16 UE capabilities.

## Slide 4: Discussion
  One example (UE Rx-Tx time difference) on the difference between the measurement for FR1 and FR2 in Uu positioning:
  Proposal: FR2 specific reference point for the measurement(s) introduced in SL positioning should be specified, to make one of following clarifications in the WID:
    “NOTE: SL PRS transmission in FR2 is not precluded but no FR2 specific aspects will be specified (This does not preclude to specify FR2 specific reference point for the measurement(s)). “ Or,
    “Specify measurements for both FR1 and FR2 to support RTT-type solutions using SL, SL-AoA, and SL-TDOA [RAN1, RAN2].”