## Slide 1: WI scope for XR awareness
LG Electronics

## Slide 2: Approved WI scope in RAN#98 (RP-223502)
Specify the enhancements related to power saving:
  DRX support of XR frame rates corresponding to non-integer periodicities (through at least semi-static mechanisms e.g. RRC signalling) (RAN2).
Specify the enhancements related to capacity:
  Multiple CG PUSCH transmission occasions in a period of a single CG PUSCH configuration (RAN1, RAN2);
  Dynamic indication of unused CG PUSCH occasion(s) based on UCI by the UE (RAN1);
  BSR enhancements including at least new BS Table(s); (RAN2);
  Delay reporting of buffered data in uplink; (RAN2);
  Provision of XR traffic assistance information for DL and UL (e.g. periodicity); (RAN2);
  Discard operation of PDU Sets (RAN2);
Specify the enhancements for XR Awareness (RAN2, RAN3): TBD (detailed objectives will be further clarified at RAN#99 based on the conclusions of TR38.835, and work to be started only after RAN#99)
XR awareness scope should be specified in RAN#99

## Slide 3: Progress on XR awareness in RAN2#121
  Agreements related to XR awareness
    RAN2 thinks that how PSER is enforced is up to network implementation.
    Introduce UL PDU Set Importance. How UE derives this will be handled in UE implementation.
    Can indicate that in RAN2 considers PDU set concept applicable to both UL and DL in LS to SA2.
    RAN2 thinks UL jitter may be present for XR (e.g. for tethering use cases). It is unclear how network would use UL jitter information (depends on what would be signalled, and would anyway be up to network implementation).
    RAN2 intends to support tethering use case for XR. This may require signalling of some UL traffic arrival information from UE to network.
    Since we already agreed to not support delay-aware LCP, RAN2 aims not to introduce changes to LCP due to PDU prioritization.
    RAN2 thinks PSI can be useful for PDU set-based discard. RAN2 aims to introduce a mechanism to allow UE to handle discarding of packets with different PSI in case of congestion. FFS for other cases.
    Support of RLC bearer splitting should be limited to existing cases (e.g. PDCP duplication), no new XR-specific functionality.
XR awareness scope can be made based on above three RAN2 agreements

## Slide 4: Proposed WI scope for XR awareness
Agreements: RAN2 intends to support tethering use case for XR. This may require signalling of some UL traffic arrival information from UE to network.
  Proposed scope: Signaling of UL traffic arrival information
Agreements: RAN2 thinks PSI can be useful for PDU set-based discard. RAN2 aims to introduce a mechanism to allow UE to handle discarding of packets with different PSI in case of congestion.
  Proposed scope: PDU set discard at congestion based on PDU set importance
Agreements: Support of RLC bearer splitting should be limited to existing cases (e.g. PDCP duplication), no new XR-specific functionality.
  Proposed scope: PDCP duplication based on PDU set importance

## Slide 5: Issues in XR power saving in RAN2#121
Agreements: Whether the issue of retransmission-less CG for UL pose transmission is addressed in the WI needs to be discussed in RAN
The need for retransmission-less CG
  Pose information is periodically transmitted in uplink
  CG is useful for periodic UL transmission
  Each time UL transmission is performed on CG, the UE moves to DRX Active Time due to drx-RetransmissionTimerUL

## Slide 6: Proposals
Include new objectives for XR awareness with followings:
  Signaling of UL traffic arrival information
  PDU set discard at congestion based on PDU set importance
  PDCP duplication based on PDU set importance