## Slide 1
3GPP TSG RAN Meeting #99 RP-230377
Rotterdam, Netherlands, March 20-23, 2023
Source: vivo
Document for: Discussion
Agenda Item: 9.13
Study on AI based mobility enhancement in Rel-19

## Slide 2
Motivation
Observation 1: For mobility optimization, if the Model Inference function can be deployed on the UE side:
More detailed local information from UE can be utilized as the input to improve prediction accuracy without privacy concerns.
Local model inference can reduce inference latency and therefore interruption.
In Rel-17, the AI/ML based mobility optimization was studied in the FS_NR_ENDC_data_collect SI and the subsequent WI in Rel-18 is ongoing.
The Model Inference function resides within the RAN node only.
Some location-related information of UE (e.g., coordinates) was required as the input of AI/ML model, which may introduce UE privacy concerns.
Frequent exchange of the input between network and UE will introduce massive signaling overhead and latency.
In Rel-18, the NR_AIML_Air SI would introduce the framework and model life cycle management to enable the inference functionality on the UE side.
The framework can be reused to facilitate more AI-based use cases, e.g., AI-based mobility, between UE and network.

## Slide 3
Potential Issues
For the legacy HO, the triggering condition for RRM reporting shall be met at T0 and shall last for TTT (Time To Trigger) duration, which may lead to:
HO at a non-optimal time, poor user experience at source cell.
Failed to receive the HO command or failed to RA to the target cell, i.e., too-late HO.
For CHO, the UE can RA to the target cell without receiving the HO command if the triggering condition is met during TTT. However, there is still a risk of RLF due to low SINR at the source cell during TTT and the UE cannot perform HO at a optimal time.
The legacy solution to the above issue by reducing TTT duration may result in other unintended events, e.g., too-early HO, ping-pong HO, especially for the high-speed UEs.
If an RLF occurs shortly after a successful HO, the UE may attempt to re-establish the radio link connection in a cell other than the source cell and the target cell, which is identified as HO to wrong cell.
……
triggering condition
is met
TTT
T0
T0+TTT
RRM
report
HO decision &
Admission control
RA
HO command
Omitted for CHO
Re-establish in another cell
RLF occur

## Slide 4
Solution1: RSRP prediction based HO
The RSRP prediction is performed at the UE side.
For the legacy HO, with RSRP prediction, the UE can send the RRM report once the triggering condition is met at T0 (i.e., no need to wait for TTT duration).
RSRP prediction within the T0 +TTT period shall meet the triggering condition,
The UE may send the RSRP prediction of neighbor cells during RA in the RRM report for HO decision,
Higher success rate for receiving HO command when the RRM report was sent at an optimal time.
For CHO, with RSRP prediction, the UE can RA to the target cell once the triggering condition is met at T0.
RSRP prediction within the T0 + TTT period shall meet the triggering condition,
Lower risk of RLF at the source cell when the HO is performed at a optimal time.
During the HO decision and target cell selection, the RSRP prediction can be used to reduce the unintended events, e.g., ping-pong HO, too early HO, HO to wrong cell.
HO decision &
Admission control
RA
T0
RRM
report
HO command
Omitted for CHO

## Slide 5
Solution2: SINR prediction based HO
The SINR prediction is performed at the UE side.
For the legacy HO, with SINR prediction, the UE can send the RRM report once the triggering condition is met at T0 (i.e., no need to wait for TTT duration).
SINR prediction of the serving cell within the T0 +TTT period is below the threshold,
Higher success rate for receiving HO command when the UE still in the coverage of serving cell.
Note that solution1 and solution2 can be combined to optimize the mobility performance.
HO decision &
Admission control
RA
T0
RRM
report
HO command
Omitted for CHO

## Slide 6
Scenario1: HO to wrong cell at crossover
UE1 speed: 30km/h
T1 duration: 1960ms
UE2 speed: 60km/h
T2 duration: 960ms
When the UE passes through the crossover, the RSRP of cell2 will change dramatically.
The UE1 at a low speed should handover to Cell2 upon RSRP rises to achieve better quality of service during T1 duration.
The UE2 at a high speed should handover to Cell3 rather than Cell2 to avoid HO to wrong cell or ping-pong HO.
RSRP prediction is the key to achieve the above expected different UE behaviors.
Simulation scenario and UE trajectory
T1
T2

## Slide 7
Feasibility evaluation – scenario1
 | Cell 1 | Cell 2 | Cell 3
Prediction 1 | RMSE = 0.0044dB | RMSE = 1.08dB | RMSE = 0.26dB
Prediction 2 | RMSE = 0.0062dB | RMSE = 1.11dB | RMSE = 0.26dB
Prediction 3 | RMSE = 0.0844dB | RMSE = 1.23dB | RMSE = 0.28dB
Carrier Frequency: FR2, 30GHz Prediction 1: RSRP of every 80ms in 320ms after T0 Prediction 2: RSRP of 1s after T0 Prediction 3: RSRP of 2s after T0 |  |  | 
Accuracy of RRM measurement prediction
Step1: UE1/UE2 decides to trigger the RRM reporting based on the predicted RSRP of every 80ms in 320ms after T0
Step2: The Source cell determines the target cell based on the predicted RSRP of 1s and/or 2s after T0:
For UE1, the RSRP prediction of Cell2 will last for a specific period ( T1>1s), and Cell2 is selected as target cell,
For UE2, the RSRP prediction of Cell2 will decrease at a short time (T2<1s), then Cell3 is selected as target cell.
Step3: The UEs receive different HO commands and HO to separate suitable cells.
Expected signaling procedure

## Slide 8
Scenario2: unintended event due to TTT
Simulation scenario and UE trajectory
Simulation assumption
Attributes | Values or assumptions
Carrier Frequency | FR1: 4GHz; FR2: 30GHz
TRP Number | 7 sites, 3 sector per site
Channel Model | 3D-Uma in TR 38.901, support Spatial consistency ISD = 200m
UE speed | 120km/h
Mobility management | Event: A3; Hysteresis: 2dB; Offset: 1dB; TimeToTrigger: 320ms, 40ms Handover preparation time: 50ms; Handover execution time: 40ms
RLM | L1 measurement period: 20ms Qin sliding window length: 100ms Qout sliding window length: 200ms Qin threshold: -6dB; Qout threshold: -8dB N310: 1; N311: 1; T310: 1s
Handover model and corresponding metrics | As defined in TR 36.839 Short time of stay: served by the target cell for less than 1s after HO
Simulation scenario

## Slide 9
Feasibility evaluation - RSRP prediction based HO
 | Prediction 1 | Prediction 2
FR1 | RMSE = 0.38 dB | RMSE = 1.6 dB
FR2 | RMSE = 1.3 dB | RMSE = 3.3 dB
Training dataset: Same large scale channel parameters for different drops Prediction 1: RSRP of every 80ms in 320ms after T0 Prediction 2: RSRP of 1s after T0 |  | 
Accuracy of RSRP prediction
Legacy HO:
UE can decide whether to trigger the RRM reporting based on the predicted RSRP of every 80ms in 320ms after T0,
Source cell can determine the target cell based on the predicted RSRP of 1s after T0 to avoid too early HO or HO to wrong cell,
Source cell can forward the predicted RSRP to target cell for admission control.
CHO:
UE can decide to trigger the target cell selection based on the predicted RSRP of every 80ms in 320ms after T0,
UE can choose the target cell based on the predicted RSRP of 1s after T0 to avoid too early HO or HO to wrong cell.
Usage of RSRP prediction

## Slide 10
Feasibility evaluation - RSRP prediction based HO
RSRP prediction based HO
 |  | Legacy HO, TTT = 320 | Legacy HO, TTT = 40 | AI based HO | CHO, TTT = 320 | CHO, TTT = 40 | AI based CHO
FR1 | HOF rate | 9.16% | 2.2% | 1.95% | 0.28% | 0.15% | 0.32%
 | Ping-pong HO rate | 1.1% | 3.6% | 0.37% | 1.0% | 3.7% | 0.37%
 | Short Time of Stay (1s) rate | 13.4% | 18.9% | 5.7% | 13.6% | 18.8% | 5.67%
FR2 | HOF rate | 7.4% | 2.5% | 2.0% | 0.42% | 0.43% | 0.44%
 | Ping-pong HO rate | 5.2% | 10.3% | 2.7% | 5.2% | 10.3% | 2.7%
 | Short Time of Stay (1s) rate | 24.1% | 36.7% | 10.4% | 24.4% | 36.5% | 10.8%
Observation 2: With RSRP prediction, the unintended events rate during HO and CHO can be significantly reduced, including HOF rate, ping-pong HO rate and short time of stay rate.

## Slide 11
Feasibility evaluation - SINR prediction based HO
 | prediction of the minimum SINR during TTT
FR1 | RMSE = 0.79 dB
FR2 | RMSE = 2.12 dB
Training dataset: Same large scale channel parameters for different drops | 
Accuracy of SINR prediction
Legacy HO:
If the predicted minimum SINR during TTT is below the threshold, UE can trigger the legacy RRM reporting.
Source cell can determine the target cell based on the reporting RSRP, i.e., real measurement RSRP.
Usage of SINR prediction

## Slide 12
Feasibility evaluation - SINR prediction based HO
SINR prediction based HO
 |  | Legacy HO, TTT = 320 | Legacy HO, TTT = 40 | AI based HO
FR1 | HOF rate | 9.16% | 2.2% | 1.60%
 | Ping-pong HO rate | 1.1% | 3.6% | 1.87%
 | Short Time of Stay (1s) rate | 13.4% | 18.9% | 13.5%
 | Average SINR during HO (dB) | 1.81 | 3.00 | 6.01
 | 5% SINR during HO (dB) | -8.05 | -4.81 | -0.19
FR2 | HOF rate | 7.4% | 2.5% | 1.7%
 | Ping-pong HO rate | 5.2% | 10.3% | 9.8%
 | Short Time of Stay (1s) rate | 24.1% | 36.7% | 33.8%
 | Average SINR during HO (dB) | 6.24 | 10.28 | 12.7
 | 5% SINR during HO (dB) | -5.26 | -0.54 | 3.77
Observation 3: With SINR prediction, the average SINR during the HO can be increased 2~6dB and 5% SINR can be increased 4~8dB, which will reduce the HOF rate, reduce ping-pong rate in short TTT and improve UE throughput during HO.

## Slide 13
Conclusion
Observation 1: For mobility optimization, if the Model Inference function can be deployed on the UE side:
More detailed local information from UE can be utilized as the input to improve prediction accuracy without privacy concerns.
Local model inference can reduce inference latency and therefore interruption.
Observation 2: With RSRP prediction, the unintended events rate during HO and CHO can be significantly reduced, including HOF rate, ping-pong HO rate and short time of stay rate.
Observation 3: With SINR prediction, the average SINR during the HO can be increased 2~6dB and 5% SINR can be increased 4~8dB, which will reduce the HOF rate, reduce ping-pong rate in short TTT and improve UE throughput during HO.
Proposal 1: An Rel-19 RAN2-led study item is agreed to study the performance benefit and specification impacts of AI based mobility enhancements.