## Slide 1
3GPP TSG RAN Meeting #99 RP-230380
Rotterdam, Netherlands, March 20-23, 2023
Motivations on further sidelink enhancement in Rel-19
Source: vivo
Document for: Discussion
Agenda Item: 9.13

## Slide 2
SL underlay
SL RedCap
Agenda

## Slide 3
Motivations
Sidelink Underlay
In addition to traditional Uu communication, there is increasing demand for short range device to device (D2D) communication (e.g. P1-G1) due to XR services
NR sidelink technologies are designed for D2D but
  Sidelink over dedicated ITS spectrum: Only available for V2X use cases.
  Sidelink over licensed spectrum (Uu): The current design (and RAN4 spec) assumes that sidelink (if deployed) uses orthogonal resource than Uu, leading to capacity degradation to Uu and/or complicated NW scheduler.
  Sidelink over unlicensed spectrum: Not reliable and need to employ complex channel access mechanism, with little/limited involvement of operators.
Candidate Uu
resource
Sidelink resource pool
Observation: It is desirable to enable operators to deploy high quality commercial D2D business on existing licensed spectrum without degradation to existing Uu cellular service.

## Slide 4
Key idea for potential enhancement
Sidelink Underlay
Sidelink Underlay Transmission over licensed spectrum uses wide bandwidth and a stringent PSD restriction, to exploit higher spatial multiplexing gain from existing cellular spectrum.
  Power domain: Sidelink underlay transmission follows a UWB-like PSD restriction (e.g. <-40dBm/MHz)
  Frequency domain: Sidelink underlay transmission spans a wideband (e.g. 100MHz) that is fully shared with cellular transmission (Uu)
  Time domain: Sidelink underlay transmission is limited to in certain slots (e.g. UL slots)
frequency
Uu
Uu
SL
SL
frequency
Uu
Uu
SL
Typical Sidelink
Sidelink Underlay
Tx Power
Tx Power
Uu
Proposal: Study the feasibility and benefit, and specify necessary specification changes to support Sidelink underlay transmission over licensed spectrum
Licensed carrier (e.g. 100MHz)

## Slide 5
Benefits
Sidelink Underlay
Sidelink underlay transmission over licensed spectrum can have the following benefits
  Benefit 1: Increase the applicable spectrum to address the increasing demand of commercial D2D communication
    Reason: No need to reserve an orthogonal resource or coordinate resource allocation from Uu interface for sidelink underlay communication
  Benefit 2: Provides better QoS than unlicensed spectrum
    Reason: No need to perform channel access due to competing spectrum with other systems
  Benefit 3: Increase the spectrum efficiency (more spatial reuse of the spectrum) by serving D2D communication with no impact to cellular communications
    Reason: No reduction of Uu capacity due to very low power sidelink underlay transmission while additional D2D capacity is introduced
  Benefit 4: Enables better involvement of operators into the commercial D2D business
    Reason: Operators can step into the business by providing higher quality/less interfering spectrum (than unlicensed band), as well as radio link/network management/administration.

## Slide 6
Feasibility study (sidelink->cellular interference)
Sidelink Underlay
Interference from sidelink D2D to cellular Uu
  Baseline: Dense Urban with cellular Uu users only (10 Uu UEs/cell, 100MHz carrier)
  Sidelink Underlay: Dense Urban with both cellular Uu users and sidelink D2D pairs (10 Uu UEs/cell, 5 D2D pairs/cell with full buffer traffic, 100MHz carrier)
  System level evaluation (assumption in Appendix) is performed to compare UPT performance of the above two scenarios
Observation: When UL resource is used for SL underlay transmission, the impact to Uu UL from sidelink D2D can be ignored (UPT loss <=0.5%) if sidelink transmission PSD<=-40dBm/MHz
Chart: Uplink UPT loss in Dense Urban Scenario
| Baseline | PSD=-20 | PSD=-40 | PSD=-60
Mean UPT | 419.951 | 400.3977 | 417.846 | 419.2269
UPT loss | 0.046559 | 0.0050101 | 0.0017219
Curve for PSD=-40/-60 dBm/MHz almost coincides with baseline

## Slide 7
Feasibility study (cellular->sidelink interference)
Sidelink Underlay
Interference from cellular Uu to sidelink D2D
  Figure a: Interference CDF to SL in dense urban from Uu interface
  Figure b: SL Link level performance with interference according to Fig. (a) with different traffic load (RU)
  Table c: Equivalent sidelink (communication range 5m) SNR is ~8.5dB when PSD is -40dBm/MHz
Observation: Sidelink underlay transmission with PSD=-40dBm/MHz can work (low MCS) even when the Uu UL traffic load is high, and higher MCS (e.g. 16QAM) can be possible when the Uu UL traffic load is low.
(b)
(a)
Frequency (GHz) | 4
SCS (KHz) | 30
PRB number | 273
Bandwidth (MHz) | 98.28
PSD (dBm/MHz) | -40
Total Tx Power (dBm) | -20.07534852
Tx power Per PRB (dBm) | -44.43697499
Noise power Per PRB (dBm) | -109.437
Range (m) | 5
Channel model | InH - Office LOS
Pathloss | 56.5333809
Rx power Per PRB | -100.9703559
Equivalent SNR | 8.466644106
(c)

## Slide 8
SL underlay
SL RedCap
Agenda

## Slide 9
Personal local IoT Networks
SL RedCap
Home automation
Wearable devices
Great demand in the industry on the non-cellular wireless commercial IoT use cases
  Including such as the personal IoT device (earbuds, sensor, etc.), wireless docking, wireless streaming, etc.
Personal local IoT networks
  Becoming complex network topology while self organizing/management/maintenance is desirable
    Typically installed/maintained by a consumer, not a telecom or wireless specialist/professional
  Demanding high traffic volume, e.g., Hi-Res Audio/Music, Wireless Display, gaming, etc.
  While devices are severely sensitive to the weight and size of the devices, and most highly battery constrained.
    Usually constrained by the physical dimension limitations, such as sensor, earbuds, etc.
Observation: NR sidelink has very high potentials to enable 3GPP system in this market, E.g., highly controllable and manageable with operators involved.

## Slide 10
NR sidelink has very high potentials to enable 3GPP system in the personal IoT market
  E.g., highly controllable/manageable with operators involved
However, the power consumption and device complexity level are not good enough for many commercial personal devices (HMD, watch, earbud, etc.).
Motivation
SL RedCap
Proposal: Supporting SL RedCap in Rel-19
  Enabling PA-less sidelink device (next page)
  Enabling very low power (VLP) operations (such as SL underlay, VLP channel access, etc.)
  Introducing SL WUS signal and operations

## Slide 11
UE power class
  Power class 3 (23dBm), Power class 2(26dBm) supported for general use cases of Uu (as well as for sidelink)
  LTE eMTC and NB-IOT supports power class 5 (20dBm) and power class 6 (14dBm) (Not supported for sidelink)
PA-less sidelink devices
SL RedCap
GaAs based external PA is required to support 23dBm
  The PAE (PA efficiency) is very low (less than 5%) at low power level, e.g. 0~10dBm
    Typically for personal IoT or XR/gaming where the traffic is predominately within the localized area
  GaAs based PA also increases the device cost
    10-12% overall relative cost saving
  Consuming internal device space
    Especially for some personal IoT device such as glasses frames, earbuds, blood pressure monitor, etc
Figure 1. Power efficiency (marked red when less than 5%), N78 and N41
Two PA implementation choices: 1) Constant 4.2V P_DC; 2) APT (adaptive power tracking)

## Slide 13
Appendix
SLS evaluation assumption for sidelink underlay
Parameters | Value
Scenario | Dense Urban single layer
Layout | hexagonal grid, 7 macro sites, 3 sectors per site with wrap around
Inter-BS distance | 200m
Minimum BS-UE (2D) distance | 35m
Minimum UE-UE (2D) distance | 2m
Carrier frequency | 4GHz
Simulation bandwidth | 100MHz (273RB for 30kHz SCS)
Subcarrier spacing | 30kHz
TDD | All UL slot
BS Tx power | 49dBm
UE Tx power | 23dBm, P0 = -80, Alpha = 0.8
UE distribution | 80% indoor 3km/h and 20% outdoor 30km/h
BS receiver noise figure | 5dB
UE receiver noise figure | 9dB
UE number | 10 uu users/cell, 5 D2D pairs/cell
BS antenna height | 25m
UE antenna height | hUT = 3(nf1-1) +1.5, nf1 for outdoor UEs: 1, nf1 for indoor UEs: nf1~uniform (1, Nf1) where Nf1 = 1
BS antenna configurations | (M,N,P,Mg,Ng;Mp,Np)= (8,8,2,1,1;2,8), (dH, dV) =(0.5, 0.8)λ
Uu UE antenna configurations | (M,N,P,Mg,Ng;Mp,Np)= (1,2,2,1,1; 1,2)
SL UE antenna configurations | (M,N,P,Mg,Ng;Mp,Np)= (1,1,1,1,1; 1,1)
receiver | MMSE-IRC as the baseline receiver
Traffic model for Uu UL | 0.5Mbytes/packet, 18 packet/s
Traffic model for sidelink | Full buffer