## Slide 1: Rel-19: Motivation for studying enhancements to URLLC for industrial factory applications
3GPP TSG RAN#99 RP-230459
Rotterdam-Netherlands, March 20 –23, 2023
Agenda Item: 15
Source: Lenovo
Document for: Discussion

## Slide 2: NR Sidelink Evolution
NR SL Rel-16
NR SL Rel-17
V2X Relay (L2 & L3)
V2X Remote UE to NW Relay
Discovery mechanism
Mode 2: Inter-UE coordination schemes
Mode 2: Partial Sensing for VRU
DRX
NR SL Evo Rel-18
SL FR2: Beam-management
SL unlicensed for handset
SL positioning for V2X/IIoT/handset
V2X UE to UE Relay
Multi-hop Relay
V2X
Public safety (PS) possible
V2X,VRU
Power saving in VRU and handset
Extend support to handset such as XR
5G V2X Architecture
KPI: 3ms@99.99%
FR1
OFDM
SCS: 15kHz, 30kHz and 60kHz SCS
Mode 1 + Mode 2
UniCast/GroupCast/ Broadcast
HARQ & CSI reporting
NR SL Evo Rel-19
SL IIoT/URLLC
SL FR2 WI

## Slide 3: Motivation for using sidelink in industrial communications (1/2)
To date – focus on study and definition of sidelink/D2D communication(QoS) for V2X (3ms latency and 99.99% Reliability)
No work to date on use of sidelink and additional QoS requirements and how to meet them for deterministic communication beyond V2X
Industry 4.0 deployment mainly focuses on using licensed spectrum using FR1
  Limited spectrum availability in FR1 to serve multiple use case underscores importance of spectral efficiency
5G-ACIA investigating sidelink deployment for industrial factory and the white paper is expected H2-2023
Utilizing gNB based communication implies potential extra hops in various scenarios
  For example, PLC connected to UE controlling various Sensors/Actuators (S/As)
  Data exchange between collaborating mobile robots
  Using sidelink can eliminate this extra hop and resulting spectral inefficiency.
5G core
UE-1
UPF
gNB
UE-2
(Controller)
S/A
NR-Uu
NR-Uu
NR-PC5
DS-TT
DS-TT
Figure: Showing the extra hop via gNB compared to Sidelink

## Slide 4: Motivation for using sidelink in industrial communications (1/2)
Using Sidelink rotating part of the robot is connected to controller as shown in the right figure
Inter- S/A data transfer could be Sidelink based for latency reduction
Sidelink is complementary to the gNB deployment in the factory
  For In-coverage, Sidelink offers a resource efficient deployment & latency reduction for a smaller service area and limited number of UEs
  For out of coverage, sidelink as a relay offers coverage enhancement
Controller
S/A
UE-2
DS--TT
gNB
S/A
S/A
UE-1
(GW)
DS--TT
NR-Uu
NR-Uu
SL
Figure: Showing field devices exchanging data directly without routing via controller
UE-2
DS-TT
S/A
UE-1
(Controller)
DS-TT
Figure: wired replacement in a rotating part of the robot

## Slide 5: Sidelink URLLC/IIoT (1)
Use Case 1:
Closed loop motion control
  High reliability low-latency communication: 1ms, 2ms@99.9999%
  Time sensitive communication (TSN)
Motion controller in a production line
  Motion controller connected to gNB
  Motion controller connected to a UE
Field device (sensor/actuator) connected to PLC (controller)
  Deployment 1: Each field device(S/A) in an industrial network may require wireless connectivity to a controller as illustrated in the right figure (e.g., UE-2)
  Deployment 2: Field devices (S/A) connected to a wireless gateway using wired interface and gateway UE wirelessly connected to a controller as illustrated in the right figure (e.g., UE-1)
Table: Requirements of motion control use case requiring 99.999 to 99.999 99 for a service area of 50 m x 10 m x 10 m
Message size [byte] | Transfer interval [ms] | No. of UEs | Survival time [ms]
50 | 0.5 | ≤ 20 | 0.5
40 | 1 | ≤ 50 | 1
20 | 2 | ≤ 100 | 2
Controller
S/A
UE-2
DS--TT
gNB
S/A
S/A
UE-1
(GW)
DS--TT
NR-Uu
NR-Uu
Controller
S/A
UE-2
DS--TT
UE
S/A
S/A
UE-1
(GW)
DS--TT
SL
SL
Figure: Controller connected to a UE
and illustrating sidelink deployments
Figure: Showing field devices exchanging data directly without routing via controller

## Slide 6: Sidelink URLLC/IIoT (2)
Use Case 2:
Cooperative carrying robots/AGVs supporting Sidelink device-to-device communication requires
  Exchange of control commands and control feedback done using periodic deterministic communication and time-sensitive networking
  High reliability low-latency communication:99.9999%@2.5ms
  Time sensitive communication (TSN) @1µs clock synchronicity
Use Case 3:
Controller to controller wireless communication;
  Several controller communicate in large printing machine
  Individual machine handling common task involves coordinated handover of work pieces
Sidelink device-to-device communication for C2C requires
  High reliability low-latency: 1 k @99.9999% and 10ms & 50ms latency
  Time sensitive communication (TSN) @1µs clock synchronicity
  Stationary UEs
Figure: Mobile robots / AGVs carrying a large work piece cooperatively from 3GPP TS 22.104
Message size [byte] | Transfer interval [ms] | Latency [ms] | No. of UEs | Survival time [ms]
250; 500 with localisation information | > 5 ms > 2.5 ms > 1.7 ms | < 0.5 x transfer interval | 2 to 8 | 0 transfer interval 2 x transfer interval
Table: Requirements of cooperative carrying robot use case requiring 99.9999 to 99.999 999 availability for a service area of 10 m x 10 m x 5 m from 3GPP TS 22.104
Message size [byte] | Transfer interval [ms] | Latency [ms] | No. of UEs | Survival time [ms]
1k | ≤ 10 ms | < transfer interval | 5 to 10 | 10ms
1k | ≤ 50 ms | < transfer interval | 5 to 10 | 50ms
Figure: controller to controller use case from 3GPP TS 22.104
Table: Requirements from controller to controller use case from 3GPP TS 22.104

## Slide 7: Proposed Areas of Study for Sidelink Enhancements
URLLC/IIoT:
  Feasibility study for supporting URLLC communication for various industrial factory applications using sidelink taking into account Rel17 URLLC-IIoT as baseline [RAN1/RAN2] targeting:
    Improvements to physical layer reliability and latency of sidelink control/data channel communications
    In-coverage, partial coverage and out-of-coverage scenarios for FR1
  Study on the need and implementation of sidelink based time sensitive communication [RAN1/RAN2]
    Potential impact on 3GPP architecture in collaborations with SA WG2