## Slide 1
RP-230569
3GPP TSG RAN Meeting #99
Rotterdam, Netherlands, March 20-23, 2023
Source: Huawei, HiSilicon
Title: On support of UL/SUL indicator as Type 2 field
Document for: Discussion and decision
Agenda Item: 9.3.1.2

## Slide 2
In RAN1#111 meeting, it was agreed to support UL/SUL indicator for DCI format 0_X, with FFS on which type it belongs to.
The relevant definition of the field types based on RAN1 agreements are provided here for information
  Type-1 field:
    Type-1A field: A single field indicating common information to all the co-scheduled cells
    Type-1C field: A single field indicating an information to only one of co-scheduled cells
  Type-2 field: Separate field for each of the co-scheduled cells
  Type-3 field: Common or separate to each of the co-scheduled cells, or separate to each sub-group, depending on configuration
In RAN1#112 meeting, the following was proposed (Chair’s note RAN1#112 v20) as a potential way forward
  UL/SUL indicator in DCI format 0_X belongs to Type-2
    Note: It is RAN1 understanding that above does not revert the RAN#96 agreement on scenarios for UL TX switching (captured in RP-221880)
    Note: It is RAN1 understanding that above does not revert the RAN#98 agreement on NR CA band combinations with two SUL cells (captured in RP-223553)
Companies have different interpretations on Note 2 in RP-223553, thus did not reach conclusions on the UL/SUL indicator for DCI format 0_X
Observation: A resolution is needed for completion of the inclusion of UL/SUL indicator field in DCI format 0_X.
Background

## Slide 3
  UL/SUL indicator field in DCI format 0_X belongs to Type-2
  For single DCI, whether a configured cell is scheduled or not is indicated dynamically and independently by the new DCI format 0_X. The same criteria shall be applied to the uplink carriers for the serving cells with SUL.
  Type 2 for UL/SUL indicator suits the above very well, since type 2 enables separate indication of cells with SUL
    Type 1A restricts that the SULs of the co-scheduled cells always have to function simultaneously, despite that there could be difference in terms of channel quality and load for different carriers
    Type 1C restricts that only one SUL can be configured/indicated at a time, eliminating the PDCCH capacity improvement benefits by joint scheduling multi-carriers with the single DCI
  Whether/how to clarify Note 2 in RP-223553 is an independent discussion, which shall not prevent the completion of UL/SUL indicator in DCI format 0_X.
  RAN1 and RAN2 specifications shall be generic to the band combinations defined in RAN4, in order to be forward compatible
    This is quite normal, or even desirable from specification work perspective. Example: RAN4 so far has not defined CA with up to 16 CCs, which is allowed by RAN1 and RAN2 specifications since Rel-15.
  Support of type 2 field for UL/SUL indicator does not revert any agreement from previous RAN plenary meetings, e.g. agreements on UL TX switching (RP-221880) or band combinations with two SULs (RP-223553)
On field type for UL/SUL indicator
Proposal: RAN to conclude that UL/SUL indicator in DCI format 0_X belongs to Type-2.

## Slide 4
  Note 2 in RP-223553, i.e. New WID: NR CA band combinations with two SUL cells in Rel-18, is copied below:
  NOTE 2: No simultaneous uplink configuration on the two SUL bands according to Table 1.
  Note 2 in RP-223553 does not prevent a UE to be configured via RRC with two service cells, each with SUL
  During the GTW session when RP-223553 was approved, it was clarified that Note 2 in RP-223553 is not related to serving cell RRC configuration for a UE; rather the “UL configuration” in Note 2 refers to the those already captured in Table 1 of RP-223553
  The second column in Table 1 in RP-223553 is for RAN4 to define the corresponding RF requirements
  Take the first row, as copied below, in Table 1 in RP-223553 as an example, RAN4 will define the RF requirements for SUL_n41A-n95A, SUL_n79A-n98A and CA_n41A-n79A. For example,
    For a UE reporting the support of all the three cases (i.e. , SUL_n41A-n95A, SUL_n79A-n98A and CA_n41A-n79A), it is able to meet the RF requirements for switched UL transmission between n41 and n95, switched UL transmission between n79 and n98, and simultaneous UL transmission on n41 and n79. For such kind of UE, from serving cell RRC configuration perspective, it is able to support the configuration of cell 1: n41 (NUL) + n95 (SUL) and cell 2: n79 (NUL) + n98 (SUL).
  Huawei’s understanding on the WI in RP-223553 is to support two serving cells, each with SUL, for a UE. During the discussion and approval process, it is a compromise not to support simultaneous uplink transmission of n41+n98, n79+n95, and n95+n98, which are reflected in Table 1 of RP-223553 and no corresponding RF requirements are to be specified in this WI.
On Note 2 in RP-223553
NR CA configuration | Uplink CA configuration or SUL configuration | Power Class
CA_SUL_n41A-n95A_SUL_n79A-n98A | SUL_n41A-n95A SUL_n79A-n98A CA_n41A-n79A | PC3, PC2
Conclusion: Note 2 in RP-223553 does not prevent a UE to be configured via RRC with two serving cells, each with SUL. Simultaneous uplink transmissions and corresponding RF requirements are to be specified according to Table 1 of RP-223553.

## Slide 6
    Table 1 mentioned in Note 2 in RP-223553 is as below:
Appendix
NR CA configuration | Uplink CA configuration or SUL configuration | Power Class | contact name, company | Contact email | other supporting companies (min. 3) | status (new, ongoing, completed, stopped)
CA_SUL_n41A-n95A_SUL_n79A-n98A | SUL_n41A-n95A SUL_n79A-n98A CA_n41A-n79A | PC3, PC2 | Xiaoran ZHANG, CMCC | zhangxiaoran@chinamobile.com | CBN, Huawei, HiSilicon | New
CA_SUL_n41A-n98A_SUL_n79A-n95A | SUL_n41A-n98A SUL_n79A-n95A CA_n41A-n79A | PC3, PC2 | Xiaoran ZHANG, CMCC | zhangxiaoran@chinamobile.com | CBN, Huawei, HiSilicon | New
CA_SUL_n41A-n83A_SUL_n79A-n98A | SUL_n41A-n83A SUL_n79A-n98A CA_n41A-n79A | PC3 applicable for n83 of SUL_n41A-n83A; PC3 and PC2 for other uplink configurations | Xiaoran ZHANG, CMCC | zhangxiaoran@chinamobile.com | CBN, Huawei, HiSilicon | New
CA_SUL_n41A-n83A_SUL_n79A-n95A | SUL_n41A-n83A SUL_n79A-n95A CA_n41A-n79A | PC3 applicable for n83 of SUL_n41A-n83A; PC3 and PC2 for other uplink configurations | Xiaoran ZHANG, CMCC | zhangxiaoran@chinamobile.com | CBN, Huawei, HiSilicon | New
CA_SUL_n78A-n81A_SUL_n78A-n84A | SUL_n78A-n81A SUL_n78A-n84A CA_n78C | PC3 applicable for n81 of SUL_n78A-n81A and n84 of SUL_n78A-n84A; PC3 and PC2 for other uplink configurations | Lei GAO, China Telecom | gaol8@chinatelecom.cn | China Unicom, Huawei, HiSilicon | New
CA_SUL_n78A-n80A_SUL_n78A-n84A | SUL_n78A-n80A SUL_n78A-n84A CA_n78C | PC3 applicable for n80 of SUL_n78A-n80A and n84 of SUL_n78A-n84A; PC3 and PC2 for other uplink configurations | Lei GAO, China Telecom | gaol8@chinatelecom.cn | China Unicom, Huawei, HiSilicon | New