## Slide 1: Offline discussion summary on RAN1-MultiCarrier
NTT DOCOMO, INC.
3GPP TSG RAN #99
Rotterdam, Netherlands, March 20th - 23rd, 2023
Agenda Item: 9.3.1.2
Document for: Decision
RP-230749

## Slide 2: Background
Reference
  RP-230144 About Multi-cell Scheduling by Single DCI in Rel-18 MC-Enh OPPO
  RP-230292 Discussion on UL/SUL indicator in multi-cell PUSCH/PDSCH scheduling CMCC
  RP-230356 Status report for WI: Multi-carrier enhancements for NR NTT DOCOMO, INC.
  RP-230569 On support of UL/SUL indicator as Type 2 field Huawei, HiSilicon
  RP-230606 On support of more than one cell with a SUL carrier Nokia, Nokia Shanghai Bell, Ericsson, Qualcomm
Issues to be discussed
  Issue 1: RAN4 TU request (0356)
  Issue 2: Clarification on RAN4 remaining issues (0356(Flagged))
  Issue 3: Possible revision of RAN1 agreement regarding co-scheduled cell indication (0144)
  Issue 4: Possible clarification on support of multiple sets of cells (0144)
  Issue 5: Clarification on Note 2 in RP-223553 (0292, 0569, 0606)
  Issue 6: Type of UL/SUL indicator field in DCI format 0_X (0292, 0569, 0606)

## Slide 3: Issue 1: RAN4 TU request (0356)
In RP-230356,
  RAN4 plan was to complete their work for this WI at RAN#99. However, although many agreements and progress were made at RAN4#106 meetings, there are number of remaining RAN4 discussion points to complete this WI in RAN4, where some discussion points are depending on other WGs’ conclusion. Therefore, it is requested in this status report to have an additional RAN4 TU for RAN4#106-e-bis and RAN4#107 meeting (0.5 TU for RF and RD for each meeting (0.5 x 2 x 2=2.0TU)).
  The following agreement is captured in RAN4#106 chairman’s note
  Agreement:
  RAN4 proposes to extend the work item for Multi-carrier enhancements for NR
There has been no objection/concern/flag on the request of additional RAN4 TU for RAN4#106bis-e and RAN4#107 meetings
  RAN4 chair kindly confirmed that the request is ok and is already taken in account for RAN4 SR
Proposal 1 from moderator:
  additional 2 TUs are allocated to Rel-18 MC enh WI for RAN4 in Q2 2023 (0.5 TU for RF and 0.5 TU for RD in each of RAN4#106bis-e and RAN4#107 meetings) by using RAN4 reserved TUs.

## Slide 4: Issue 2: Clarification on RAN4 remaining issues (0356(Flagged))
In RP-230356,
There is a flag from Qualcomm as below
  The SR captures several open issues for RAN4, it is not clear whether the bullet related to dual UL (3rd bullet) refers to simultaneous switching or not. This is an open issue, there is a LS to RAN1 with questions related to this in R4-2303507.
Clarification from moderator:
  The wording “Time mask for dualUL related switching scenarios” comes from RAN4 WF in R4-2303693 (Issue 1-4-3) as well as other bullets. So, the 3rd bullet is related to simultaneous switching and corresponding LS to RAN1
2.4.2 Remaining Open issues
Some potential issues related to RAN4 from WID on Multi-carrier enhancements for NR as below
-Specify RF core requirements on UL Tx switching schemes across up to 3 or 4 bands including the following remaining issues.
Fallback of Rel-18 Tx switching to Rel-16/17 Tx switching
2-layer UL-MIMO support for carrier(s) capable of 2Tx
Time mask for dualUL related switching scenarios
Location of switching period in relation to time T0
Additional RF specification impact for Tx switching with dual TAGs
-Specify RRM test cases related to core requirements on UL Tx switching schemes across up to 3 or 4 bands

## Slide 5: Issue 3: Possible revision of RAN1 agreement regarding co-scheduled cell indication (0144)
In RP-230144,
The RAN1 agreement on co-scheduled cell indication was made based on extensive discussion in RAN1#112 meeting and compromise among companies to complete RAN1 work.
  Companies understood the concern explained in RP-230144, but the RAN1 agreement was made as above.
  Agreed mechanisms work, i.e., there is no critical issue identified so far.
Suggestion from moderator:
  We should not repeat the discussion, and should not revert RAN1 agreement unless critical issue is identified
Proposal 1: RANP is to revise the concerned RAN1 agreement into one of following formulations.
Opt-1: keep “if”-procedure and drop “otherwise”-procedure.
Opt-2: keep “otherwise”-procedure and drop “if”-procedure.
Opt-3: Combine the co-scheduled cell identification in “if”-procedure and the payload size determination in “otherwise”-procedure.

## Slide 6: Issue 4: Possible clarification on support of multiple sets of cells (0144)
In RP-230144,
RAN1 has not discussed above proposal.
RAN1 can discuss such clarification in maintenance phase if necessary.
  In RAN1 status report (RP-230003),
Suggestion from moderator:
  Such clarification as Proposal 2 in RP-230144 is left to RAN1 in maintenance phase if necessary
Proposal 2: RANP concludes the following is NOT supported in Rel-18 MC-Enh.
From UE perspective, one cell is configured as a scheduled cell in one co-scheduled cell set and meanwhile is configured as the scheduling cell for a different co-scheduled cell set.
To meet the functional freeze target date of 2023.Q3 for Rel-18, RAN1 will
  Start review of draft CRs after RAN1#112bis-e (April) starting with select WIs (eDSS, NCR, MC-Enh)

## Slide 7: Issue 5: Clarification on Note 2 in RP-223553 (0292, 0569, 0606)
In RP-223553,
In RP-230292 and RP-230569,
  That is the “No simultaneous uplink configuration on the two SUL bands” only means one UE cannot simultaneously transmit UL on two aggregated SUL bands from RAN4’s perspective. However, the two SUL carriers can be configured simultaneously to one UE’s two serving cells by RRC signaling, respectively.
  For a UE reporting the support of all the three cases (i.e. , SUL_n41A-n95A, SUL_n79A-n98A and CA_n41A-n79A), it is able to meet the RF requirements for switched UL transmission between n41 and n95, switched UL transmission between n79 and n98, and simultaneous UL transmission on n41 and n79. For such kind of UE, from serving cell RRC configuration perspective, it is able to support the configuration of cell 1: n41 (NUL) + n95 (SUL) and cell 2: n79 (NUL) + n98 (SUL).
NR CA configuration | Uplink CA configuration or SUL configuration | Power Class | contact name, company | Contact email | other supporting companies (min. 3) | status (new, ongoing, completed, stopped)
CA_SUL_n41A-n95A_SUL_n79A-n98A | SUL_n41A-n95A SUL_n79A-n98A CA_n41A-n79A | PC3, PC2 | Xiaoran ZHANG, CMCC | zhangxiaoran@chinamobile.com | CBN, Huawei, HiSilicon | New
… | … |  |  |  |  | 
The NR inter-band CA band combination configurations with two SUL cells are defined in Table 1 below:
NOTE 1: the fall back combinations/configurations should be finalized no later than the proposed NR CA configurations.
NOTE 2: No simultaneous uplink configuration on the two SUL bands according to Table 1.
Table 1: NR Inter-band CA with two SUL cells

## Slide 8: Issue 5: Clarification on Note 2 in RP-223553 (0292, 0569, 0606)
In RP-223553,
In RP-230606,
  In each row of Table 1 that defines ‘NR CA configuration’, the UE’s uplink can be configured with one, and only one of the entries in the second column ‘Uplink CA configuration or SUL configuration’. Combining any two or more entries is not a valid configuration.
Moderator’s observations:
  Regarding whether “combining any two or more entries in ‘Uplink CA configuration or SUL configuration’ column is valid configuration or not”, companies have different views.
  Companies would have same understanding that simultaneous transmission on SUL+SUL, SUL+NUL are not to be specified according to RP-223553
NR CA configuration | Uplink CA configuration or SUL configuration | Power Class | contact name, company | Contact email | other supporting companies (min. 3) | status (new, ongoing, completed, stopped)
CA_SUL_n41A-n95A_SUL_n79A-n98A | SUL_n41A-n95A SUL_n79A-n98A CA_n41A-n79A | PC3, PC2 | Xiaoran ZHANG, CMCC | zhangxiaoran@chinamobile.com | CBN, Huawei, HiSilicon | New
… | … |  |  |  |  | 
The NR inter-band CA band combination configurations with two SUL cells are defined in Table 1 below:
NOTE 1: the fall back combinations/configurations should be finalized no later than the proposed NR CA configurations.
NOTE 2: No simultaneous uplink configuration on the two SUL bands according to Table 1.
Table 1: NR Inter-band CA with two SUL cells

## Slide 9: Issue 5: Clarification on Note 2 in RP-223553 (0292, 0569, 0606)
If we check other WID having such table,
  E.g., RP-222834 Revised WID: Rel-18 NR Inter-band Carrier Aggregation/Dual Connectivity for 3 bands DL with x bands UL (x=1,2)
  For inter-band UL CA, only one of the entries in the second column is to be configured for UL at a time
    Simultaneous configuration of two or more entries in the second column seems not valid (e.g., even if a UE supports band A+B, A+C and B+C for UL, the UE cannot be configured with A+B+C for UL unless the UE supports A+B+C for UL while the UE can be configured with A+B+C for DL as the UE supports it)
  For UL Tx switching, two or more entries in the second column may be configured simultaneously
    E.g., if a UE supports DL CA for A+B+C and Rel-18 UL Tx switching across A, B and C, even if the UE does not support A+B+C for UL CA, the UE can be configured with A+B+C for DL/UL
Moderator’s observation:
  Regarding whether “combining any two or more entries in ‘Uplink CA configuration or SUL configuration’ column is valid configuration or not”, it should be discussed with considering UL CA and UL switching scenarios
Band combination configuration | UpLink configuration
CA_n3A-n8A-n41A | CA_n3A-n8A CA_n3A-n41A CA_n8A-n41A
NR CA configuration | Uplink CA configuration or single uplink carrier6 | NR Band | Channel bandwidth (MHz) (NOTE 3) | Bandwidth combination set
CA_n3A-n8A-n41A | CA_n3A-n8A CA_n3A-n41A CA_n8A-n41A | n3 | 5, 10, 15, 20, 25, 30 | 0
 |  | n8 | 5, 10, 15, 20 | 
 |  | n41 | 10, 15, 20, 30, 40, 50, 60, 80, 90, 100 | 
Table 5.5A.3.2-1: NR CA configurations and bandwidth combinations sets defined for inter-band CA (three bands)

## Slide 10: Issue 6: Type of UL/SUL indicator field in DCI format 0_X (0292, 0569, 0606)
In RP-230292 and RP-230569,
  Considering operators have the spectrum demands of two SUL cells CA band combinations, the UL/SUL indicator in DCI format 0_X can be specified as Type 2 field with separate indication for each co-scheduled cell for more scheduling flexibility. In addition, in current RAN4 CA band combinations, the maximum number of SUL cells can be aggregated is two, thus the two UL/SUL indicator bits have negligible DCI payload impact on DCI format 0_X.
  Whether/how to clarify Note 2 in RP-223553 is an independent discussion, which shall not prevent the completion of UL/SUL indicator in DCI format 0_X. RAN1 and RAN2 specifications shall be generic to the band combinations defined in RAN4, in order to be forward compatible.
  Proposal: UL/SUL indicator in DCI format 0_X belongs to Type-2.
In RP-230606,
  there is no support for band combinations allowing for a configuration with more than one cell with uplink when a SUL carrier is part of the UL band combination. From this perspective defining the SUL field of the multi-cell scheduling DCI format 0_X that supports multiple cells with a SUL carrier is of no use, when no such configuration is a) possible and b) not motivated by the SUL feature to begin with.
  Proposal: Adopt either Alternative #1 or Alternative #3 of the RAN#98 moderator’s proposal
    Alt.1: UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is 1 bit (when it is present), which is for one serving cell within the set of co-scheduled cells (i.e., Type 1C).
    Alt.3: UL/SUL indicator field is excluded from a DCI format 0_X

## Slide 11: Issue 6: Type of UL/SUL indicator field in DCI format 0_X (0292, 0569, 0606)
Moderator’s observations:
  Proposals in {0292, 0569} and 0606 are different because of different views on Issue 5, i.e., whether a UE can be configured with more than one UL cell with SUL or not.
  Possible proposals based on 0292, 0569 and 0606 are basically same as in RAN#98-e as below
    Alt.1: UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is 1 bit (when it is present), which is for one serving cell within the set of co-scheduled cells (i.e., Type 1C).
    Alt.2: UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is sum of {0, 1} bits for each cell in the set configured for the DCI format 0_X (i.e., Type 2)
      The number of bit (i.e., 0 or 1) for a cell in the set is determined according to the existing mechanism defined in TS 38.212 for UL/SUL indicator field.
    [Alt.3: UL/SUL indicator field is excluded from a DCI format 0_X. (only if RAN cannot converge on either Alt.1 or Alt.2)]
    [Alt.4: UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is 1 bit (when it is present), which is commonly applied for all serving cell(s) with SUL within the set of co-scheduled cells (i.e., Type 1A).]

## Slide 12: Issue 5&6 (0292, 0569, 0606)
Moderator’s observation:
  Based on offline discussion with companies, there are multiple companies who strongly believe the Note 2 in RP-223553 is quite clear that “No simultaneous uplink configuration on the two SUL bands” is allowed by RP-223553 as it clearly describes so
    But for Issue 6, they can accept following proposal (i.e., Type-2) discussed at the RAN1#112 meeting
    In addition, it is more constructive to discuss potential update for RP-223553 (RP-230719) separately
Moderator’s suggestion:
  Agree on above proposal (with potential wording update) to conclude Issue 5&6
  Discuss potential update for RP-223553 (RP-230719) separately
UL/SUL indicator in DCI format 0_X belongs to Type-3 field, i.e., configurable between Type-1A and Type-2.
Simultaneous configuration of two cells with SUL is not allowed as foreseen by RP-223553
Simultaneous transmission on SUL carrier and on another uplink is not allowed
Note: It is RAN1 understanding that above does not revert the RAN#96 agreement on scenarios for UL TX switching (captured in RP-221880).
Note: It is RAN1 understanding that above does not revert the RAN#98 agreement on NR CA band combinations with two SUL cells (captured in RP-223553).

## Slide 13: Final Proposals (1/2)
RP-230356 (WI status report) can be noted with capturing below in the meeting minutes
  additional 2 TUs are allocated to Rel-18 MC enh WI for RAN4 in Q2 2023 (0.5 TU for RF and 0.5 TU for RD in each of RAN4#106bis-e and RAN4#107 meetings) by using RAN4 reserved TUs
  The wording “Time mask for dualUL related switching scenarios” comes from RAN4 WF in R4-2303693 (Issue 1-4-3) as well as other bullets. So, the 3rd bullet is related to simultaneous switching and corresponding LS to RAN1
  Clarification as Proposal 2 in RP-230144 is left to RAN1 in maintenance phase if necessary

## Slide 14: Final Proposals (2/2)
UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is sum of {0, 1} bits for each cell in the set configured for the DCI format 0_X (i.e., Type 2)
  The number of bit (i.e., 0 or 1) for a cell in the set is determined according to the existing mechanism defined in TS 38.212 for UL/SUL indicator field in DCI format 0_1.
  Note 1: Simultaneous configuration of two cells with SUL is not allowed by current description in RP-223553 (RP-230719)
  Note 2: Simultaneous transmission on SUL carrier and on another uplink is not allowed by current description in RP-223553 (RP-230719)
  Note 3: This does not revert the RAN#96 agreement on scenarios for UL TX switching (captured in RP-221880)
  Note 4: When simultaneous configuration of two cells with SUL becomes supported by specification, this UL/SUL indicator design for DCI format 0_X should not prevent potential further RAN1/2 impact to support the scenario
Task RAN4 to discuss whether/how to define band combinations for Rel-18 UL Tx switching with 3 or 4 bands
Discuss potential update for the WI RP-223553 (RP-230719) or potential another WID for simultaneous configuration of two cells with SUL separately
  Task RAN4 to assess the additional, if any, RAN4 specification impact and UE implementation impact for a UE configured with two serving cells, each with SUL, whether back-to-back transmissions on two SUL carriers could be supported without any switching period, or whether the UE can only support such configuration in the UL Tx switching framework with UE capability based switching period
    Example band combinations are referred to RP-223553 (RP-230719)
    Further check the status in RAN#100

## Slide 15: Another version (2/2)
UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is sum of {0, 1} bits for each cell in the set configured for the DCI format 0_X (i.e., Type 2)
  The number of bit (i.e., 0 or 1) for a cell in the set is determined according to the existing mechanism defined in TS 38.212 for UL/SUL indicator field in DCI format 0_1.
  Note 1: Simultaneous configuration of two cells with SUL is not allowed by current description of Note 2 in RP-223553 (RP-230719)
  Note 2: Simultaneous transmission on SUL carrier and on another uplink is not allowed by current description in RP-223553 (RP-230719)
  Note 3: This does not revert the RAN#96 agreement on scenarios for UL TX switching (captured in RP-221880)
  Note 4: This UL/SUL indicator design for DCI format 0_X should not prevent potential further RAN1/2 impact to support the simultaneous configuration of two cells with SUL
Task RAN4 to discuss whether/how to define band combinations for Rel-18 UL Tx switching with 3 or 4 bands
Discuss potential update for the WI RP-223553 (RP-230719) or potential another WID for simultaneous configuration of two cells with SUL separately
  Task RAN4 to assess the additional, if any, RAN4 specification impact and UE implementation impact for a UE configured with two serving cells, each with SUL, whether back-to-back transmissions on two SUL carriers could be supported without any switching period, or whether the UE can only support such configuration in the UL Tx switching framework with UE capability based switching period
    Example band combinations are referred to RP-223553 (RP-230719)
    Further check the status in RAN#100