## Slide 1: Way forward on R18 SL-Evo WI objectives
Moderator (OPPO)
3GPP TSG RAN Meeting #99
Rotterdam, Netherlands, March 20 – 23, 2023
Agenda: 9.3.1.5
Document for: Endorsement
RP-230769

## Slide 2: Scope for SL CA objective
List of restrictions in order to minimize WG efforts to support a basic version of SL CA in Rel-18.
Only Mode 2 operation
Intra-band CA only in FR1 ITS band (i.e., Band n47)
Same subcarrier spacing (SCS) among CA carriers to avoid resource selection enhancements and AGC issues
  Time resources for PSFCH are aligned among the carriers for CA
No enhancement related to SCI transmissions on PSCCH/PSSCH, PSFCH transmission, RSRP feedback, CSI feedback and congestion control compared to Rel-16 (i.e., per-carrier operation)
  SL resource indication remains to be per-resource pool and per-carrier basis (no cross-carrier scheduling in SCI)
  UE transmits SL HARQ feedback on the same carrier on which it receives the associated PSSCH
No consideration for limited transmission and reception capability
No primary/secondary carrier differentiation
Reuse the LTE sidelink CA design for the following aspects:
  Sidelink carrier (re-)selection, synchronization of aggregated carriers, Tx power split for simultaneous sidelink transmissions, packet duplication
The CA band combination work in RAN4 is limited to intra-band contiguous CA in Rel-18.
Note: The SL CA work in Rel-18 mainly targets some V2X use cases

## Slide 3: Guidance for Co-Ex objective
Solution guidance in order to minimize WG efforts to support 15/30kHz SCSs for NR SL with dynamic pool sharing in Rel-18.
RAN1 is tasked to support only 15 and 30 kHz SCSs for dynamic resource pool sharing. Existing RAN1 agreements for dynamic resource pool sharing apply to support of 30 kHz.
  For NR PSCCH/PSSCH transmissions in 30kHz SCS, NR SL UE selects in MAC layer at least the first of NR SL slots overlapping with an LTE SL subframe, and can select the subsequent overlapping NR SL slot in MAC layer
    No change to the R16/17 resource allocation procedure in PHY due to this restriction
    The existing SL slot structure from Rel-16 is unchanged
    The starting symbol of the first of the overlapping NR SL slots is assumed to be aligned with the first symbol of the LTE SL subframe
  For NR SL with 15/30kHz SCSs, NR SL UE avoids selecting resources for PSCCH/PSSCH transmissions where the corresponding PSFCH transmission occasions overlap with LTE SL reservations in time domain
    Note, this is inline with Option 1-2 in the working assumption made in RAN1#112. No other options from the working assumption need to be considered.
  Mode 2 operation only

## Slide 4: Proposals
Proposal 1: To endorse the additional objective scope and guidance in slide 2 and 3, and update WID objective 1, 4 and 5, accordingly.
Proposal 2:
WGs are tasked to complete Co-Ex objective (#4) by June 2023.
SL CA objective (#1) starts in RAN1 from RAN#100 or earlier if the work for Co-Ex completes before June 2023.
SL CA objective (#1) starts in RAN2/4 from RAN#99.
The work on Co-Ex and SL CA in RAN1 are not prioritized over SL-U and FR2 beam management