## Slide 1: ViewS on rel-18
3GPP RAN Plenary Release 18 Workshop, June 28th – July 2nd 2021, eMeeting
Evolution towards 5G-Advanced
Rel-18
RWS-210318

## Slide 2: Fraunhofer‘s View on Release 18 Topics
RWS-210318
4.2 Non-eMBB
4.3 Cross eMBB/non-eMBB
NTN Enhancements
  RWS-210321
Positioning
  RWS-210322
Support of Sidelink Positioning
  RWS-210323
RedCap / IoT / NR-U
  RWS-210324
Sidelink Enhancements
  RWS-210325
4.1 eMBB
MIMO Enhancements
  RWS-210319
Mobile IAB
  RWS-210320
Full Duplex Radio
  RWS-210326

## Slide 3: 4.1 MIMO Enhancements for Release 18 (1) CSI enhancements for UE mobility scenarios
Motivation
  Current type-II CSI feedback schemes lack performance in scenarios where UEs move [~30% performance loss at 30 km/h]
Scope: CSI feedback compression based on delay-Doppler spectrum-related information:
    to take channel aging at gNB side into account
    to improve performance and for massive feedback overhead reduction
Sensor Sharing
Frequency (MHz)
Delay (μs)
Delay (us)
Doppler (Hz)
Time (ms)
Time (ms)
Doppler-delay spectrum
Time-delay spectrum (R16)
Time-Frequency spectrum (R15)
Sensor Sharing
time
Performance
CSI update interval (stationarity time)
CSI (ideal)
CSI (without Doppler information)
CSI (with Doppler information)
CSI Burst
=> Details in RWS-210319

## Slide 4: 4.1 MIMO Enhancements for Release 18 (2) CSI enhancements for UE mobility scenarios
=> Details in RWS-210319
see details in video: RWS-210319.mp4

## Slide 5: 4.1 MIMO Enhancements for Release 18 (3) CSI enhancements for UE mobility scenarios
CSI feedback compression based on delay-Doppler spectrum-related information
Improved performance
Massive feedback overhead reduction
=> Details in RWS-210319

## Slide 6: 4.1 mIAB – A new IAB Use Case (1) Motivation
Improving coverage (& capacity) for UEs in cars, trains and busses
  Overcoming vehicular enclosure signal attenuation, particularly in FR2
Augmenting capacity & coverage through creation of additional (portable) hot-spots/backhaul links
  Bringing coverage into out-of-coverage/poor coverage areas
Boosting mIAB deployments by supporting a combination of access links in unlicensed & backhaul links in licensed spectrum
BH link
Access
mIAB
Fixed IAB
=> Details in RWS-210320

## Slide 7: 4.1 mIAB Scope: Connectivity & service continuity (2)
Proposed objectives for Rel-18 (1/2)
Addressing challenges in mobility procedures associated with moving nodes/networks
  Study required enhancements to HO/DC mechanisms for mIABs and UEs
  Study group-mobility management procedures for improved signalling efficiency & reduced latency
Fixed IAB node
IAB Donor 1
Provide flexible mechanisms for a frequent (ex)change of Master/Secondary nodes
Fixed IAB node
mIAB HO
UEs HO
Address signalling overhead & latency
IAB Donor 2
IAB Donor 3
IAB Donor 1
IAB Donor 2
SN
MN
MN
SN
MN
MN
=> Details in RWS-210320

## Slide 8: 4.1 mIAB Scope: Shared infrastructure & in-vehicle NR-U; Minimising interference (3)
Proposed objectives for Rel-18 (2/2)
Enable variety of implementation options for shared infrastructure
  Enhancements to enable NR-U on the access (DU) with single/multiple backhaul connections (MT)
  Study mechanisms for connectivity/service continuity when moving from a shared to a non-shared network
Addressing a more complex interference environment due to dynamic network topology
  Specify further enhancements to radio resource coordination & CLI framework
Shared IAB node
DU (e.g. NR-U)
MT
Shared IAB Donor
CN (PLMN1)
CN (PLMN2)
IAB Donor (PLMN1)
Shared IAB node
MT
DU (e.g. NR-U)
IAB Donor (PLMN2)
MT
=> Details in RWS-210320

## Slide 9: 4.2 NR-NTN Enhancements Scope
Vehicular Platooning
Sensor Sharing
Flexible advanced system and satellite architectures
  Regenerative payload, gNB(s) on board of a satellite, CU/DU split
  Inter-Satellite Links & Satellite routing, interconnectivity between GEO, LEO, HAPS
  NTN indirect access: Enable access by terrestrial UEs via SL to NTN-enabled UEs
Waveform improvements: Smaller bandwidths and energy efficient waveforms
  DFT-s-OFDM in DL in Rel-18;
  Improved waveforms potentially a topic for beyond 5G/6G
Supporting Low-cost Terminals
  UEs without GNSS capability
  Leveraging RedCap features and coverage enhancements for NTN
Network based UE localization for improved reliability and flexibility
Flexible spectrum access and interoperability
=> Details in RWS-210321

## Slide 10: 4.2 Low Power and Low Complexity Positioning (1) Motivation
Enable positioning for use cases with low complexity and low power industry devices.
Support network low complex solutions and positioning methods
Low Power Applications
Smart Factory
Mission Critical Applications
=> Details in RWS-210322

## Slide 11: 4.2 Low Power and Low Complexity Positioning (2) Objectives
Support positioning for low-power devices with advanced positioning capabilities
Support positioning for RedCap devices
Study techniques and methods to reduce network complexity
=> Details in RWS-210322

## Slide 12: 4.2 Positioning Enhancements Motivation and Scope
Motivation
  Address solutions to enhance the positioning accuracy and reliability in challenging environments
Objectives
  Beam management enhancement for positioning in FR2
  Improvements for high accuracy continuous tracking
    Enable seamless positioning for mobility scenarios between positioning methods based on integrity and quality
    Increase efficiency of parallel tracking of many devices
    Phase measurements for positioning
Impact of beam selection on the positioning accuracy:
CDF for 81 beam pair error on 8 positions (P1…P8) using
real-World FR2 evalaution on Rel-16 positioning signals.
=> Details in RWS-210322

## Slide 13: 4.2 Sidelink Positioning Motivation and Scope
Motivation
  Precise positioning required by advanced use cases for V2X, Public Safety, e.g. to ensure safety of VRUs
Vehicular Platooning
Sensor Sharing
Scope
  New positioning techniques to enable 1D range measurements and enhance the UL, DL and UL+DL positioning accuracy
  Support sidelink positioning for all coverage scenarios and architectures (UE-based, UE-assisted), also combined with RAT-dependent and RAT-independent positioning methods
  Support vehicular Distributed Antenna Systems (DAS)
=> Details in RWS-210323

## Slide 14: 4.2 RedCap, PowSav, NB-IoT and IIoT
Target NR low complexity devices
Enhancements for Power Saving
Enhancements for NB-IoT
Enhancements for Industrial-IoT
Motivation
  Target use cases below the current RedCap WI
  Further cost and capability reductions are required to cover the whole spectrum
Scope and Objective
  Small bandwidth support for RedCap devices (<=5MHz, NPN support)
  NR-U Enhancements for RedCap devices (WI PowSav, WI RedCap)
Motivation
  Expanding use cases and further reduced power consumption
  Energy harvesting devices for longer lifetime
Scope and Objective
  Power Saving in Connected Mode (measurements, PDCCH monitoring, mobility)
Motivation
  Energy efficient data transmission for low-priority, latency tolerant devices
  Enhancements for deep coverage
Scope and Objective
  CB-PUR – Contention-based Preconfigured Uplink Resources
  Coverage extension via relaying (dedicated or dual-use UE) for NB-IoT
  Support small data transmission in preconfigured, shared uplink resources (NB-IOT)
Motivation
  Enable small scale industrial deployments in unlicensed spectrum
  Support for XR cloud services
Scope and Objective
  Enhanced URLLC support for IIoT/factory automation in unlicensed bands
  LBT enhancements, e.g. beam based access and directional LBT
  Enhancements for AR/VR applications
    High throughput
    Low latency HARQ improvements
=> Details in RWS-210324

## Slide 15: 4.2 Enhanced Sidelink Features for Rel-18
Active UEs
Inactive UEs
UE-Managed Centralized Sub-networks
Location-based Features for SL UEs
Predictive QoS and Service Continuity
Vehicular Relays for Inside and Outside UEs
Motivation
  UE-managed networks reduce the load on the gNB to provide resource grants to each UE, while the gNB still retains control over sidelink configurations
  Power saving gains when member UEs rely on the manager UE (GL UE) to provide resources
  Applicable for vehicular and commercial use cases
Scope and Objective
  Introduce hierarchical UEs that are capable of providing resource configurations to a group of UEs
    These UEs will also manage the resource allocation for member UE transmissions
Motivation
  IIoT and commercial UEs need to actively transmit and receive only in pre-defined locations
  Functionality of different UEs based on their geo-location can vary, e.g., machines/robots within an industrial plant would function differently from vehicles operating outside
Scope and Objective
  Introduce location-based configurations, such as resource pools, for UEs that are active only in specific pre-defined locations
  Restrict UEs from active transmission and reception for enhanced power saving
  Advanced SL DRX with location-based WUS/GTS
Motivation
  Allows seamless service deployments across cellular grids in exceptional scenarios, such as cell-edge or in high-interference zones
  Allow robust implementation of safety-related applications
Scope and Objective
  Enhance UE reporting functionality to maintain or upgrade QoS
  Introduce pre-reservation of resources along routes by enabling predictive handover
  Layered QoS flows with instantaneous service updates, especially to overcome temporary service degradations
Motivation
  Mobile relays can be deployed in highly congested areas conveniently
  Caters to passengers inside the vehicle, like in public transport systems such as buses, as well as to pedestrians in the vicinity
Scope and Objective
  Facilitate the relaying of configurations and scheduling grants from the gNB to UEs via vehicular relays
  Support UE-to-UE relaying via sidelink to enhance coverage, power saving and QoS
  Study the possibility of using mIAB or relays connected to a gNB via Uu as well as to UEs via SL
=> Details in RWS-210325

## Slide 16: 4.3 Full Duplex Radio Motivation, Objective, Scope
Motivation
  Increase spectral efficiency, RTT latency reduction, more flexible band allocations, improved relaying and device-to-device communication, more flexibility in spectral-temporal scheduling
Objectives
  Definition of Self-and Cross-Link-Interference-Requirements
    Support of legacy devices
    Flexible sub-band allocation
Scope
  Study and categorize relevant Use Cases and Application Scenarios
  Enhanced throughput, reliability, sensing and positioning by supporting FDR
  Enhanced interference management in FDR scenarios e.g. by enhanced CLI reporting functionality
Sensor Sharing
=> Details in RWS-210326