## Slide 1: Enhanced Sidelink Features for Rel-18
3GPP TSG RAN Rel-18 workshop RWS-210325
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: Overview of Applicability for Enhanced Sidelink Features
Advanced Vehicular Communications
Industrial IoT
Commercial Communications
Real-time high volume sensor data sharing to support HD and XR functionality
In-vehicle connectivity for passengers
Seamless end-to-end QoS adaptability across cells to ensure safety applications
In-plant coordination between workers and machines
Coherent switching between public and non-public networks,
RSU interconnectivity for advanced cross-functional deployments
Communication between network-connected smart home appliances
Interoperability between smart devices for healthcare applications

## Slide 3: Enhanced Sidelink Features
UE-Managed Centralized Sub-networks
Motivation
  UE-managed networks reduce the load on the gNB to provide resource grants to each UE, while the gNB still retains control over sidelink configurations
  Higher resource efficiency with lesser collisions for UEs operating in Mode 2
  Power saving gains when member UEs rely on the manager UE (GL UE) to provide resources
  Applicable for vehicular and commercial use cases
Scope and Objective
  Introduce hierarchical UEs that are capable of providing resource configurations to a group of UEs
    These UEs will also manage the resource allocation for member UE transmissions
Vehicular Use Case
Commercial Use Case

## Slide 4: Enhanced Sidelink Features
Location-based Features for SL UEs
Motivation
  IIoT and commercial UEs need to actively transmit and receive only in specific locations that can be pre-defined
  Functionality of different UEs based on their geo-location can vary, e.g., machines/robots within an industrial plant would function differently from vehicles operating outside
Scope and Objective
  Introduce location-based configurations, such as resource pools, for UEs that are active only in specific pre-defined locations
  Restrict UEs from active transmission and reception for enhanced power saving
  Support advanced SL DRX with location-based WUS/GTS
Active UEs
Inactive UEs

## Slide 5: Enhanced Sidelink Features
Vehicular Relays for Inside and Outside UEs
Motivation
  Mobile relays can be deployed in highly congested areas conveniently
  Caters to passengers inside the vehicle, like in public transport systems such as buses, as well as to pedestrians in the vicinity
Scope and Objective
  Facilitate the relaying of configurations and scheduling grants from the gNB to UEs via vehicular relays
  Support UE-to-UE relaying via SL to enhance coverage, power saving and QoS
  Study the possibility of using mIAB or relay nodes connected to the gNB over Uu as well as UEs via SL

## Slide 6: Enhanced Sidelink Features
Predictive QoS and Service Continuity
Motivation
  Allows seamless service deployments across cellular grids in exceptional scenarios, such as at cell-edge or in high-interference zones
  Allow robust implementation of safety-related applications
Scope and Objective
  Enhance UE reporting functionality to maintain or upgrade QoS
  Introduce pre-reservation of resources along routes by enabling predictive handover
  Layered QoS flows with instantaneous service updates, especially to overcome temporary service degradations
Continuous safety flow
Enhancement services
Radio channel statistic
[SINR]
QoS Degradation
Time
Quality
QoS Recovery
QoS
Requirement

## Slide 7: Enhanced Sidelink Features
Other Topics of Interest
Slot aggregation
  Enable transmissions of larger packets which are ideal for raw sensor data and commercial applications
Shared resource pools between UEs
  In order to increase resource efficiency, resource pools can be shared between LTE and NR V2X, as well as between UEs in different operational modes
  Advantageous due to efficient reuse of common subchannels across UEs from different releases
Carrier aggregation
  Facilitate the use of fragmented V2X spectrum for high throughput applications, e.g., HD and XR content delivery
  Enhance positioning accuracy by supporting multiple carriers

## Slide 8: Enhanced Sidelink Features
Summary of Objectives for Rel-18 SID/WID
Specify resource allocation mechanisms in Mode 1 and Mode 2 for hierarchical UEs [RAN1, RAN2]
  NR sidelink configurations by the gNB to the GL UE to facilitate scheduling capability
  Scheduling of resources for member UEs by the GL UE
Define mechanisms for location-based UE configurations that are active only in specific pre-defined locations [RAN1, RAN2]
  Introduce restrictions for UEs from active transmission and reception based on their locations
  Introduce advanced sidelink DRX with location-based WUS/GTS for enhanced power saving
Facilitate relaying configurations and scheduling grants from the gNB to UEs via vehicular relays [RAN2]
  Study the feasibility of mIAB or relay nodes connected to the gNB over Uu as well as UEs via PC5
  UE-to-UE relaying via sidelink to enhance coverage, power saving and QoS
Support enhanced UE reporting functionality to maintain or upgrade QoS [RAN2]
  Introduce pre-reservation of resources along routes by enabling predictive handover
  Study layered QoS flows with instantaneous service updates, especially to overcome temporary service degradations
Specify mechanism for slot aggregation for large packet transmissions [RAN1]
Support configuration of shared resource pools for increased resource efficiency [RAN1, RAN2, RAN4]
  Resource pools can be shared across LTE and NR V2X, as well as operational modes
Support sidelink carrier aggregation for high throughput applications and enhanced positioning accuracy [RAN1, RAN2]