## Slide 1: AI/ML for NG-RAN
Taipei, June 15-16, 2023
Agenda Item: 5
Source: Nokia, Nokia Shanghai Bell
RWS-230023 3GPP TSG RAN Rel-19 workshop

## Slide 2
AI/ML for NG-RAN
Motivation
Rel-18 focused on the basic framework for introducing AI/ML in NG-RAN
  Energy Saving, Load Balancing and Mobility Optimization use cases were prioritized
  The Rel-18 use cases can be further enhanced in Rel-19
In Rel-18, AI/ML Training and AI/ML Inference in the RAN are performed at the gNB-CU
  This is feasible for cell-based decisions (e.g., cell switch on/off) but may be impractical for certain use cases
  AI/ML Air Interface is currently studying use cases with focus on gNB-DU operations, e.g., CSI compression and beam management
  Energy Saving operations under gNB-DU control have also been introduced in RAN1-led work on Network Energy Saving (e.g., beam switch-off/switch on)
  AI/ML Training and AI/ML Inference at the gNB-DU can be considered in Rel-19

## Slide 3
AI/ML for NG-RAN
Enhancement of UE Trajectory Prediction to support additional use cases
UE trajectory prediction was introduced in Rel-18 for the Mobility Optimization use case
  It is a cell-level prediction sent during handover, which is limited to cells of the target gNB
UE trajectory prediction can be further enhanced in Rel-19 to benefit additional use cases
    Multi-hop UE trajectory prediction is useful to predict incoming load for predicting Energy Saving (e.g., determine best switch-off time at a capacity cell)
    Beam-level prediction enables beam-based decisions, e.g., beam switch-on/off
Time T-T’
Capacity cell 2
Current Trajectory
(time T)
Predicted trajectory
Capacity cell 1
Time T+T’’

## Slide 4
AI/ML for NG-RAN
Enhancements of Network Energy Saving
Rel-18 Network Energy Saving topics can be extended to consider AI/ML functionality
Such extensions could consider
  Beam-based AI/ML actions instead of cell-based e.g., predict when to switch-on/switch-off a beam as opposed to a cell
  Predictions of preferred cell DTX/DRX patterns at a node and corresponding sleep opportunities
Cell DTX cycle
Cell DTX
on-duration
Cell DTX
off-duration
Time
Cell DTX/DRX pattern configuration
Cell DTX/DRX cycle: periodicity with which cell DTX/DRX periods repeat
Cell DTX/DRX on-duration period: duration of active time
Cell DTX/DRX offset: point in time, where a DTX/DRX pattern starts
Cell DTX
offset
pattern x
Cell DTX
on-duration
Cell DTX
off-duration

## Slide 5
AI/ML for NG-RAN
CU/DU split architecture considerations
CU/DU split architecture has not been considered in Rel-18
AI/ML in the gNB-DU may be more efficient for scenarios where data is available at the gNB-DU and/or when actions are at the gNB-DU
  Example: gNB-DU has greater awareness of energy consumption
CU
DU
AI/ML
DU
DU
AI/ML
AI/ML
CU
DU
DU
DU
AI/ML

## Slide 6
AI/ML for NG-RAN
Summary of Potential Objectives
Potential objectives of a Rel-19 work item:
  Enabling multi-hop trajectory prediction of finer granularity, e.g., beam-based multi-hop trajectories
  AI/ML Energy Saving for actions pertaining to the gNB-DU, e.g., predictions of preferred DTX/DRX patterns and their corresponding sleep opportunities, beam switch-on/switch-off
  Considerations of CU/DU split architecture
Any new use cases would need a study first