## Slide 1: Emerging mission-critical use cases for 5G Sidelink, technology gaps and proposed enhancements
3GPP TSG RAN Rel-19 Workshop
June 15-June 16, 2023
RWS-230030
Agenda Item: 5
National Spectrum Consortium, Johns Hopkins University Applied Physics Laboratory

## Slide 2: Motivation
Sidelink for mission-critical use cases:
  Unstructured mobility, ultra-low latency, local traffic off-load, out of range of a base station.
Current use cases: public safety, emergency assistance and vehicle to everything (V2X) communications.
Other emerging mission-critical use cases.
Goal: Identify other emerging use cases, technology gaps with the existing Sidelink architecture and discuss required enhancements to support these use-cases for Sidelink.

## Slide 3: Emerging Use Cases of Sidelink Communications
Public Safety
V2X
Biometrics
Telehealth
Drone Swarms
IoT integration with NTN
Smart City Safety Sensor Network
Human-Machine Integration
Wireless AR/VR Headset Network
Subterranean Communications
Disaster Relief Operations
Factory automation

## Slide 4: Technology Gaps
Supporting only one-hop UE-to-UE and UE-to-Network relay as part of the existing standards.
Additional Sidelink use cases require multi-hop networking relaying to support low-latency, resilient and infrastructure-less operation with coverage extension.
Multi-hop relaying would require new solutions for network control, end-to-end quality of service (QoS) management, service continuity, resource allocation, and UE/relay discovery.
New decentralized networking algorithms are required to achieve specific performance goals related to each mission-critical use case.
Other technology gaps identified include UE authentication, novel medium access control (MAC) schemes, multi access edge computing (MEC) requirements and methods to reduce energy consumption at the UE.

## Slide 5: Proposed Enhancements
Release 18 enhancing UE-to-network relay support
  Adding support for UE-to-UE relay, and studying multi-path support where a UE is connected to a gNB using one direct path and one indirect path via a Sidelink relay.
Release 18 initially included multi-hop extension as a follow-up work item but this functionality is currently out of scope for Release 18.
Release 19 should consider supporting multi-hop relay capability for diverse coverage scenarios (in-coverage, partial coverage, out-of-coverage) for enterprise, public and ad-hoc operations for Sidelink.
  Persistent communications in multi-domain operations without relying on fixed infrastructure.
  Resilient relaying to allow continuous operation for disrupted networks (interference, PNT, etc.).