## Slide 1: Proposal on AI/ML for NR air interface in Rel-19

## Slide 2: Overall Motivation
Rel-18 AI/ML SI studies general framework and 6 sub-use cases including
  CSI feedback enhancement
    CSI compression based on two-sided model
    CSI predication based on UE-sided model
  Beam management
    Spatial domain beam prediction based on one-sided model
    Temporal domain beam prediction based on one-sided model
  Positioning accuracy enhancement
    Direct positioning based on one-sided model
    AI/ML assisted positioning based on one-sided model
Each sub-use case evaluates performance benefit and assesses potential specification impact during the study item.
In general, AI/ML model based operation provides potential gain compared to existing scheme in terms of performance and/or overhead.

## Slide 3: Consideration Point
Possible incompleteness of Rel-18 study
  According to [1], the overall progress of this SI was 30%, and although there has been some progress in RAN1#112b-e and RAN1#113, it is doubtful that the study can be completed.
  Some challenging parts are
    Model transfer
    Dataset delivery
    Model identification over-the-air
Way forward
  In order to facilitate AI/ML applications in air-interface, it will be beneficial to start work item with focused scope in Rel-19
  The work scope should be selected based on the following aspects
    Completeness level of study
    Easier adaptation to vendors (e.g. keeping vendor-specific proprietary information)
    Expected performance gain
    Expected amount of specification impact

## Slide 4: Enhanced UE capability framework
Motivation
  In Rel-18 AI/ML SI, AI/ML framework is discussed for functionality/model-based LCM(life-cycle management)
  A key enhancement to facilitate AI/ML operation for UE-side model is to introduce enhanced UE capability framework
    In current specification, UE should report its capability based on “worst case” assumption to support a feature in any case.
    When UE uses AI/ML algorithm for a feature, the feature may not be supported in some condition, e.g. due to site/scenario-specific model, model deactivation/update, etc.
      Based on current UE capability framework, UE may have to report “not” support the feature due to the worst case assumption.
Scope
  Specify enhanced UE capability framework to facilitate UE-side AI/ML operation (e.g. dynamic update of applicable UE functionality)

## Slide 5: CSI feedback enhancement
Motivation
  For CSI compression based on two-sided model,
    at least three different types of offline training collaboration types were identified, but it is still under discussion in RAN1 on their pros/cons in terms of flexibility, extendibility, performance and privacy/proprietary, etc.
    Till the RAN1#113 meeting, compared to the benchmark, it is observed that AI/ML based CSI compression provides not very promising performance gain.
      -4~17% gain and -4~30% gain for mean UPT gain and 5% UPT gain, respectively, under FTP traffic model [2].
  For CSI prediction based on UE-sided model,
    Discussions on potential specification impact has not been started yet in RAN1.
    Rel-18 MIMO CSI enhancement should be take in to account for performance comparison.
Scope
  Study and, if needed, specify CSI prediction (1st priority) or CSI compression with limited training collaboration type(s) (2nd priority) including at least following aspects.
    Data collection – No CSI-RS enhancement is assumed
    Inference
    LCM-related aspect
Figure 1. Illustration of CSI compression

## Slide 6: Beam management
Motivation
  For temporal/spatial domain prediction based on one-sided model, followings are studied
    Alt.1: DL Tx beam prediction
    Alt.2: DL Rx beam prediction (deprioritized)
    Alt.3: DL Tx-Rx Beam pair prediction
  Compared to DL Tx beam prediction, DL Tx-Rx beam pair prediction has a lot of practical challenges such as representing UE beams in standard form, revealing vendor-specific proprietary information, restricting UE implementation-specific beam optimization.
    Note that till RAN1#113 clear performance benefit from DL Tx-Rx beam pair prediction over DL Tx beam prediction is not observed.
Scope
  Specify spatial/temporal DL Tx beam prediction based on one-sided AI/ML model including at least following aspects.
    Data collection – No SSB/CSI-RS enhancement is assumed
    Inference
    LCM-related aspect
Figure 2. Illustration of beam prediction

## Slide 7: Positioning accuracy enhancement
Motivation
  During the study item, following AI/ML based positioning method were studied.
    Direct AI/ML positioning : the output of AI/ML model inference is UE location
    AI/ML assisted positioning: the output of the model inference is new measurement and/or enhancement of existing measurement
      E.g., LoS/NLoS indicator, timing information, likelihood of measurement etc.
  Till RAN1#113, it is observed both AI/ML positioning methods can provide performance gain over existing positioning methods when generalization aspects are not considered. The generalization performance for both AI/ML positioning methods need to be further justified.
  For AI/Ml assisted positioning, there are more variations according to positioning algorithms (e.g., DL/UL-TDOA, multi-RTT, etc), measurements, etc.
Scope
  Specify direct AI/ML positioning based one-sided model including at least following aspects.
    Data collection – No PRS/SRS enhancement is assumed
    Inference
    LCM-related aspect

## Slide 8: Proposals
Specify enhanced UE capability framework to facilitate UE-side AI/ML operation (e.g. dynamic update of applicable UE functionality).
Study and, if needed, specify CSI prediction (1st priority) or CSI compression with limited training collaboration type(s) (2nd priority).
Specify spatial/temporal DL Tx beam prediction based on one-sided AI/ML model.
Specify direct AI/ML positioning based one-sided model.
Above use cases should be considered following aspects
  Focus on signaling-based collaboration without model transfer (collaboration level y only).
  Focus on offline training only.
  Specification impact on
    Data collection without RS enhancement,
    Inference,
    Functionality/model based LCM operation.

## Slide 9: Reference
[1] RP-230661, “Status report for SI Study on AI/ML for NR air interface; rapporteur: Qualcomm”
[2] RAN1#113 chairman’s note