## Slide 1: Proposal on ambient IoT in Rel-19

## Slide 2: Background
Generic requirements of ambient IoT devices
  Ultra-low complexity, ultra-low power, and compact form factor
  Device types/categories/set of devices
  Device A: No energy storage, backscattering transmission
  Device B: Has limited energy storage (e.g., capacitor), backscattering transmission
  Device C: Has energy storage, independent signal generation
  Target use cases
  Inventory, sensors, positioning, and command
  Indoor and outdoor
  Competing non-3GPP IoT technologies
  RFID and barcode
  Compared to existing 3GPP IoT technologies
  (NB-IoT/LTE MTC/RedCap)
  Power and complexity orders of magnitude lower
  Device (connection) density orders of magnitude higher
  Coverage much smaller, especially for Devices A and B

## Slide 3: Motivation
Supporting ambient IoT in 3GPP is beneficial
  To accelerate automation and digitization of various industries
  To expand the 3GPP echo system and create a new market opportunity
We support to introduce RAN WG-level SI for ambient IoT in Rel-19
  To gain a deeper insight into feasibility and potential specification effort needed to support the ambient IoT in 3GPP
  To continue feasibility study in WG level on power, complexity, coverage, and so on (mainly by RAN1)
  Timely completion of Rel-19 SI/WI within the 18-month time frame is important
  * At some point of time in Rel-19, we may need to (and we are open to) discuss whether to proceed with a normative work on ambient IoT, but, for now, we think it is more realistic to pursue the study phase only in Rel-19
Proposal: Introduce RAN WG-level SI for the feasibility study of ambient IoT in Rel-19
  The study to be led by RAN1

## Slide 4: Motivation
Connectivity topologies (Rel-18 RAN study)
WG-level study to focus on topology 1 in Rel-19
  Feasibility study on topology 1 can be the basis for studying other topologies. Therefore, studying topology 1 is considered to be most important as well as urgent in Rel-19
  To extend the deployment scenarios (and hence use cases), study on topologies 2 and 3 can start in a later phase in Rel-19 or in the next release
  * For topology 1, being without the intermediate/assisting node, whether it is feasible, in terms of power, complexity, and coverage, that it can be supported by all ambient IoT devices (Device A/B/C) needs to be discussed.
SI focuses on (or prioritize) connectivity topology 1 (BS  Ambient IoT device):
  Further consideration : whether to additionally study connectivity topologies 2 and 3 in Rel-19
  Further consideration : whether to focus on Device C [and B] for topology 1, or consider all ambient IoT devices (Device A/B/C)
Topology 1:
BS  Ambient IoT device
Topology 2:
BS ↔ intermediate node ↔ Ambient IoT device
Topology 3:
BS ↔ assisting node ↔ Ambient IoT device ↔ BS
Topology 4:
UE ↔ Ambient IoT device
Topology 3 with DL assistance
Topology 3 with UL assistance

## Slide 5: Motivation
Spectrum in deployment scenarios (Rel-18 RAN study)
  Licensed FDD, licensed TDD, and unlicensed were agreed as the spectrum in deployment scenarios, with a note “Further discuss if the study should apply any limitations to the cases for which unlicensed spectrum is studied”
WG-level study to focus on licensed spectrum in Rel-19
  WG-level study in Rel-19 should focus on supporting the ambient IoT in licensed spectrum in FR1
  After feasibility study on the licensed spectrum, study on operation in unlicensed spectrum can start in later releases
  For FR2, discussion on justification in terms of applications and use cases, and the feasibility in terms of power, complexity, coverage, etc., needs to be preceded before starting the study/work in RAN WG
  * Currently, non-3GPP competing technology (e.g., RFID) is mainly operating in ISM bands. To support the ambient IoT in licensed FDD, we think there is a need to check if there is any (regional) spectrum regulation issues, especially for the devices based on backscattering communications, which is why we put “further consideration” on the licensed FDD
SI focuses on (or prioritize) the licensed spectrum in FR1:
  Licensed TDD in FR1
  Further consideration : licensed FDD

## Slide 6: Motivation
Major topics to be included in the WG-level study
  PHY layer DL/UL signal design & L1 procedures to support ambient IoT
    Study on PHY layer signal design & L1 procedures is needed to support the ambient IoT devices in NR network
  Collision/interference/load handling
    As stated in the SID, these are considered as the areas that need enhancements to support larger coverage and denser deployment of devices compared to existing non-3GPP IoT technologies
  Coexistence/harmonization with existing NR signals/channels
    Concerning the operating band of the ambient IoT in relation to NR band, WG study can be focused on in-band deployment scenario in Rel-19 and later on extended to other scenarios, i.e., guard-band and standalone band
    Coexistence/harmonization with existing NR signals/channels is an important design criterion especially for in-band
SI includes study on
  PHY layer DL/UL signal design & L1 procedures to support ambient IoT
  Collision/interference/load handling
  Coexistence/harmonization with existing NR signals/channels

## Slide 7: Proposal on ambient IoT in Rel-19
Introduce RAN WG-level SI for the feasibility study of ambient IoT in Rel-19
  The study to be led by RAN1
SI focuses on (or prioritize) connectivity topology 1 (BS  Ambient IoT device):
  Further consideration : whether to additionally study connectivity topologies 2 and 3 in Rel-19
  Further consideration : whether to focus on Device C [and B] for topology 1, or consider all ambient IoT devices (Device A/B/C)
SI focuses on (or prioritize) the licensed spectrum in FR1:
  Licensed TDD in FR1
  Further consideration : licensed FDD
SI includes study on
  PHY layer DL/UL signal design & L1 procedures to support ambient IoT
  Collision/interference/load handling
  Coexistence/harmonization with existing NR signals/channels