## Slide 1: Proposal on ML-Aided Predictive Mobility in Rel-19

## Slide 2: Justification
Higher layer application of AIML
  In Rel-18, CSI/beam prediction has been considered as one of the main use cases.
  However, higher layer application of AIML remains unexplored. In Rel-19, higher layer application of AIML capabilities should be explored with an aim to at least study or even to specify relevant functionalities.
Predictive mobility based on Predictive measurements
  In our view, mobility is the most important and suitable area to consider as higher layer application of AIML capabilities.
  Mobility is triggered based on L3 measurements. That is, predictive measurement framework is fundamental to enable predictive mobility.
    Predictive L1 measurements has been studied in Rel-18.
    Predictive L3 measurement results can be obtained by consolidating predictive L1 measurements. Predictive mobility based on predictive L3 measurements can be explored.
  In Rel-19, RAN WGs are recommended to study and specify predictive measurement framework and predictive mobility as main higher layer application of AIML
    Predictive measurement framework can be extended to consider predictive failure detection and proactive failure avoidance.

## Slide 3: Justification
Handover failure or unnecessary handover
  Handover problems such as handover failures or unnecessary handovers incur data interruption causing significant QoS degradation.
  The root cause of the handover problems is that the mobility decision is currently based on the present radio link quality. If there is a quality gap between the present and the future, the chance of the handover failure or wrong handover increases. Optimal mobility decision necessarily requires the knowledge of the future radio conditions for an appropriate time span.
Predictive Measurement and Predictive Mobility
  Time domain measurement prediction capabilities enabled by UE’s ML capabilities allows UE to predict radio quality for a source cell as well as target cells.
  Such predictive measurement capabilities can give new opportunity to avoid handover problem by performing predictive measurement reporting and/or predictive mobility execution.
  By avoiding handover problem via predictive measurement reporting and/or predictive mobility execution, quality of service can be significantly improved.
Time
RSRP
Time
RSRP
Time
RSRP
Serving Cell (1)
Neighbour Cell (2)
(a) Too Late HO
RLF
Serving Cell (1)
Neighbour Cell (2)
(b) Too Early HO
Neighbour Cell (2)
Serving Cell (1)
mobility
(Cell 1 -> Cell 2)
RLF
Neighbour Cell (3)
mobility
(Cell 1 -> Cell 2)
mobility
(Cell 2-> Cell 1)
(c) Ping-pong
Stiff
gradient

## Slide 4: Justification
Predictive Measurements
  Predictive Measurements for future time
    UE can perform measurements for serving cell and neighbour cells for future time.
    UE can derive predictive measurement results for a future time.
    UE can derive a future time at which predictive measurement results meet the report condition or execution condition for mobility.
Time
RSRP
Serving Cell (1)
Neighbour Cell (2)
Neighbour Cell (3)
Neighbour Cell (4)
Predictive measurement
Perform measurement
< Predictive Measurements for future time , and at >

## Slide 5: Justification
Predictive Mobility
  Predictive mobility decision based on predictive measurements
    Network-triggered Mobility
      UE can send measurement reports including predictive measurement results
      Network can decide a handover with an appropriate cell and an appropriate time based on predictive measurement reports.
    Conditional mobility
      UE can execute CHO to a suitable target cell among candidate target cells based on predictive measurement results of target cells
    Based on the predictive mobility, handover problems such as handover failures or unnecessary handovers can be avoided.
Time
RSRP
Time
RSRP
Time
RSRP
Serving Cell (1)
Neighbour Cell (2)
(1)Predictive measurement
(2)Mobility
Cell 1 -> Cell 2
(t1)
(t2)
(a) Avoidance of late HO
RLF
w/ Legacy mobility
Serving Cell (1)
Neighbour Cell (2)
(1)Predictive measurement
(t1)
(2)Mobility
Cell 1 -> Cell 2
(t2)
(b) Avoidance of early HO
Neighbour Cell (2)
Serving Cell (1)
Legacy mobility
(Cell 1 -> Cell 2)
RLF
w/ Legacy mobility
Neighbour Cell (3)
(1)Predictive measurement
(t1)
(2)Mobility
Cell 1 -> Cell 3
Legacy mobility
(Cell 1 -> Cell 2)
Legacy mobility
(Cell 2-> Cell 1)
(t2)
(c) Avoidance of Ping-pong

## Slide 6: Justification
Radio Link Failure and Reactive Recovery
  Currently UE declares radio link failure (RLF) if ‘consecutive’ failures are detected. Radio link monitoring is based on measurement results of RLM-RS.
  Upon detection of RLF for a cell group, the operation of the cell group is suspended, i.e., service is interrupted or degraded.
  Recovery procedure is initiated via RRC re-establishment or, in case of DC, fast recovery. Until the recovery is completed, interruption or degraded service quality persists. Depending on the recovery procedure, UE may experience severe QoS degradation.
NR RLF
RSRP in ENDC (LTE B13 + NR FR2 n261) for mobile UE

## Slide 7: Justification
Predictive RLF Detection and Proactive Recovery
  Time domain measurement prediction capabilities enabled by UE’s ML capabilities allows UE to predict the occurrence of RLF in advance. Such predictive RLF detection can give new opportunity to avoid the pending RLF by triggering e.g., proactive failure reporting of mobility, rather than waiting for the RLF to just happen.
  By avoiding RLF via predictive RLF detection and proactive actions, quality of service can be significantly improved.
Predictive Beam Failure detection and Proactive Recovery
  Beam failure detection and BFR can be enhanced to predictive BFD and proactive BFR. Predictive BFD and proactive BFR can also improve QoS by avoiding beam interruption.

## Slide 8: Justification
ML-based model management for predictive mobility
  R18 ML-based model management is specific to RAN1 use cases
  In R19, ML-based model management for predictive mobility is required
    For model management in LCM perspective (Model selection/(de)activation/switching/etc) based on predictive L3 measurement results and/or predictive mobility results
Model Training
Model Management
Model Inference
Model Storage
Predictive
Measurement Results
Trained/Updated Model
Monitoring Data
Model (de)activate, switching, etc.
Training Data.
Model Transfer/Delivery
Data Collection
Predictive Measurement Results
HO Success/Failure
Predictive Mobility
Inference Data.
General Framework for predictive mobility

## Slide 9: Proposed R19 Work Plan
Possible Work Plan for Predictive Mobility
  Alt1: SI only in Rel-19
  Alt2: Work Item with study phase
    Whether to have work item in Rel-19 is highly dependent of the progress of Rel-18 AIML study item
Proposed R19 Work Plan for Predictive Mobility
  Study phase is necessary to identify requirements and functionalities to enable predictive measurements and predictive mobility.
  3GPP can aim at specifying predictive measurement and mobility procedure in Rel-19 on top of Rel-18 study item and Rel-19 study phase, but whether WI is possible is highly dependent of Rel-18 AIML SI progress:
    R18 CSI/beam prediction
    R18 ML lifecycle management (LCM)
    R18 UE capabilities

## Slide 10: Objectives for R19
Objectives for SI scope :
  1) To study requirement and functionalities to enable predictive mobility
    To study requirements and functionalities to enable predictive measurements and measurement reporting
      L3 filtering mechanism based on beam prediction.
      Reporting condition for predictive measurements.
    To study requirements and functionalities to enable predictive mobility
      Predictive NW-triggered HO based on predictive measurement reporting is studied.
      Conditional HO based on predictive measurement evaluation is studied.
      Both UE and network side impacts need to be studied.
    To study requirements and functionalities to enable predictive link failure detection and proactive recovery
  2) To study ML-based model management mechanism for predictive mobility
    To study means for network to evaluate the accuracy of predictive measurements
    To study means for network to activate/deactivate/switch predictive mobility.

## Slide 11: Objectives for R19
Objectives for WI scope :
  1) To specify predictive measurements and measurement reporting procedure
    Configuration of predictive measurements.
    Reporting condition for predictive measurement reporting.
  2) To specify predictive mobility procedure
    Enhancements of network-triggered mobility based on predictive measurement reporting over radio interface.
    Enhancements of conditional mobility based on predictive measurements and evaluations, including execution conditions dedicated to predictive mobility.
    Enhancements of inter-node signaling for predictive mobility
  3) To specify proactive link recovery procedure
    Mechanisms to enable predictive radio link failure or beam failure
    Proactive recovery actions upon detection of predictive link/beam failure.
  4) To specify ML-based model management mechanism for predictive mobility
    To specify report mechanism with assistance information
    To specify UE/NW operation according to performance metric(s), e.g., model (de)activation, switching, etc.