## Slide 1: Proposal on XR enhancement in Rel-19

## Slide 2: Motivation for XR awareness
In XR, dependency between PDU sets is important factor for XR service. For dependency, SA2 agreed that each PDU set within a QoS flow can have different importance (priority) level.
  Even if all PDUs in the non-important PDU set are successfully received, If at least one PDU in the important PDU set is missed, all other PDUs in the non-important PDU set are meaningless since the non-important PDU set is decoded based on the important PDU set.
In Rel-18, traffic awareness enhancement is limited to discard operation based on PSI (PDU Set Importance) at network congestion. But, it does not fully satisfy requirement of PSI. Thus, scheduling enhancement for important PDU set should be considered in Rel-19.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Motivation for XR awareness
The PDCP duplication introduced in Rel-15 is used for enhancing the reliable transmission for the specific service by duplicating all PDUs within a DRB.
  The PDCP duplication in Rel-15 is inappropriate to increase reliability of XR traffic since it consumes much radio resource to duplicate all PDUs for the high throughput of XR traffic.
  Increasing reliability of important PDU set is much more important than non-important PDU set to improve user experience.
However, there is no mechanism to increase reliable transmission of the important PDU set than the non-importance PDU set.
In order to improve the user experience, it is essential to support the prioritized handling and reliable transmission of the important PDU set.
Selective PDCP duplication
Transmission via different RLC entities

## Slide 4: Motivation for XR power saving
In XR, the power saving is critical since XR services consume more UE power than other services in order to satisfy tight QoS requirements, e.g., higher throughput and low latency.
  However, Rel-18 XR power saving enhancement is limited to handle non-integer periodicity and SFN wrap around problems in DRX operation.
Rel-18 XR power saving enhancements may not be sufficient to support other important XR traffic characteristics, e.g., multiple flows and jitters, and it does not bring considerable power saving gain.
  Since only one XR flow is aligned with the DRX cycle, it may cause the transmission delay for other XR flows.
  Due to jitter, it may cause the transmission delay and unnecessary PDCCH monitoring.
Transmission delay due to one DRX configuration
Unnecessary PDCCH monitoring and Transmission delay due to jitter

## Slide 5: Motivation for XR power saving
Considering that the XR traffic requires the low latency, the delayed transmission of XR traffic would degrade the user experience.
In Rel-18 XR SI, it was already identified that main power saving gain comes from minimizing the unnecessary PDCCH monitoring as captured in TR38.838.
  However, even though this aspect is important for XR power saving, it is not fully considered in Rel-18 XR power saving enhancement.
In order to avoid the transmission delay and unnecessary PDCCH monitoring, it is essential to improve power saving gain for multiple flows and jitter.
Multiple DRX configurations
Jitter efficient DRX operation

## Slide 6: Objectives
Traffic awareness enhancement
  Reliability improvement for important PDU set, e.g. selective PDCP duplication.
  Prioritized scheduling for important PDU set, e.g. transmission via different RLC entities.
Power saving enhancement
  Support for multiple flows, e.g. multiple DRX configurations.
  Jitter efficient DRX operation, e.g. additional onDuration.