## Slide 1: Further enhanced SL relay in Rel-19

## Slide 2: Motivation for power saving and reduced UE complexity
  The UE configured with Rel-18 multi-path relaying should always maintain both direct path and indirect path regardless of which path is actually selected for user data transmission, otherwise frequent path addition, modification and/or removal are required.
    Rel-18 UE can be reconfigured with path removal and addition for releasing one path and adding one path for power saving, which requires signaling overhead and power consumption with frequency RRC reconfigurations for both relay UE and remote UE.
    Dynamic direct/indirect path activation/deactivation and possibly dynamic path selection can be helpful for power saving and better usage of multi-path operation.
  Multi-path relaying is beneifical especially when the remote UE is at cell edge. Direct uplink transmission can be restricted for the remote UE for power saving and reduced UE complexity
    This helps the remote UE save UE power and reduce UE complexity required for multi-path operation.
    Uplink L1 control channels can be kept but uplink user data can go on indirect path via the relay UE.
    RedCap UE capable of sidelink or WiFi (e.g. smart watch) can be implemented with reduced uplink capability.
  Rel-18 multi-path relaying can be further enhanced for power saving and reduced capability.

## Slide 3: Motivation for enhancing non-3GPP based UE-to-UE link
  In Rel-18 Scenario 2, UE-to-UE link is hidden in 3GPP with some restrictions:
    Bearer mapping on indirect path is restricted.
    Only ideal UE-to-UE link and one candidate relay UE are considered
  Such restrictions can be removed for inter-operability and usage extension e.g. for in-car passenger device connectivity using relay in the vehicle mounted UE; smart watch connectivity using smart phone or vehicle as relay; and better control of indirect path under gNB.
    Restriction to bearer mapping on indirect path can be removed by using an adaptation layer on non-3GPP based UE-to-UE link in Rel-19.
    More than one relay UE with or without direct path can be considered for better usage of multi-path operation e.g. mobility of remote UE between vehicle and house, mobility of smart watch between smart phone and vehicle, dynamic indirect path selection for IoT devices.
    CN impact is seldom considered in Rel-18 Scenario 2. Considering SA workload for enhanced feature, RAN can keep CN less impacted in Rel-19.
  Enhance non-3GPP based UE-to-UE link for intra-gNB case without CN impact (as specified in Rel-18)

## Slide 4: Other aspects for Rel-19 discussion
  Inter-gNB multi-path relaying
    In Rel-18, only intra-gNB multi-path relaying is supported.
  Multi-hop U2N relay
    gNB – Relay UE1 – Relay UE2 – Remote UE
    Remote UE1 – Relay UE1 – Relay UE2 – Remote UE2

## Slide 5: Objective
    Support power saving and reduced UE complexity for intra-gNB multi-path relaying [RAN2]
      Restriction to direct uplink data transmission
      Dynamic path activation/deactivation
        Support multiple indirect paths with or without direct path (e.g. smart watch via vehicle and smart phone)
        Only one active indirect among one or more configured indirect paths under a same gNB
      Based on current CN operation i.e. without CN impact
    Enhance single path or multi-path relaying with non-3GPP based UE-to-UE link for intra-gNB case without CN impact [RAN2]
      Support non-ideal UE-to-UE link and adaptation layer i.e. no Rel-18 bearer mapping restriction
      Support multiple candidate relay UEs