## Slide 1: Views on Rel-19 MIMO Enhancement
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-2300315
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Outline on Rel-19 MIMO enhancement
  Support 3Tx UL MIMO
  Further enhance multi-TA for multiple TRP transmission
  Enhance uplink multi-panel transmission
  Enhance multi-beam operation

## Slide 3: Support 3Tx UL MIMO
  Motivations
    Boosting the UL throughput is demanding for some UL-heavy services and attracting interests from many companies [RP-211652]
    Throughput of commercial handheld UEs (e.g., smartphone) is restricted by 2 Tx chains
    Thanks to the evolution of hardware, it is possible for an advanced smartphone to support 3 Tx chains in one band
    4 Tx chains is not likely in the near future due to limited form factor
Smart phone: RF chains for one band

## Slide 4: Support 3Tx UL MIMO
Benefit:
  It can provide better user experience for UL-heavy services
  Significant gain in UL throughput is observed:
    50% throughput improvement for cell-center UEs
Proposals:
  Specify signaling/mechanism to enable 3 Tx UL MIMO transmission, including
    3-port codebook
    3-port SRS resource
    Corresponding UE capability
    RAN4 requirements

## Slide 5: Further enhance multi-TA for multiple TRP transmission
Motivation:
  TA acquisition for multiple TRP transmission
    For RACH-based TA acquisition, RACH resources are reserved for UEs. That costs additional either contention-based or contention-free UL resources.
    RACH-less TA acquisition approach by measuring the difference of DL timing reference between serving cell and non-serving cell(s) may save UE efforts in UL.
    In Rel-18, LTM has confirmed the working assumption on RACH-less TA acquisition for synchronous TRPs.
  Rel-18 multi-TA for multiple TRP relies on unified TCI framework (specified in Rel-17), but does not support Rel-15/16 UL spatial relation framework
Benefits:
RACH-less TA acquisition allows UE to obtain TRP-specific TA without RACH procedure
Relaxing the dependency between multi-TA mechanism and Rel-17 unified TCI framework can enable more UEs/gNBs to support the multiple TA scenarios
Proposals:
Support RACH-less TA acquisition based on DL timing reference measurement of different TRPs.
Support multiple TAs for multiple TRPs when legacy Rel-15/16 spatial relation framework is applied

## Slide 6: Enhance uplink multi-panel transmission
Motivation:
  Multi-panel UL simultaneous transmission is specified in Rel-18. However, the design does not support asymmetric panels which in envisioned for CPE/FWA/vehicles type UEs.
  In multi-DCI based multiple TRP system, PUSCH+PUSCH is supported in Rel-18. However, the cases of PUSCH+PUCCH and PUCCH+PUCCH are not supported, which would restrict the flexibility of system operation and limit the system throughput/latency enhancement.
Benefits:
Supporting asymmetric panels can optimize the uplink transmission performance for CPE/FWA/vehicles type UEs
Allowing PUCCH+PUCCH/PUSCH+PUCCH can further improve the throughput and reduce uplink latency
Proposals:
Extend the single-DCI based multi-panel uplink transmission and multi-DCI based multi-panel uplink transmission to UEs with asymmetric panels
Specify PUCCH+PUCCH multi-panel transmission in multi-DCI based multi-TRP system
Specify PUSCH+PUCCH multi-panel transmission in multi-DCI based multi-TRP system

## Slide 7: Enhance uplink multi-panel transmission
Motivation:
  All the beam reporting and beam switch/update specified in NR up to Rel-18 are NW-initiated method
  NW-initiated beam reporting and beam switch might result in latency and signaling overhead because UE is always the first one who knows the best beam.
  LTM beam reporting involves large number of candidate cells and large number of reported beams.
  UE can be aware of the dynamic change of radio environment timely.
Benefits:
UE initiated beam reporting reduces the signaling overhead for beam reporting.
UE initiated beam switch reduces beam update/switch latency and also reduce possibility of beam link failure
Proposals:
Specify signaling/mechanism to facilitate UE-initiated beam management procedure, including,
  UE-initiated L1 beam reporting.
  UE-initiated beam switch/update