## Slide 1: Views on positioning enhancement in Rel-19
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-2300316
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Outline
  Ambient IoT positioning
  SL positioning
    SL-U positioning
    SL positioning in FR2
    SL CPP
  Further enhancement for carrier phase positioning (CPP)

## Slide 3: Ambient IoT Positioning based on phase difference
  Motivation:
    There is urgent need for in Rel-19 ambient IoT positioning based on the discussion in SA1
      Use cases agreed including manufacturing, logistics and warehousing, finding items in smart home etc.
      Positioning accuracy of 1-3 meters for the targeted use cases should be achieved by Ambient IoT devices with ultra-low complexity and power consumption
    Positioning based phase difference will be the most promising method suitable for ambient IoT device, due to its ultra-low device complexity(e.g. narrow bandwidth, poor timing stability etc.)
      Difficult to acquire accurate RSRP measurement due to low device complexity
      Measurement of TOA/TDOA is not possible due to very narrow operation bandwidth
      On the other hand, there is method to measure the phase difference of different carriers
RSRP based ambient positioning
Phase difference based ambient positioning
  Example:
  The central carrier is the incoming signal
  2 carriers on both sides are backscattered by device with frequency shifting
  Measuring phase difference derive distance in accuracy of meter level

## Slide 4: Ambient IoT Positioning (2/2)
  Potential scope:
    Study the deployment scenario(e.g. positioning by gNB or UE) for the typical ambient IoT positioning use cases
    Study the possible operation mode (e.g. to position a target ambient IoT device or to position a target UE assisted by ambient IoT devices)
    Study possible positioning methods suitable for ambient IoT, including phase difference of 2 carriers
  Please refer to our companion contribution RWS-230317 for more details.

## Slide 5: Motivation for SL-U positioning
There is a strong need to use unlicensed spectrum for SL positioning
  Use cases and corresponding requirements were studied in Rel-18, horizontal and vertical accuracy requirements of most SL positioning use cases identified by RAN1 are in meter-level, and Set B accuracy requirements of V2X and IIoT are in sub-meter level.
  RAN1 also evaluated the performance of SL positioning in Rel-18, to satisfy the requirements RAN1 recommended that SL PRS bandwidth of up to 100MHz are supported on in FR1.
  In Rel-18, only ITS and licensed spectrum in FR1 are supported for SL positioning, however, available spectrum for SL on ITS and licensed band are less than 40MHz so far.
The basis to use unlicensed spectrum for SL positioning will be ready in Rel-19
  SL positioning will be specified in Rel-18, positioning methods, SL PRS, resource allocation, signaling and procedures, etc., could mostly be reused for SL-U positioning.
  The solutions specified in SL-U could be mostly reused for SL PRS transmission on unlicensed spectrum.

## Slide 6: Evaluation results on SL-U positioning
Our evaluation show that under same bandwidth the accuracy loss in unlicensed carrier is marginal comparing to licensed carrier, SL-U positioning can achieve better performance thanks to more available spectrum in unlicensed band for SL operation

## Slide 7: SL-U positioning
  Specify channel access mechanism to support SL PRS and associated channel(s) on unlicensed spectrum
    e.g., LBT, COT sharing, SCSt, etc.
    Channel access mechanism for Rel-18 SL-U should be the baseline.
  Specify physical structure of SL PRS and associated channel(s), including the multiplexing scheme.
    Physical structure of SL PRS and associated channel(s) on ITS/licensed band are used as the baseline.
    IRB structure may not be necessary since PRS demands large bandwidth, i.e., naturally OCB/PSD requirement can be met.
  Support both shared resource pool with Rel-18 SL-U and dedicated resource pool for SL-U positioning.
    Backward compatibility with Rel-18 UE should be ensured in the shared resource pool.
  Study to simplify the signaling procedure for SL-U positioning to reduce the possibility of signaling collision .

## Slide 8: SL positioning in FR2
  Motivation:
    SL PRS transmission in FR2 is allowed but beam management for SL PRS is not supported in Rel-18.
    SL spectrum in FR1 is extremely limited, the larger bandwidth in FR2 is desirable to satisfy the accuracy requirements of the use cases.
    Enhanced SL operation on FR2 licensed spectrum being studied in Rel-18 is supposed to go into normative phase in Rel-19, beam management specified in this item can be used as baseline for beam management of SL PRS and associated channels.
  Scope:
    Study and specify beam management for SL PRS and associated SL channel(s).
    Focus on ITS and licensed spectrum only.
    The work can start after sufficient progress is achieved in enhanced SL operation on FR2 licensed spectrum.
    Strive to reuse beam management for SL communication.

## Slide 9: SL CPP
  Motivation:
    CPP (Carrier Phase Positioning) is supported in Rel-18, based on the study in Rel-18, it is feasible to use existing DL PRS and SRS signals to obtain the carrier phase measurements for achieving a horizontal accuracy of up to a few centimeters at least at 50% under certain conditions.
    CPP is helpful to SL positioning in FR1 licensed spectrum as this method does not reply on PRS bandwidth to achieve high accuracy.
  Scope:
    Specify physical layer measurements and signaling to support SL carrier phase positioning.
    Use Rel-18 CPP in Uu positioning as baseline.
    Focus on ITS and licensed spectrum on FR1.
    SL signal(s) defined in Rel-18 is used for SL carrier phase measurement.

## Slide 10: Further enhancement for carrier phase positioning (CPP)
  Motivation:
    Rel-18 introduces carrier phase positioning (CPP) based on the existing DL RPS and UL SRS
    Rel-18 CPP mechanism only supports carrier phase (CP) measurement for single carrier
    The issue of integer ambiguity of carrier phase measurement is not well resolved in Rel-18
    R18 CPP only works well for the LOS-heavy scenarios, but cannot suppress the multipath effect efficiently
  Scope:
    Support advanced CPP based on the carrier phase measurement on multiple DL/UL carriers/sub-bands
    Multi-frequency based CPP measurement is also one candidate to resolve the issue of integer ambiguity
    Enhance mechanism to facilitate CPP to mitigate multipath